## Slide 1: Lecture 1-1 Hardware/Software Interface Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module1

## Slide 2
Agenda
Machine Language Program
Instruction Set Architecture

## Slide 3: Machine Language Program
Hardware/Software Interface

## Slide 4: What is This?
000000 00000 00101 00010 00010000000
000000 00100 00010 00010 00000100000
100011 00010 01111 00000 00000000000
100011 00010 10000 00000 00000000100
101011 00010 10000 00000 00000000000
101011 00010 01111 00000 00000000100
000000 11111 00000 00000 00000001000

## Slide 5: Machine Language Program (for MIPS)
000000 00000 00101 00010 00010000000
000000 00100 00010 00010 00000100000
100011 00010 01111 00000 00000000000
100011 00010 10000 00000 00000000100
101011 00010 10000 00000 00000000000
101011 00010 01111 00000 00000000100
000000 11111 00000 00000 00000001000
Binary Digit or Bit
: One of the two
numbers in base 2
(0 or 1)
: Off / On Switch in electrical devices
Instruction
: A command that computer hardware understands & obeys

## Slide 6
000000 00000 00101 00010 00010000000
000000 00100 00010 00010 00000100000
100011 00010 01111 00000 00000000000
100011 00010 10000 00000 00000000100
101011 00010 10000 00000 00000000000
101011 00010 01111 00000 00000000100
000000 11111 00000 00000 00000001000
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Assembly Language Program (for MIPS)
Machine Language
: A binary representation of machine instructions
Assembly language
: A symbolic representation of machine instructions

## Slide 7: Assembly Language Program (for MIPS)
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Assembler
: A program translating assembly codes into machine codes
Program
: A set of instructions specifying operations/operands and sequence

## Slide 8: High-level Language Program (in C)
void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
Compiler
: A program translating high-level language codes into assembly codes
High-level Language
: A portable language consisting of words and algebraic notations (C, C++, Java) that humans understand

## Slide 9: Machine Language Program (for MIPS)
High-level language program (in C)
void swap (int v[], int k)
. . .
Assembly language program (for MIPS)
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Machine (object) code (for MIPS)
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
C - Compiler
Assembler

## Slide 10: Instruction Set Architecture
Hardware/Software Interface

## Slide 11: Instruction Set Architecture (ISA)
Syntax and semantics of a list of instructions
Interface description separating the hardware and software
Many ISAs
  X86/ia32, ia64, ARM, MIPS, PowerPC, etc.
RISC vs. CISC
  Reduced Instruction-Set Computer
  Complex Instruction-Set Computer
instruction set architecture
software
hardware

## Slide 12: Main Concepts
Instructions are also data
  Encoded in binary and stored in memory
Program Counter
  Points to the location of the instruction to be executed
Fetch instruction from
memory location pointed
to by the PC
Execute the instruction
Update the PC
CPU
Memory
Address
Data
(Instruction)
A Stored Program Computer
: Memory holds program
: CPU executes instructions sequentially at a time
: Von Neumann Architecture

## Slide 13: MIPS R4000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point: coprocessor
  Memory Management
  Special
3 Instruction Formats: all 32 bits wide
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
Registers
3 Main Instruction Types

## Slide 14: Below Your Program (Set of Instructions)
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
Applications software
Systems software
Hardware

## Slide 15: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 16: Components of a Computer
Same components for all kinds of computers
  Desktop PC
  Server
  Embedded Computers
  etc.
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler
The BIG Picture

## Slide 17
Machine Language Program, Assembly Language Program, High-level Language Program
Instruction Set Architecture = Computer Architecture
Computer = Processor (Datapath and Control) + Memory + Input/Output
Summary