## Slide 1: Lecture 1-2 Instructions (MIPS) Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture – Module1

## Slide 2
Agenda
MIPS ISA and Organization
Arithmetic & Logical Instructions
Data Transfer Instructions
Branch Instructions

## Slide 3: MIPS ISA and Organization
Instructions (MIPS)

## Slide 4: MIPS R4000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point: coprocessor
  Memory Management
  Special
3 Instruction Formats: all 32 bits wide
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
Registers

## Slide 5: MIPS Register File
Register File
  Holds thirty-two 32-bit registers
  Two read ports and
  One write port
  R0 is hardwired to 0
Registers are
  Faster than main memory
  Easier for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order
  Can hold variables so that
    code density improves (since register are named with fewer bits than a memory location)
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32

## Slide 6: MIPS Register Convention
Name | Register Number | Usage
$zero | 0 | the constant 0
$v0 - $v1 | 2-3 | returned values
$a0 - $a3 | 4-7 | arguments
$t0 - $t7 | 8-15 | temporaries
$s0 - $s7 | 16-23 | saved values
$t8 - $t9 | 24-25 | temporaries
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | return address

## Slide 7: MIPS Organization
32
32
32
R data
32
32
32
5
5
5
32
1
5
Processor
Memory
32 bits
230
words
R / W addr
W data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
Write data
32 bits
src1
data
src2
data
32 registers
32
32
ALU
0
2
3
7
6
4
byte address
(Big Endian)
Fetch
PC = PC+4
Decode
Execute

## Slide 8: MIPS ALU
32-bit ALU
  2 32-bit sources
  1 32-bit result
Operations
  Arithmetic
    ADD, SUB, ...
  Logical
    AND, OR, NOR, XOR, …
32
32
32
ALU

## Slide 9: View of the Memory
Memory is viewed as a large, single-dimension array, with an address
A memory address is an index into the array
Processor
Memory
? locations
read addr/
write addr
read data
write data
32
32
32
232
? width
Notes: For class handout

## Slide 10: Memory Organization
How wide is the memory?
What is each unit?
Each unit is a bit
  0, 1
8-bits = 1 byte
  In MIPS, memory is byte addressable
  232 locations of 1 byte
Software likes to operate on “words”
  1 word = 4 bytes = 32 bits
  230 locations of 1 word
Memory
232 Locations
8-bit
Memory
32-bit
230 Locations

## Slide 11: Arithmetic and Logical Instructions
Instructions (MIPS)

## Slide 12: Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction specifies exactly three operands
  destination  source1 op source2
All operands are contained in the Register File
  $t0, $s1, $s2 are in Register File

## Slide 13: How does it work?
sub $t0, $s1, $s2
Register File
src1 reg no
src2 reg no
src1 data
src2 data
$t0  R8
$s1  R17
$s2  R18
R0
R1
R8
25
R17
R18
17
18
10
25
10
-
dst addr
write data
15
8
15
15
R31
25
10
Arithmetic instructions can only change the contents of the Register File
  In CISC processors, arithmetic instructions are much more powerful – they can read and change the contents of the memory

## Slide 14: Data Transfer Instructions
Instructions (MIPS)

## Slide 15: Accessing Memory
MIPS has two basic data transfer instructions for accessing memory
Lw $t0, 4($s3) #load word from memory
Sw $t0, 8($s3) #store word to memory
(assume $s3 holds 2410)
The data transfer instruction must specify
  Memory address
    where in memory to read from (load) or write to (store)
  Register destination (source)
    where in the register file to write to (load) or read from (store)
The memory address is formed by
  Adding the constant portion of the instruction and the contents of the second register
28
32
Notes: For lecture
What is the memory address of the given load and store instructions if $s3 contains the address 24?

## Slide 16: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the MIPS assembly code for the C statement
A[8] = A[2] - b
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
Notes: For lecture
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)

## Slide 17: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the MIPS assembly code for the C statement
A[8] = A[2] - b
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
Notes: For lecture
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)

## Slide 18: Branch Instructions
Instructions (MIPS)

## Slide 19: Branch Instructions
Decision making instructions
  alter the control flow of the program
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: bne $s0, $s1, Label #go to Label if $s0$s1 beq $s0, $s1, Label #go to Label if $s0=$s1
Example: if (i==j) h = i + j;
bne $s0, $s1, Lab1 add $s3, $s0, $s1 Lab1: ...

## Slide 20: Unconditional Jumps
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Example: if (i!=j) h=i+j; else h=i-j;
beq $s0, $s1, Lab1 add $s3, $s0, $s1 j Lab2 Lab1: sub $s3, $s0, $s1 Lab2: ...

## Slide 21: Compiling Loops
Compile the assembly code for the C while loop where i is in $s0, j is in $s1, and k is in $s2
while (i!=k) i=i+j;
Loop: beq $s0, $s2, Exit add $s0, $s0, $s1 j Loop Exit: . . .

## Slide 22: Summary of MIPS Instructions
Category | Instruction | Op Code | Example
Arithmetic (R format) | add | 0 and 32 | add $s1, $s2, $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3
Data Transfer (I format) | load word | 35 | lw $s1, 100($s2)
 | store word | 43 | sw $s1, 100($s2)
Cond. Branch | br on equal | 4 | beq $s1, $s2, L
 | br on not equal | 5 | bne $s1, $s2, L
Uncond. Jump | jump | 2 | j 2500
 | jump register | 0 and 8 | jr $t1