## Slide 1: Lecture 2-2 Stacks & Registers Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module1

## Slide 2
Agenda
Requirements for Functions
  Pass arguments to the function
  Get results from the function
  Can call the function from anywhere
  Can always return back
  Nested and recursive functions
  Saving and restoring registers
  Functions with more than 4 parameters

## Slide 3: Stacks and Registers for Function Calls
Function Calls

## Slide 4: Using the Stack for Saving & Restoring Registers
sumSquare:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x)
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y;
  }
“push”
Stack
0xFFFB
0xFFF7
[$ra]
$a1=y
[0($sp)]
[4($sp)]
$sp
0x
0xFFF7

## Slide 5: Using the Stack for Saving & Restoring Registers
sumSquare:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x)
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y;
  }
“push”
“pop”
Stack
0xFFFB
0xFFF7
[$ra]
$a1=y
[0($sp)]
[4($sp)]

## Slide 6: Using the Stack for Saving & Restoring Registers
sumSquare:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x)
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y;
  }
“push”
“pop”
Stack
0xFFFB
0xFFF7
[$ra]
$a1=y
[0($sp)]
[4($sp)]

## Slide 7: Using the Stack for Saving & Restoring Registers
sumSquare:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x)
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y;
  }
“push”
“pop”
Stack
0xFFFB
0xFFF7
[$ra]
$a1=y
[0($sp)]
[4($sp)]

## Slide 8: Register Conventions
CalleR: the calling function
CalleE: the function being called
When callee returns from executing, the caller needs to know which registers may have changed and which are guaranteed to be unchanged.
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (jal) and which may be changed.

## Slide 9: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 10: Summary - Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call the function from anywhere
  jal
Can always return back
  jr
Nested and recursive functions
  Save $ra on stack
Saving and restoring registers
  Register Conventions
Functions with more than 4 parameters
  Pass them on the stack

## Slide 11: Example of Procedure Call
leaf_example:
addi $sp,$sp,-12 # space on stack
sw $t1, 8($sp) # save $t1
sw $t0, 4($sp) # save $t0
sw $s0, 0($sp) # save $s0
add $t0,$a0,$a1 # $t0 = g+h
add $t1,$a2,$a3 # $t1 = i+j
sub $s0,$t0,$t1 # (g+h)-(i+j)
add $v0,$s0,$zero # save the return value
lw $s0, 0($sp) # restore $s0
lw $t0, 4($sp) # restore $t0
lw $t1, 8($sp) # restore $t1
addi $sp,$sp, 12 # adjust stack to delete 3 items
jr $ra
  int leaf_example(int g, int h, int i, int j) {
  int f;
  f = (g+h)-(i+j); return f;
  }
Stack
0xFFFF
0xFFFB
$t1
$t0
[4($sp)]
[8($sp)]
[0($sp)]
0xFFF7
$s0

## Slide 12: Example of Procedure Call (alt.)
leaf_example:
addi $sp,$sp,-8 # space on stack
sw $t1, 4($sp) # save $t1
sw $t0, 0($sp) # save $t0
add $t0,$a0,$a1 # $t0 = g+h
add $t1,$a2,$a3 # $t1 = i+j
add $v0,$t0,$t1 # save the return value
lw $t0, 0($sp) # restore $t0
lw $t1, 4($sp) # restore $t1
addi $sp,$sp, 8 # adjust stack to delete 2 items
jr $ra
  int leaf_example(int g, int h, int i, int j) { return (g+h)-(i+j);
  }
Stack
0xFFFF
0xFFFB
$t1
$t0
[0($sp)]
[4($sp)]

## Slide 13: Example of Recursive Call (factorial)
  int fact (int n) {
  if (n < 1)
  return (1);
  else
  return (n * fact(n – 1)); }

## Slide 14: Example of Recursive Call (factorial)
fact:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save $ra
sw $a0, 0($sp) # save $a0 (argument)
slti $t0,$a0,1 # test for n < 1
beq $t0,$zero,Lab1 # if n >= 1, go to Lab1
addi $v0,$zero,1 # return 1
addi $sp,$sp,8 # adjust stack
jr $ra # return to caller
Lab1: addi $a0, $a0,-1 # n >= 1: argument($a0) gets (n-1)
jal fact # call fact recursively with (n-1)
lw $a0, 0($sp) # return from jal: restore argu. N
lw $ra, 4($sp) # restore the return address
addi $sp,$sp,8 # adjust stack to pop 2 items
mul $v0,$a0,$v0 # return n*fact(n-1)
jr $ra # return to the caller
  int fact (int n) {
  if (n < 1) return (1);
  else return (n * fact(n – 1));}
Stack
0xFFFF
0xFFFB
$ra
$a0
[0($sp)]
[4($sp)]