## Slide 1: Lecture 2-3 Assembly Code Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module1

## Slide 2
Agenda
Arithmetic Instruction and Assembly
Load/Store Instruction and Assembly
Branch Instruction and Assembly

## Slide 3: Assemble Arithmetic Instructions
Assembly Code

## Slide 4: MIPS Instruction Fields
op
rs
rt
rd
shamt
funct
op rs rt rd shamt funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
= 32 bits
: opcode indicating operation to be performed
: address (or name) of the first register source operand
: address (or name) of the second register source operand
: the register destination address
: shift amount (for shift instructions)
: function code that selects the specific variant of the operation specified in the opcode field
R Format
Notes: for lecture

## Slide 5: Assembly Generation: Arithmetic Instructions
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0,$s1,$s2
  registers have numbers $t0=$8, $s1=$17, $s2=$18
Instruction Format:
000000 10001 10010 01000 00000 100000
0
31
op rs rt rd shamt funct
Notes: For lecture

## Slide 6: Assemble Load/Store Instructions
Assembly Code

## Slide 7: Assembly Generation: Load Instruction
op rs rt 16 bit number
100011 10010 01000 0000000000011000
35 18 8 24
I Format
Introduce a new type of instruction format
  I-type for data transfer instructions
  previous format was R-type for register
Example: lw $t0, 24($s2)
Notes: For lecture
destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 8: Assembly Generation: Store Instruction
sw $t0, 24($s2)
op rs rt 16 bit number
43 18 8 24
10101110010010000000000000011000
A 16-bit address means that access is limited to memory locations within a region of 213 or 8,192 words (215 or 32,768 bytes) of the address in the base register $s2
Notes: For lecture
why is it 2**13 (2**15) and NOT 2**14 (2**16) like we just saw with memory (here we have to represent signed numbers so the most significant bit is the sign bit)

## Slide 9: Assemble Branch Instructions
Assembly Code

## Slide 10: Assembling Branches
op rs rt 16 bit number
I format
5 16 17 ????
4 16 17 ????
How is the branch destination address specified?
Instructions:
bne $s0, $s1, Label #go to Label if $s0$s1 beq $s0, $s1, Label #go to Label if $s0=$s1
Machine Formats:

## Slide 11: What happens to the br. offset ?
32
32
32
32
32
32
PC
Add
4
Add
br offset
2
16
00
Offset Pre-processing:
Sign Extended 16-bit offset
Shift-left 2-bits, to access the correct instruction word
Branch instructions
 Offset + PC + 4
= Distance (in number of bytes) to the target from PC+4

## Slide 12: Assembling Branches Example
op rs rt 16 bit offset
5 16 17
I format
1
Remember
  After the bne instruction is fetched, the PC is updated to address the add instruction (PC = PC + 4).
  Two low-order zeros are concatenated to the offset number (which is a sign-extended 32-bit value) is added to the (updated) PC
Assembly code
bne $s0, $s1, Lab1 add $s3, $s0, $s1 Lab1: ...
Machine Format of bne:
Notes: For lecture.
For the code shown, the offset field should be 1 instruction (resulting in 4 = 1|00) not two instructions (resulting in 8 = 10|00) since the PC is now pointing to the add instruction (after the bne is fetched).

## Slide 13: Assembling Jumps
Instruction:
j label #go to label
Machine Format:
How is the jump destination address specified?
  As an absolute address formed by
    concatenating the upper 4 bits of the current PC (now PC+4) to the 26-bit address and
    concatenating 00 as the 2 low-order bits
op 26-bit address
J format
2 ????

## Slide 14: Summary - MIPS R3000 ISA and Assembly
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point: coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
Registers
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
3 Instruction Formats: all 32 bits wide
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target