## Slide 1: Lecture 3-1 Simple Processor Design Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module1

## Slide 2
Agenda
Simple Processor Design
  Fetching
  Decoding
  Executing

## Slide 3: Processor Design
Simple Processor Implementation

## Slide 4: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory (IM)
  updating the PC to hold the address of the next instruction
Control Signals for Fetching
  PC is updated every cycle, so it doesn’t need an explicit write control signal
  IM is read every cycle, so it doesn’t need an explicit read control signal
Add
4
32
Read
Address
Instruction
Instruction Memory
PC
32

## Slide 5: Decoding Instructions
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
Control
Unit
rs
rt
op, funct
6+6=12
Register File
Decoding instructions involves
  sending the fetched instruction’s opcode (6) and function field (6) bits to the control unit
  Reading two values from the Register File
    Register file addresses (rs & rt) are contained in the instruction

## Slide 6: Executing R Format Operations
R-type
31
25
20
op
rs
rt
15
5
0
rd
funct
shamt
10
Instr
W Data
R Addr 1
R Addr 2
W Addr
Read
Data 1
Read
Data 2
A L U
overflow
zero
ALU control
rd
Register File
RegWrite
R format operations
  add, sub, slt, and, or, etc.
  perform the indicated (by op and funct) operation on values in rs and rt
  store the result back into the Register File (into location rd)
  Note that Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File

## Slide 7: Executing Load and Store
Load and store operations
  compute a memory address by adding the base register (in rs) to the 16-bit signed offset field in the instruction
    base register was read from the Register File during decode
    offset value in the low order 16 bits of the instruction must be sign- extended to create a 32-bit signed value
  store value, read from the Register File during decode: must be written to the Data Memory
  load value, read from the Data Memory: must be stored in the Register File
I-Type:
op
rs
rt
address offset
31
25
20
15
0
15
5
0
rd
funct
shamt
10
R-Type:

## Slide 8: Executing Store and Load
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Address
Write Data
Sign
Extend
MemWrite
MemRead
16
32
Base Address in [rs]
Bits 15-0
from
Instruction
Computed Address
Data for
Memory Write
Data from
Memory Read
Register File
Data Memory
Notes: For lecture

## Slide 9: Executing Branch Operations
Conditional Branch operations have to
  compare the operands read from the Register File during decode (rs and rt values) for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the sign-extended 16-bit offset field in the instruction
    “base register” is the updated PC
    offset value in the low order 16 bits of the instruction must be sign-extended to create a 32-bit signed value
    and then shifted left by 2 bits to turn it into a word address
I-Type:
op
rs
rt
address offset
31
25
20
15
0

## Slide 10: Executing Branch Operations
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch
control logic)
Bits 15-0 from Instruction
Data for compare operation
32
PC + 4
Update PC to Fetch the next Instruction
Notes: For lecture

## Slide 11: Executing Jump Operations
Read
Address
Instr
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
addr
26
4
28
J-Type:
op
31
25
0
jump target address
[25-0]
From Instruction
Bits [31-28]
from PC+4
Jump operations have to
  replace the lower 28 bits of the PC with the lower 26 bits (target address) of the fetched instruction shifted left by 2 bits

## Slide 12
Fetch, Decode, & Execute Instructions
Instruction Formats
Summary
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target