## Slide 1: Lecture 5 Hazards Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module2

## Slide 2
Agenda
Structural Hazard
Data Hazard
Control Hazard

## Slide 3: Structural Hazards
Hazard

## Slide 4: Instructions interact within the Pipeline
Structural Hazard – An instruction in the pipeline needs a resource being used by another instruction in the pipeline
Data Hazard – An instruction depends on a data value produced by an earlier instruction
Control Hazard – Whether or not an instruction should be executed, depends on a control decision made by an earlier instruction
Hazards

## Slide 5: Memory Structures
Unified Memory
Instructions + Data
Unified Memory
Inst Addr
Data Addr
Data
Inst
Instruction Memory
Harvard Memory
Inst Addr
Data Addr
Data
Inst
Data Memory
ALU
Reg
IM
DM
Reg
ALU
Reg
IM
DM
Reg

## Slide 6: Structural Hazard
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
Time
Load
Instruction 1
Instruction 2
Instruction 3
Instruction 4
What’s the problem here?
In the case of “Unified Memory”

## Slide 7: Structural Hazards - Overview
Structural hazards occur when two instructions need the same hardware resource at the same time.
Approaches to resolving structural hazards:
  Schedule – Programmer explicitly avoids scheduling instructions that would create structural hazards
  Stall – Hardware includes control logic that stalls until either instruction is no longer using contended resource
  Duplicate – Add more hardware to design so that each instruction can access independent resources at the same time
Simple 5-stage MIPS pipeline has no structural hazard specifically because the ISA was designed that way.

## Slide 8: How is it resolved?
Time
Stall
Instruction 3
B
B
B
B
B
Pipeline generally stalled by
inserting a “bubble” or NOP
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
ALU
Reg
Mem
DM
Reg
Load
Instruction 1
Instruction 2
ALU
Reg
Mem
DM
Reg

## Slide 9: Or alternatively…
Inst. # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
LOAD | IF | ID | EX | MEM | WB |  |  |  |  | 
Inst. i+1 |  | IF | ID | EX | MEM | WB |  |  |  | 
Inst. i+2 |  |  | IF | ID | EX | MEM | WB |  |  | 
Inst. i+3 |  |  |  | stall | IF | ID | EX | MEM | WB | 
Inst. i+4 |  |  |  |  |  | IF | ID | EX | MEM | WB
Inst. i+5 |  |  |  |  |  |  | IF | ID | EX | MEM
Inst. i+6 |  |  |  |  |  |  |  | IF | ID | EX
Clock Number
LOAD instruction “steals” an instruction fetch cycle which will cause the pipeline to stall.
Thus, no instruction completes on clock cycle 8

## Slide 10: Dual-port vs. Single-port Memory
Machine A: Dual ported memory (“Harvard Architecture”)
Machine B: Single ported memory, but its pipelined implementation has a 1.05 times faster clock rate
Ideal CPI = 1 for both
Loads are 40% of instructions executed
SpeedUpB = SpeedUpA * 1.05 / 1.4
= SpeedUpA * 0.75
SpeedUpA / SpeedUpB = 1.33

## Slide 11
An instruction in the pipeline needs a resource being used by another instruction in the pipeline – ( ) hazard
List Approaches to resolving structural hazards
Quiz / Assignments
① Structural ② Data ③ Control

## Slide 12
Structural Hazards
Dual-port vs. Single-port Memory
Summary