## Slide 1: Lecture 6 Control Hazards and Branch Prediction Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module2

## Slide 2
Agenda
Structural Hazard
Data Hazard
Control Hazard

## Slide 3: Control Hazards
Hazard

## Slide 4: Control Hazards
When the flow of instruction addresses is not sequential (i.e., PC = PC + 4); incurred by change of flow instructions
  Conditional branches (beq, bne)
  Unconditional branches (j, jal, jr)
  Exceptions
Possible approaches
  Stall (impacts CPI)
  Move decision point as early in the pipeline as possible, thereby reducing the number of stall cycles
  Delay slot (requires compiler support), Predication, Branch Hinting (requires compiler support), Predict and hope for the best !
Control hazards occur less frequently than data hazards, but there is nothing as effective against control hazards as forwarding is for data hazards

## Slide 5: Datapath Branch and Jump Hardware
ID/EX
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign Extend
EX/MEM
MEM/WB
Control
ALU
Control
Forward
Unit
Branch
PCSrc
Shift
left 2
Add
Shift
left 2
Jump
PC+4[31-28]
Notes: For lecture

## Slide 6: Jumps Incur One Stall
Fortunately, jumps are very infrequent – only 3% of the SPECint instruction mix
Jumps not decoded until ID, so one flush is needed
flush
I
n
s
t
r.
O
r
d
e
r
j
j target
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix jump hazard
by waiting – stall –
but affects CPI
ALU
IM
Reg
DM
Reg
Notes: Fortunately, jumps are very infrequent – less that 2% of the SPECint instructions and x% of the SPECfp ones.

## Slide 7: Supporting ID Stage Jumps
ID/EX
Read
Address
Instruction
Memory
Add
PC
4
Register File
16
32
ALU
Data
Memory
IF/ID
Sign Extend
EX/MEM
MEM/WB
Control
ALU
cntrl
Forward
Unit
Branch
PCSrc
Shift
left 2
Add
Shift
left 2
Jump
PC+4[31-28]
0
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
Address
Write Data
Read
Data
Notes: For lecture

## Slide 8: Two “Types” of Stalls
Noop instruction (or bubble) inserted between two instructions in the pipeline (as done for load-use situations)
  Keep the instructions earlier in the pipeline (later in the code) from progressing down the pipeline for a cycle (“bounce” them in place with write control signals)
  Insert noop by zeroing control bits in the pipeline register at the appropriate stage
  Let the instructions later in the pipeline (earlier in the code) progress normally down the pipeline
Flushes (or instruction squashing) were an instruction in the pipeline is replaced with a noop instruction (as done for instructions located sequentially after j instructions)
  Zero the control bits for the instruction to be flushed

## Slide 9: Branches incur three cycle stalls
flush
flush
flush
I
n
s
t
r.
O
r
d
e
r
beq
ALU
IM
Reg
DM
Reg
beq target
ALU
IM
Reg
DM
Reg
Fix branch hazard by waiting – stall – but affects CPI
Notes: Another “solution” is to put in enough extra hardware so that we can test registers, calculate the branch address, and update the PC during the second stage of the pipeline. That would reduce the number of stalls to only one.
A third approach is to prediction to handle branches, e.g., always predict that branches will be untaken. When right, the pipeline proceeds at full speed. When wrong, have to stall (and make sure nothing completes – changes machine state – that shouldn’t have). Will talk about these options in more detail in next,next lecture.

## Slide 10: Moving Branch Decisions Earlier in Pipe
Solution 1: Move the branch decision hardware back to the EX stage
  Reduces the number of stall (flush) cycles to two
  Adds an and gate and a 2x1 mux to the EX timing path
10
Notes: Want a small branch penalty.
Need more forwarding and hazard detection hardware for second option (one stall implementation) since a branch depended on a result still in the pipeline (that is one of the source operands for the comparison logic) must be forwarded from the EX/MEM or MEM/WB pipeline latches.

## Slide 11: Datapath Branch and Jump Hardware
ID/EX
Read
Address
Instruction
Memory
Add
PC
4
Register File
16
32
ALU
Data
Memory
IF/ID
Sign Extend
EX/MEM
MEM/WB
Control
ALU
cntrl
Forward
Unit
Branch
PCSrc
Shift
left 2
Add
Shift
left 2
Jump
PC+4[31-28]
Write Data
Read Addr 1
Read Addr 2
Write Addr
Read
Data 1
Read
Data 2
Address
Write Data
Read
Data
Notes: For lecture

## Slide 12: Moving Branch Decisions Earlier in Pipe
Solution 1: Move the branch decision hardware back to the EX stage
Solution 2: Add hardware to compute the branch target address and evaluate the branch decision in the ID stage
  Reduces the number of stall (flush) cycles to one
    like with jumps
    But now need to add forwarding hardware in ID stage
  Computing branch target address can be done in parallel with RegFile read (done for all instructions – only used when needed)
  Comparing the registers can’t be done until after RegFile read, so comparing & updating the PC adds a mux, a comparator, & an and gate to the ID timing path
For deeper pipelines, branch decision points can be even later in the pipeline, incurring more stalls
Notes: Want a small branch penalty.
Need more forwarding and hazard detection hardware for second option (one stall implementation) since a branch depended on a result still in the pipeline (that is one of the source operands for the comparison logic) must be forwarded from the EX/MEM or MEM/WB pipeline latches.

## Slide 13
Explain control hazards and why they occur in the pipelined processors
List the simplest solution to fix control hazards
Quiz / Assignments

## Slide 14
Control Hazards
Stalls and Early Branch Decisions
Summary