## Slide 1: Lecture 9 Virtual Memory Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
  Bypasses
  Branch Prediction
  Out-of-order Scheduling
Memory Hierarchy
  Direct-mapped Cache
  Set-associative Cache
  Cache Parameters
  Virtual Memory
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler

## Slide 3
Agenda
Use DRAM as a Cache for DISK
Memory Management – i) Memory Sharing among Multiple Programs
Memory Management – ii) Memory Protections

## Slide 4: Motivation of Virtual Memory
Use DRAM as a Cache for Disk
  To allow a single user program to exceed the size of primary memory
  Making it fit into primary memory was up to the programmer
  Automatically manage two levels of the memory hierarchy represented by main memory and secondary storage
Memory Management
  To allow efficient and safe sharing of memory among multiple programs
    (eg) the memory needed by multiple virtual machines for cloud computing
  Implement the translation of a program’s address space to physical addresses

## Slide 5: Use DRAM as a Cache for DISK
Virtual Memory

## Slide 6
The full address space is quite large:
  32-bit addresses: ~4,000,000,000 (4 billion) bytes
  64-bit addresses: ~16,000,000,000,000,000,000 (16 quintillion) bytes
Disk storage is ~30X cheaper than DRAM storage
  8 GB of DRAM: ~ $12,000
  8 GB of disk: ~ $400
To access large amounts of data in a cost-effective manner, the bulk of the data must be stored on disk
8 GB: ~$400
256 MB: ~$400
4 MB: ~$400
Disk
DRAM
SRAM
Motivation # 1: DRAM a “Cache” for Disk

## Slide 7
Size-Speed-Cost-Tradeoff
CPU
regs
Memory
disk
16 B
8 B
4 KB
cache
virtual memory
C
a
c
h
e
C
a
c
h
e
 | register reference | L1-cache reference | L2-cache reference | memory reference | disk memory reference
Size | 608B | 128kB | 512kB~ 4MB | 128MB | 27GB
Speed | 1.4ns | 4.2ns | 16.8ns | 112ns | 9 ms
$/Mbyte |  |  | $90/MB | $2~6/MB | $ 0.01/MB
Block size | 4B | 16B | 16B | 4~8 KB | 
larger, slower, cheaper
(Numbers are for a 21264 at 700MHz)

## Slide 8
DRAM vs. disk is more extreme than SRAM vs. DRAM
  access latencies:
    DRAM is ~10X slower than SRAM
    disk is ~100,000X slower than DRAM
  importance of exploiting spatial locality:
    first byte is ~100,000X slower than successive bytes on disk
      vs. ~4X improvement for page-mode vs. regular accesses to DRAM
  “cache” size:
    main memory is ~100X larger than an SRAM cache
  addressing for disk is based on sector address, not memory address
Disk
DRAM
SRAM
DRAM vs. SRAM as a “Cache”

## Slide 9
Search for matching tag
  SRAM cache
Use indirection to look up actual object location
  virtual memory
Locating an Object in a “Cache”
X
Object Name
Tag
Data
D
243
0:
1:
N-1:
= X?
“Cache”
X
17
J
105
X
Object Name
Lookup Table
0
N-1
1
D:
J :
X:
“Cache”
243
17
105
N-1:
0:
1:
= X?

## Slide 10
Examples:
  most Cray machines, early PCs, nearly all embedded systems, etc.
0:
1:
N-1:
Memory
Store 0x10
Load 0xf0
CPU’s load or store addresses used directly to access memory.
A System with Physical Memory Only
CPU

## Slide 11
Examples:
  workstations, servers, modern PCs, etc.
Address Translation: the hardware converts virtual addresses into physical addresses via an OS-managed lookup table (page table)
0:
1:
N-1:
Memory
Load 0xf0
0:
1:
P-1:
Page Table
Store 0x10
Disk
Virtual
Addresses
Physical
Addresses
P = Total number of virtual pages
A System with Virtual Memory
CPU

## Slide 12
What if an object is on disk rather than in memory?
  Page table entry indicates that the virtual address is not in memory
  An OS trap handler is invoked, moving data from disk into memory
    current process suspends, others can resume
    OS has full control over placement, etc.
Page Faults (Similar to “Cache Misses”)
0:
1:
N-1:
Memory
Load 0xf8
0:
1:
P-1:
Page Table
Store 0x05
Disk
Virtual
Addresses
Physical
Addresses
CPU

## Slide 13
Processor Signals Controller
  Read block of length P starting at disk address X and store starting at memory address Y
Read Occurs
  Direct Memory Access
  Under control of I/O controller
I / O Controller Signals Completion
  Interrupt processor
  Can resume suspended process
Memory-I/O bus
Processor
Cache
Memory
I/O
controller
Reg
(2) DMA Transfer
(1) Initiate Block Read
(3) Read Done
Servicing a Page Fault
Disk
Disk

## Slide 14: Memory Management – i) Memory Sharing
Virtual Memory

## Slide 15
Multiple processes can reside in physical memory.
How do we resolve address conflicts?
Reserved
Text (Code)
Static Data
Stack
Dynamic Data
0000 03FF 8000 0000
Reserved
0000 0001 2000 0000
0000 0000 0001 0000
$gp
$sp
e.g., what if two different Alpha processes access their stacks at address 0x11fffff80 at the same time?
(Virtual) Memory Image for Alpha Process
Motivation #2: Memory Management
Not yet allocated
Not yet allocated

## Slide 16
Virtual and physical address spaces divided into equal-sized blocks
  “Pages” (both virtual and physical)
Each process has its own virtual address space
  operating system controls how virtual pages are assigned to physical memory
Process 1:
Virtual Addresses
Physical Addresses
VP 1
VP 2
Process 2:
PP 2
Address Translation
0
N-1
0
M-1
PP 7
PP 10
(Read-only
library code)
Solution: Separate Virtual Address Spaces
VP 1
VP 2
0
N-1

## Slide 17: Memory Management – ii) Protection
Virtual Memory

## Slide 18
Page table entry contains access rights information
  hardware enforces this protection (trap into OS if violation occurs)
Page Tables
Process i:
Physical Addr
Read?
Write?
Yes
No
Yes
Yes
No
No
VP 0:
VP 1:
VP 2:
•
•
•
•
•
•
Process j:
0:
1:
N-1:
Memory
Physical Addr
Read?
Write?
Yes
Yes
Yes
No
No
No
•
•
•
•
•
•
VP 0:
VP 1:
VP 2:
Motivation #3: Protection
PP 9
PP 4
XXXXXXX
•
•
•
PP 6
PP 9
XXXXXXX
•
•
•

## Slide 19
If DRAM was to be organized similar to an SRAM cache, how would we set the following design parameters?
  Line size?
  Associativity?
  Replacement policy (if associative)?
  Write through or write back?
What would the impact of these choices be on:
  miss rate
  hit time
  miss latency
  tag overhead
Assignments: Impact of These Properties on Design?

## Slide 20
Virtual Memory Motivation 1: DRAM as a Cache for DISK
Summary
Virtual Memory Motivation 2: Memory Management – i) Memory Sharing among Multiple Programs, ii) Memory Protections
Next: Virtual Address Translation and TLB