## Slide 1: Lecture 9 Virtual Memory Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
  Bypasses
  Branch Prediction
  Out-of-order Scheduling
Memory Hierarchy
  Direct-mapped Cache
  Set-associative Cache
  Cache Parameters
  Virtual Memory
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler

## Slide 3
Agenda
Virtual Memory Address Translation
Integrating Virtual Memory and Cache – Two Level Memory Hierarchy
Translation Lookaside Buffer (TLB)

## Slide 4: Virtual Memory Address Translation
Virtual Memory

## Slide 5: Page Tables
0
1
0
1
1
1
1
0
1
1
Page Table
(physical page
or disk address)
Physical Memory
Disk Storage
Valid
Virtual Page
Number

## Slide 6: Virtual Memory Address Translation (Mapping)
V = {0, 1, . . . , N–1} virtual address space
P = {0, 1, . . . , M–1} physical address space
MAP: V  P U {} address mapping function
N > M
MAP(a) = a' if data at virtual address a is present at physical address a' in P
=  if data at virtual address a is not present in P
Processor
Address
Translation
Mechanism
fault
handler
Main
Memory
Secondary memory
a
a'

missing item fault
physical address
OS performs this transfer
(only if miss)

## Slide 7: Virtual Memory Address Translation
virtual page number
page offset
virtual address
physical page number
page offset
physical address
0
p–1
address translation
p
m–1
n–1
0
p–1
p
Notice that the page offset bits don't change as a result of translation
Parameters
  P = 2p = page size (bytes). Typically 1KB–16KB
  N = 2n = Virtual address limit
  M = 2m = Physical address limit

## Slide 8: Address Translation via Page Table
virtual page number
page offset
virtual address
physical page number
page offset
physical address
0
p–1
p
m–1
n–1
0
p–1
p
page table base register
if valid=0
then page
not in memory
valid
physical page number
access
VPN acts as
table index
Address

## Slide 9: Page Table Operation
Translation
  Separate (set of) page table(s) per process
  VPN (Virtual Page Number) forms index into page table
Computing Physical Address
  Page Table Entry (PTE) provides information about page
    if (Valid bit = 1) then page in memory.
      Use physical page number (PPN) to construct address
    if (Valid bit = 0) then page in secondary memory
      Page fault
      Must load into main memory before continuing

## Slide 10: Page Table Operation (cont’)
Checking Protection
  Access rights field indicate allowable access
    e.g., read-only, read-write, execute-only
    typically support multiple protection modes (e.g., kernel vs. user)
  Protection violation fault if it doesn’t have necessary permission

## Slide 11: Integrating Virtual Memory & Cache
Virtual Memory

## Slide 12: Integrating Virtual Memory and Cache
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
Most Caches “Physically Addressed”
  Accessed by physical addresses
  Allows multiple processes to have blocks in cache at same time
  Allows multiple processes to share pages
  Cache doesn’t need to be concerned with protection issues
    Access rights checked as part of address translation
Perform Address Translation Before Cache Lookup
  But this could involve a memory access itself
  Of course, page table entries can also become cached

## Slide 13: Translation Looaside Buffer (TLB)
Virtual Memory

## Slide 14: Speeding up Translation with a TLB
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
“Translation Lookaside Buffer” (TLB)
  Small, usually fully associative cache
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages
    TLB is nothing but a Cache of the Page Table
    Most recently accessed page-table entries.

## Slide 15: Address Translation with a TLB
virtual address
N–1
0
p–1
p
valid
physical page number
tag
dirty
valid
tag
data
data
cache hit
tag
byte offset
index
TLB hit
virtual page number
page offset
process ID
=
= physical address(tag+index+offset)
TLB
Cache
=
physical page number page offset

## Slide 16: Assignments 1
Q1. Consider a system with Data page size = 2KB, and processor cache configuration – 1KB, fully associative cache; and TLB of 8 entries, with FIFO replacement policy. The following program is executed on this system.
#define N = 2560
int A[N]; // each element is a word = 4 Bytes
for ( i=0; i<N; i++)
C = A[ i ];
For the execution of the above program, what is the total number of TLB misses incurred?
5/4/2017
Notes: Total data accessed by the program = 2560 × 4 = 10240 Bytes = 10 KB
Total number of pages accessed = 5 = Total number of TLB entries used

## Slide 17: Assignments 2
Q2 : I have modified the program as follows:
#define N = 2560
int A[N]; // each element is a word = 4 Bytes
for ( k=0; k<5; k++)
for ( i=0; i<N; i+=2)
C = A[ i ];
For the execution of the above program, and for the same system setup, what is the total number of TLB misses incurred?
Hint: Pay attention to the data access pattern and the for loops
5/4/2017
Notes: Total data accessed by the program = 2560 × 4 = 10240 Bytes = 10 KB
Total number of pages accessed = 5 = Total number of TLB entries used
Note: The same data is accessed twice by the program, and therefore the number of TLB entries accessed are the same as earlier.

## Slide 18: Assignments 3
Q3. Consider a system with 43-bit virtual address, and 26-bit physical address space. For such a system, we need virtual memory system, and page tables. Suppose the page table entry size is 8 bytes. One way to create a page table is to create one single-level page table. Page size of the data memory = 8 KB.
What is the size of the page table, when 8192 KB of array A is allocated in the heap, for a single-level page table implementation?
Hint: You may assume that the array allocation is the one and only heap allocation in the program, and starts from a page boundary.
5/4/2017
Notes: 8KB page => 13 bit offset
243-13 = 230 VPNs
Page Table Size = (# VPNs) × (PTE size) = 230 * 8 = 233
Size of single level page table: 233B = 8GB

## Slide 19
Virtual Memory Translation
Summary
Integrating TLB, Virtual Memory, and Cache
Next: Out-of-Order Processor