## Slide 1: Lecture 7 Memory Hierarchy Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
  Bypasses
  Branch Prediction
  Out-of-order Scheduling
Memory Hierarchy
  Direct-mapped Cache
  Set-associative Cache
  Virtual Memory
  Inclusive Caches
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler

## Slide 3
Agenda
Memory Hierarchy
Caches

## Slide 4: Memory Hierarchy
Memory

## Slide 5: CPU-Memory Bottleneck
Ideally, as large as possible & as fast as possible
Performance of high-speed computers is usually limited by memory bandwidth & latency
  Latency (time for a single access)
    Memory access time >> Processor cycle time
    (e.g.) approximately ~60 ns >> 1 ns at Intel Core i7 Xeon 5500 series
  Bandwidth (number of accesses per unit time)
    if fraction m of instructions access memory,  1+m memory references / instruction  CPI = 1 requires 1+m memory refs / cycle
Memory
CPU

## Slide 6
Four-issue 2 GHz Superscalar accessing 100 ns DRAM could execute 800 instructions during time for one memory access!
Processor – DRAM Gap (Latency)

## Slide 7
Storage Latency: How Far Away is the Data?
Jim Gray’s slides - http://loci.cs.utk.edu/dsi/netstore99/docs/presentations/keynote/sld023.htm

## Slide 8: Why is bigger slower?
Physics slows us down
Racing the speed of light: (3.0x10^8m/s)
  clock = 500MHz
  how far can I go in a clock cycle?
  (3.0x10^8 m/s) / (500x10^6 cycles/s) = 0.6m/cycle
  For comparison: 21264 is about 17mm across
Capacitance:
  long wires have more capacitance
  either more powerful (bigger) transistors required, or slower
  signal propagation speed proportional to capacitance
  going “off chip” has an order of magnitude more capacitance

## Slide 9
Memory Hierarchy
Processor
Consist of multiple levels of memory with different speeds and sizes
Take advantage of the principle of locality (temporal and spatial localities)
Make an illusion of memory as large and fast as possible
Speed
Size
Cost ($/bit)
Current
Technology
Memory
Fastest
Smallest
Highest
SRAM
Memory
DRAM
Memory
Slowest
Biggest
Lowest
Magnetic
Disk

## Slide 10: Size-Speed-Cost Tradeoff
CPU
regs
Cache
Memory
disk
size:
speed:
$/Mbyte:
block size:
608 B
1.4 ns
4 B
register
reference
L2-cache
reference
memory
reference
disk memory
reference
512KB -- 4MB
16.8 ns
$90/MB
16 B
128 MB
112 ns
$2-6/MB
4-8 KB
27GB
9 ms
$0.01/MB
larger, slower, cheaper
8 B
16 B
4 KB
cache
virtual memory
Cache
128KB
4.2 ns
4 B
L1-cache
reference
(Numbers are for a 21264 at 700MHz)

## Slide 11
Memory Hierarchy | Latency
Registers | 1 ns
Caches | 4 ns
Main Memory | 112 ns
Hard Disk Drive | 9,000 ns
Memory Hierarchy Analogy – Library (writing a report)
Library | Latency (Assumption)
Information in the book | 1 s
Books in the desk | 4 s
Books in the bookshelf | 112 s
Books in the central library | 9,000 s

## Slide 12
An Alternative View of Memory Hierarchy
From UCSB

## Slide 13
Level | Access Time | Size
Registers | 1-3 ns | 1 KB
L1 Cache | 2-8 ns | 8-128 KB
L2 Cache | 5-12 ns | 0.5-8 MB
MM | 10-60 ns | 64MB-1GB
Another Alternative View of Memory Hierarchy

## Slide 14: Caches with Localities
Memory

## Slide 15: Locality of Reference
Principle of Locality:
  Programs tend to reuse data and instructions near those they have used recently
  Temporal locality: recently referenced items are likely to be referenced in the near future
  Spatial locality: items with nearby addresses tend to be referenced close together in time
Locality in Example:
  Data
    Reference array elements in succession (spatial)
  Instructions
    Reference instructions in sequence (spatial)
    Cycle through loop repeatedly (temporal)
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
*v = sum;

## Slide 16
Real Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)

## Slide 17
Typical Memory Reference Patterns
http://www-inst.eecs.berkeley.edu/~cs152/fa16/lectures/L06-Memory.pdf

## Slide 18: Caching: The Basic Idea
Main Memory
  Stores words
    A–Z in example
Cache
  Stores subset of the words
    4 in example
  Organized in lines
    Multiple words
    To exploit spatial locality
Access
  Word must be in cache for processor to access
Big, Slow Memory
A
B
C
•
•
•
Y
Z
Small,
Fast Cache
A
B
G
H
Processor

## Slide 19: How important are caches?
21264 Floorplan
Register files in middle of execution units
64 KB instruction cache
64 KB data cache
Caches take up a large fraction of the die
(Figure from Jim Keller, Compaq Corp.)

## Slide 20: Design Issues for Caches
Key Questions:
  Where should a line be placed in the cache? (line placement)
  How is a line found in the cache? (line identification)
  Which line should be replaced on a miss? (line replacement)
  What happens on a write? (write strategy)
Design Constraints:
  Design must be very simple
    Hardware realization
    All decision making within nanosecond time scale
  Want to optimize performance for “typical” programs
    Do extensive benchmarking and simulations
    Many subtle engineering tradeoffs

## Slide 21: The Cache Architecture
Decoder
Processor
Program
Memory Bus
Memory Address
Read/Write Data
Cache Blocks
MAIN MEMORY
Notes: 1) If the cache had a total of 16 blocks, with 16 bytes each,
- What is the size of the memory address ?
- How will you access byte x in Block y ?
Ans: 5bits for the 16blocks,
5bits for the 16bytes in each block
Total memory address size = 8bits
When you double the memory size, which bit differs in the modulo of cache size ?
- This is the tag id that is used to identify if the memory block in the cache -- > valid status
Now, modulo (# cache blocks) is the mapping from main memory to the cache.
To identify which cache block contains the required data, if valid bit =1, use the next set of bits to identify the set associated with the memory address.
3)

## Slide 22
What else can you see other than library as an analogy to memory hierarchy?
What makes CPU consider the memory as large as possible and as fast as possible (ideal memory)?
Quiz / Assignments

## Slide 23
Memory Hierarchy – Size vs Cost, Locality, Ideal Memory
Summary
Caches and Design Issues
Next: Direct Mapped Caches