## Slide 1: Lecture 7-2 Direct Mapped Caches Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2
Agenda
Direct Mapped Caches
Thrashing Example (Homework & Discussion at Class)
Cache Operations

## Slide 3: Direct Mapped Caches
Caches

## Slide 4: Direct-Mapped Caches: only one choice
Simplest Design
  Each memory line has a unique cache location
  32 memory lines & 8 cache lines
    Memory lines with addresses of 00101, 01101, 10101, & 11101 have cache line with 101
Notes: 1 Byte = 8 bits
4 Bytes = 1 word = 16 Bits
16 Bytes = 4 Words
32 Bytes = 8 Words

## Slide 5: Direct-Mapped Caches
Parameters
  Line (aka block) size: B = 2b
    Number of bytes (B) in each line
  Number of Sets: S = 2s
    Number of lines cache can hold
  Total Cache Size: B x S = 2b+s
Physical Address
  Address used to reference main memory
  n bits to reference N = 2n total bytes
  Partition into fields
    Offset: Lower b bits indicate which byte within line
    Set: Next s bits indicate how to locate line within cache
    Tag: Identifies this line when in cache
n-bit Physical Address
t
s
b
tag
set index
offset
Notes: 1 Byte = 8 bits
4 Bytes = 1 word = 16 Bits
16 Bytes = 4 Words
32 Bytes = 8 Words

## Slide 6: Indexing into Direct-Mapped Cache
Use set index bits to select cache set/block
Set 0:
0
1
• • •
B–1
Tag
Valid
0
1
• • •
B–1
Tag
Valid
0
1
• • •
B–1
Tag
Valid
Set 1:
Set S–1:
•
•
•
t
s
b
tag
set index
offset
Physical Address

## Slide 7: Direct-Mapped Cache Tag Matching
Identifying Line
  Must have tag match high order bits of address
  Must have Valid = 1
0
1
• • •
B–1
Tag
Valid
Selected Set:
t
s
b
tag
set index
offset
Physical Address
= ?
= 1?
Lower bits of address select byte or word within cache line

## Slide 8: Direct Mapped Cache
Main Memory
Q2: How do we find it?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Q1: Is it there?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
00
01
10
11
Cache
Tag
Data
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 9: Direct Mapped Cache
00
01
10
11
Cache
Tag
Data
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Index
0 0 0 0 0 0
0 0 0 0 0 1
0 0 0 0 1 0
0 0 0 0 1 1
tag
index
offset
0 0 0 0 0 0
0 0 0 0 0 1
0 0 0 0 1 0
0 0 0 0 1 1
tag
index
offset
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 10
8-blocks, 1 word/block, direct mapped
Initial state
Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Decimal Address | Binary Address | Hit or Miss | Cache Block
22 | 10110 |  | 110
26 | 11010 |  | 010
22 | 10110 |  | 110
26 | 11010 |  | 010
16 | 10000 |  | 000
3 | 00011 |  | 011
16 | 10000 |  | 000
18 | 10010 |  | 010
16 | 10000 |  | 000
Hit or Miss
Miss
Miss
Hit
Hit
Miss
Miss
Hit
Miss
Hit

## Slide 11
Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 12
Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 13
Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 14
Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 15
Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 16: Direct Mapped Cache
Cache Block (line): the cache data that has in its own cache tag
A 1Kbyte direct mapped cache with 1 word blocks for MIPS
  1 word = 4 Bytes
Cache Index
0
1
:
Cache Data
Byte 0
0
1
31
:
Cache Tag
Ex: 0x50
Ex: 0x01
0x50
Valid Bit
:
255
Byte 1
Byte 3
:
Byte 0
Byte 1
Byte 3
:
:
Cache Tag
Byte Select
Ex: 0x00
9
2
10

## Slide 17: Direct Mapped Cache
Cache Block (line): the cache data that has in its own cache tag
In order to take advantage of Spatial Locality: increase the block size
A 1Kbyte direct mapped cache with 32 byte blocks
Cache Index
0
1
:
Cache Data
Byte 0
0
4
31
:
Cache Tag
Ex: 0x50
Ex: 0x01
0x50
Valid Bit
:
31
Byte 1
Byte 31
:
Byte 0
Byte 1
Byte 31
:
:
Cache Tag
Byte Select
Ex: 0x00
9
5
10

## Slide 18: Multiword Block Direct Mapped Cache
Four words/block, cache size = 1K words = 4K Bytes
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
(word)
32
Block offset
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 19
How many total bits are required for a direct-mapped cache with 16 KB of data and 4 word blocks, assuming a 32-bit address?
Bits in a Cache
  16 KB is 4096 (212) words
  With a block size of 4 words, 1024 (210) blocks
  Each block has 4x32 or 128 bits of data plus a tag, which is 32 – 10 – 2 – 2 bits, plus a valid bit
  Thus, total cache size is
  210 x (4x32 + (32 – 10 – 2 – 2) + 1) = 210 x 147 = 147 K bits = 18.4 KB

## Slide 20
The total number of bits needed for a cache is a function of the cache size and the address size
Actual Size of Bits in a Cache (General)
  32-bit address (n = 32)
  A direct-mapped cache
  The cache size is 2s blocks, s bits are used for the index
  The block size is 2b-2 words (2b bytes), (b-2) bits are used for the word within the block
  Then, the size of the tag field is 32 – (s + b) = t
  The total number of bits in a direct-mapped cache is 2s x (block size + tag size + valid field size)
  2s x (2b-2 x n + t + 1) = actual size in bits
n-bit Physical Address
t
s
b
tag
set index
offset

## Slide 21
Consider a cache with 64 blocks and 16 bytes/block. To what block number does byte address 1200 map?
Mapping an Address to a Multiword Cache Block
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
  Block Address is Byte Address/Bytes per Block containing all addresses b/w (byte address/bytes per block)*bytes per block and (byte address/bytes per block)*bytes per block + (bytes per block – 1)
    Block address = 1200/16 = 75
  Block is given by (Block Address) modulo (Number of Blocks in the Cache)
    Block number = 75 modulo 64 = 11

## Slide 22: Properties of Direct Mapped Caches
Strength
  Minimal control hardware overhead
  Simple design
  (Relatively) easy to make fast
Weakness
  Vulnerable to thrashing
  Two heavily used lines have the same cache index
  Repeatedly evict one to make room for other
Cache Line

## Slide 23: Thrashing Example
Caches

## Slide 24: Vector Product Example
Machine
  DEC Station 5000
  MIPS Processor with 64KB direct-mapped cache, 16 B line size
Performance
  Good case: 24 cycles / iteration
  Bad case: 66 cycles / iteration
float dot_prod(float x[1024], y[1024])
{
float sum = 0.0;
int i;
for (i = 0; i < 1024; i++)
sum += x[i]*y[i];
return sum;
}

## Slide 25: Thrashing Example
Access one element from each array per iteration
x[1]
x[0]
x[1020]
•
•
•
•
•
•
x[3]
x[2]
x[1021]
x[1022]
x[1023]
y[1]
y[0]
y[1020]
•
•
•
•
•
•
y[3]
y[2]
y[1021]
y[1022]
y[1023]
Cache
Line
Cache
Line
Cache
Line
Cache
Line
Cache
Line
Cache
Line

## Slide 26: Thrashing Example: Good Case
Access Sequence
  Read x[0]
    x[0], x[1], x[2], x[3] loaded
  Read y[0]
    y[0], y[1], y[2], y[3] loaded
  Read x[1]
    Hit
  Read y[1]
    Hit
  • • •
  2 misses / 8 reads
x[1]
x[0]
x[3]
x[2]
y[1]
y[0]
y[3]
y[2]
Cache
Line
The TWO arrays are mapped to different blocks in the cache
Analysis
  x[i] and y[i] map to different cache lines
  Miss rate = 25%
    Two memory accesses / iteration
    On every 4th iteration have two misses
Timing
  10 cycle loop time
  28 cycles / cache miss
  Average time / iteration = 24
  10 + 0.25 * 2 * 28

## Slide 27: Thrashing Example: Bad Case
Access Pattern
  Read x[0]
    x[0], x[1], x[2], x[3] loaded
  Read y[0]
    y[0], y[1], y[2], y[3] loaded
  Read x[1]
    x[0], x[1], x[2], x[3] loaded
  Read y[1]
    y[0], y[1], y[2], y[3] loaded
  • • •
  8 misses / 8 reads
x[1]
x[0]
x[3]
x[2]
y[1]
y[0]
y[3]
y[2]
Cache
Line
The TWO arrays are mapped to SAME block in the cache
Analysis
  x[i] and y[i] map to same cache lines
  Miss rate = 100%
    Two memory accesses / iteration
    On every iteration have two misses
Timing
  10 cycle loop time
  28 cycles / cache miss
  Average time / iteration = 66
  10 + 1.0 * 2 * 28

## Slide 28: Cache Operation
Caches

## Slide 29: The Cache Architecture
Decoder
Processor
Program
Memory Bus
Memory address
Read/Write Data
Cache Blocks
MAIN MEMORY
Notes: 1) If the cache had a total of 16 blocks, with 16 bytes each,
- What is the size of the memory address ?
- How will you access byte x in Block y ?
Ans: 5bits for the 16blocks,
5bits for the 16bytes in each block
Total memory address size = 8bits
When you double the memory size, which bit differs in the modulo of cache size ?
- This is the tag id that is used to identify if the memory block in the cache -- > valid status
Now, modulo (# cache blocks) is the mapping from main memory to the cache.
To identify which cache block contains the required data, if valid bit =1, use the next set of bits to identify the set associated with the memory address.
3)

## Slide 30: Cache Operation
write to the
block
select block(s),
read tag and data
address from CPU
tag comparison
select & return
data to CPU
read or
write?
hit
read
write
miss
replace a
valid block
read from memory, write to cache, return data to CPU
write to
memory
write-through
write-back
immediate
later
read
read or
write?
write
available
block?
read from
memory
write-around
write-allocate
yes
no
yes
no

## Slide 31: Decreasing Miss Penalty with Multilevel Caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 5 GHz machine with a 5% miss rate, 100ns DRAM access
  Adding 2nd level cache with 5ns access time decreases miss rate to 0.5%
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache

## Slide 32
How do Direct Mapped Caches work with Tag, Valid, Index, and Offset?
Quiz / Assignments
What and how much is the cache miss penalty?
What is the main difference between Write-back and Write-through policies?

## Slide 33: Exercise 5.2
Caches are important to providing a high-performance memory hierarchy to processors. Below is a list of 32-bit memory address references, given as word addresses.
  3, 180, 43, 2, 191, 88, 190, 14, 191, 44, 186, 253
  For each of these references, identify the binary address, the tag, and the index given a direct-mapped cache with 16 one-word blocks. Also list if each reference is a hit or a miss, assuming the cache is initially empty.
  For each of these references, identify the binary address, the tag, and the index given a direct-mapped cache with two word blocks and a total size of 8 blocks. Also list if each reference is a hit or a miss, assuming the cache is initially empty.

## Slide 34: Exercise 5.3
For a direct-mapped cache design with a 32-bit address, the following bits of the address are used to access the cache.
  What is the cache block size (in words)?
  How many entries does the cache have?
  What is the ratio between total bits required for such a cache implementation over the data storage bits?
Tag | Index | Offset
31 – 10 | 9 – 5 | 4 – 0

## Slide 35
Direct Mapped Caches – Simplest Cache Design
Summary
Cache Operations: Write-back vs. Writh-through
Next: Set Associate Caches