## Slide 1: Lecture 8 Set Associative Caches Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
  Bypasses
  Branch Prediction
  Out-of-order Scheduling
Memory Hierarchy
  Direct-mapped Cache
  Set-associative Cache
  Cache Parameters
  Virtual Memory
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler

## Slide 3
Quiz 3 on Module 3 (Memory Hierarchy) will be delayed to 10 am on May 22nd , Mon
Due of Project 3 is May 15th, Mon
We will have 6 Wed Classes left this semester to cover 2.5 modules (Module 3/4/5)
    Considering Make-up classes on June 6th (Tue) and June 10th (Sat)
    Quiz 4 will be scheduled on June 5th, Mon
    Quiz 5 will be scheduled on June 12th, Mon
Yes, Final exam will be scheduled during the final week
Those who got 100 out of 100 for Quiz1 or Quiz2 are invited to Pizza Lunch at James Chicago Pizza Shinchon at noon on May 19th , Fri
Announcements
EXCITING Internship Recruiting at DClab during summer

## Slide 4
Agenda
Associative Caches
Associative Example
Implementation of Caches

## Slide 5: Associative Caches
Set Associative Caches

## Slide 6: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
N-way set associative
  Each set contains N entries
  Block number determines which set
    (Block number) modulo (Number of sets in cache)
  Search all entries in a given set at once
  N comparators (less expensive)

## Slide 7: Placement Policies
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Fully Associative
anywhere
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
block 12
can be placed
(2-way) Set
Associative
anywhere in set 0
(12 mod 4)
Direct Mapped
only into block 4
(12 mod 8)
0 1
(4-way) Set
Associative
anywhere in set 0
(12 mod 2)
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?

## Slide 8: Spectrum of Associativity
For a cache with 8 entries
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Block
0
1
2
3
4
5
6
7
Set
0
1
2
3
Set
0
1
One-way set associative (direct mapped)
Two-way set associative
Four-way set associative
Eight-way set associative (fully associative)

## Slide 9: Associative Example
Set Associative Caches

## Slide 10: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0]
8 | 0 | miss | Mem[8]
0 | 0 | miss | Mem[0]
6 | 2 | miss | Mem[0] |  | Mem[6]
8 | 0 | miss | Mem[8]
Mem[0] | 
Mem[6] | 

## Slide 11: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0]
8 | 0 | miss
Mem[8] | 
 | Mem[0]
0 | 0 | hit | Mem[0] | Mem[8]
6 | 0 | miss | Mem[0]
Mem[6] | 
Mem[6] | 
8 | 0 | miss | Mem[8]

## Slide 12: Associativity Example
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0]
8 |  | miss | Mem[0] | Mem[8]
0 |  | hit | Mem[0] | Mem[8]
6 |  | miss | Mem[0] | Mem[8] | Mem[6]
8 |  | hit | Mem[0] | Mem[8] | Mem[6]

## Slide 13: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 14: Implementation of Caches
Set Associative Caches

## Slide 15: Direct-Mapped Cache
Tag
Data Block
V
=
Block Offset
Tag
Index
t
s
b
t
HIT
Data Word or Byte
2s
lines
Notes: To compute the latency of accesses to a cache architecture, apply a constant time-delay for each block, and then compute the total time to access one data-block.
Max( 20ps (for HIT) 20ps (for Data Word Read) ) = 20ps
Hardware blocks involved in the data read (other than the cache structure)
1 XOR, 1 AND, 1 4x1 MUX

## Slide 16: 2-Way Set-Associative Cache
Tag
Data Block
V
=
Block Offset
Tag
Index
t
s
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t
Notes: Compare latency to direct mapped case?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
2 XOR, 2 AND, 2 TS Buffer, 1 4x1 MUX + 1 OR

## Slide 17: Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t
Notes: Compare latency to a 2-way set-associative and fully associative cache ?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
n XOR, n AND, n TS Buffer, 1 4x1 MUX + 1 OR (n = number of cache blocks)

## Slide 18
Enter the data that was retrieved from the memory address – 0x7121C5 and 0xE5ADBA
Assignments 1
How many lines are contained in this cache?
How many blocks are contained in the memory space ?

## Slide 19
Tag (binary) | Set ID (binary) | Word within block |  |  | 
 |  | 00 | 01 | 10 | 11
10100001001001 | 01101101 | 0x00 | 0x61 | 0xC2 | 0x23
11100001100100 | 01101101 | 0x10 | 0x71 | 0xD2 | 0x33
11001011010110 | 01101110 | 0x20 | 0x81 | 0xE2 | 0x43
11100101101011 | 01101110 | 0x30 | 0x91 | 0xF2 | 0x53
11110110110100 | 01101111 | 0x40 | 0xA1 | 0x02 | 0x63
10100111010101 | 01101111 | 0x50 | 0xB1 | 0x12 | 0x73
10101010111110 | 01110000 | 0x84 | 0xE5 | 0x46 | 0xA7
10101010010011 | 01110000 | 0x94 | 0xF5 | 0x56 | 0xB7
01110001001000 | 01110001 | 0xA4 | 0xA5 | 0x66 | 0xC7
00001101101101 | 01110001 | 0xB4 | 0x15 | 0x76 | 0xD7
01011010010010 | 01110010 | 0xC4 | 0x25 | 0x86 | 0xE7
10101111001011 | 01110010 | 0xD4 | 0x35 | 0x96 | 0xF7

## Slide 20: 2 way set associative cache
Set ID # | Tag Array (binary) | Data stored in the cache blocks (hex) |  |  | 
 |  | 11 11-10-01-00 | 10 11-10-01-00 | 01 11-10-01-00 | 00 11-10-01-00
… | … | … | … | … | …
102 | 0101 0001 1111 1101 1010 | 10 67 E2 F1 | 71 D3 45 A2 | D2 66 C4 33 | 33 44 6A 65
 | 0101 0000 1110 1101 1010 | 20 56 A1 B3 | 81 43 87 A3 | E2 57 9A 11 | 43 A2 F4 E1
103 | 0101 0000 1110 1001 1010 | F2 B1 C3 11 | 91 B2 45 78 | F2 A2 B3 11 | 53 B3 F2 E1
 | 0101 0001 1110 1101 1010 | 40 70 89 A2 | A1 B3 E3 11 | 02 A2 B3 76 | 63 56 79 96
104 | 0001 0001 1110 1101 1010 | 50 98 08 A2 | 56 78 98 23 | 12 D3 E1 F2 | 73 66 88 99
 | 0100 0001 1110 1101 1010 | 84 66 55 33 | E5 11 44 67 | 46 A2 B2 88 | 67 B3 F3 11
105 | 0101 0001 1010 1101 1010 | 94 A3 B4 12 | F5 34 45 67 | B1 C3 F2 11 | B7 14 C2 23
 | 0101 0001 0110 1101 1010 | A4 B3 74 34 | A5 B3 C4 34 | 66 E4 F2 34 | C7 19 A3 11
106 | 0101 0101 1110 1101 1010 | B4 B2 45 11 | 15 98 65 4A | 76 78 98 54 | 67 19 B4 12
 | 0101 1001 1110 1101 1010 | C4 C3 12 11 | 25 35 29 19 | 86 97 A3 A4 | E7 43 C4 17
… | … | … | … | … | …

## Slide 21
The diagram shows a part of the 2-way set associative cache. Notice that the set ID values start from 102, and increment every other set in the cache. The corresponding snapshot of the “Tag Array” is also given. For this cache configuration, tag is 20 bits, set ID is 8 bits, 4 words per block and each word is 4 bytes.
Note: The ordering/position of the byte/words in the cache-block are indicated.
Suppose the processor executes a Load-Byte instruction from the address 0x51EDA677.
What is the SetID, where the data will be searched?
Write the block offset and byte offset for the address
Which word in the cache block is requested by the processor?
What is the data value (byte) that is returned to the processor?
What is the address in hexa if the SetID = 103, Tag value = 0101 0001 1110 1101 1010, and the byte data returned is 0x02
Questions
Notes: 106 (0x51EDA6A7 = 0101 0001 1110 1101 1010 0110 1010 0111 binary and 01101010 = 2+8+32+64)
01 and 0111 or 11
01
86

## Slide 22
Draw a Direct-mapped Cache architecture for 64 KB size with 1024 Blocks
Assignments 2
Draw a 2-way Set Associate Cache architecture for the same size above
Draw a Fully Associative Cache architecture for the same size above

## Slide 23: Direct-Mapped Cache (64 KB, 1024 Blocks)
Block Size = 64 Bytes
Assume 32 bit address
Tag
Data Block
V
16x1
=
Offset
Tag
Index
t=16
if addr.
is 32 bit
long
s=10
b=6 (or 4 for word)
t
HIT
Data Word (Byte?64x1Mux)
210
=1024
lines
0
…
1023
Notes: To compute the latency of accesses to a cache architecture, apply a constant time-delay for each block, and then compute the total time to access one data-block.
Max( 20ps (for HIT) 20ps (for Data Word Read) ) = 20ps
Hardware blocks involved in the data read (other than the cache structure)
1 XOR, 1 AND, 1 4x1 MUX

## Slide 24: 2-Way Set-Associative Cache(64KB,1024 blks)
Tag
Data Block
V
=
Offset
Tag
Index
t
=
17
s=9
b=6
HIT
Tag
Data Block
V
64x1
Data Byte
(Word?16x1 Mux)
=
t=17
Assume 32 bit address
Block Size = 64 Bytes, Number of Sets = 512
512 bits
64 B
64 byte
0
…
511
Notes: Compare latency to direct mapped case?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
2 XOR, 2 AND, 2 TS Buffer, 1 4x1 MUX + 1 OR

## Slide 25: 4-Way Set-Associative Cache(64KB,1024 blks)
Tag
Block
V
=
Offset
Tag
Index
t
=
18
s=8
b=6
HIT
64x1
Data Byte
(Word?16x1 Mux)
=
t=18
Assume 32 bit address
Block Size = 64 Bytes, Number of Sets = 256
512
0
…
255
Tag
Block
=
Tag
Block
=
V
V
Notes: Compare latency to direct mapped case?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
2 XOR, 2 AND, 2 TS Buffer, 1 4x1 MUX + 1 OR

## Slide 26: 16-Way Set-Associative Cache(64KB,1024 blks)
Tag
Block
V
=
Offset
Tag
Index
t
=
20
s=6
b=6
HIT
64x1
Data Byte
(Word?16x1 Mux)
=
20
Assume 32 bit address
Block Size = 64 Bytes, Number of Sets = 64
512
0
…
63
Tag
Block
=
Tag
Block
16 blocks/set
16 comparators
and etc.
Notes: Compare latency to direct mapped case?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
2 XOR, 2 AND, 2 TS Buffer, 1 4x1 MUX + 1 OR

## Slide 27: Fully Associative Cache(64KB,1024 blks)
Tag
Block
V
=
Offset
Tag
t=26
b=6
HIT
64x1
Data Byte
(Word?16x1 Mux)
=
26
Assume 32 bit address
Block Size = 64 Bytes, Number of Sets = 1
512
Tag
Block
=
Tag
Block
1024 blocks
1024 comparators
and etc.
V
V
Notes: Compare latency to direct mapped case?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
2 XOR, 2 AND, 2 TS Buffer, 1 4x1 MUX + 1 OR

## Slide 28: Fully Associative Cache (Alt View)
Tag
Data Block
V
=
Block
Offset
Tag
t=26
b=6
HIT
Data
Word
or Byte
=
=
t=26
Assume 32 bit address
Assume 32 bit address
Block Size = 64 Bytes, Number of Sets = 1
Notes: Compare latency to a 2-way set-associative and fully associative cache ?
- Max (30ps (for HIT), 20ps (for Data Word read)) = 30ps
Hardware blocks involved in the data read (other than the cache structure)
n XOR, n AND, n TS Buffer, 1 4x1 MUX + 1 OR (n = number of cache blocks)

## Slide 29
Do caches fall into 3 categorizations?
Indeed, are they are set associative caches?
Can a cache block only go in one spot in the direct-mapped cache? Is it easy to find a block, but isn’t it flexible?
Can a cache block go in any spot in fully associative cache? No index bits?
When set associativity increases (higher n-way) under the fixed address,
  do we need fewer sets, and thus fewer index bits?
  And do we have larger tags?
  What about block offsets?
  More comparators?
  More expensive in terms of the cost and performance?
  More flexible in terms of block placements?
Cache Questions

## Slide 30
Set Associativity – Fully Associative Caches vs. N-way Set-Associative Caches
Summary
Cache Implementation – Set-Associative Caches vs. Direct-mapped Caches
Next: Cache Parameters