## Slide 1: Lecture 8 Set Associative Caches Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module3

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
  Bypasses
  Branch Prediction
  Out-of-order Scheduling
Memory Hierarchy
  Direct-mapped Cache
  Set-associative Cache
  Cache Parameters
  Virtual Memory
Input
Output
Interface
Computer
Datapath
Processor
Memory
Control
Compiler

## Slide 3
Agenda
Cache Parameters
Cache Misses
Multi-level Caches

## Slide 4: Cache Parameters
Set Associative Caches

## Slide 5
Cache Size
Block Size
Set Associativity
Replacement Policy
Cache Write Policy
Etc.
Cache Parameters

## Slide 6: Replacement Policy
In an associative cache, which block from a set should be evicted when the set becomes full?
Random
Least Recently Used (LRU)
  LRU cache state must be updated on every access
  true implementation only feasible for small sets (2-way)
  pseudo-LRU binary tree often used for 4-8 way
First In, First Out (FIFO) a.k.a. Round-Robin
  used in highly associative caches
Not Least Recently Used (NLRU)
  FIFO with exception for most recently used block or blocks
This is a second-order effect. Why?
Replacement only happens on cache-misses
Notes: NLRU used in Alpha TLBs (jse)

## Slide 7: Block Size and Spatial Locality
Block is unit of transfer between the cache and memory
Larger block size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing block size?
Word3
Word0
Word1
Word2
block address offsetb
2b = block size a.k.a line size (in bytes)
Split CPU address
b bits
32 – b bits
Tag
4 word block, b=2
Fewer blocks => more conflicts. Can waste bandwidth.
Notes: Larger block size will reduce compulsory misses (first miss to a block).
Larger blocks may increase conflict misses since the number of blocks
is smaller.

## Slide 8: Improving Cache Performance
Average memory access time =
  Hit time + Miss rate x Miss penalty
To improve performance:
  reduce the hit time
  reduce the miss rate
  reduce the miss penalty
What is the simplest design strategy?
Biggest cache that doesn’t increase hit time past 1-2 cycles (approx 8-32KB in modern technology)
[ design issues more complex with out-of-order superscalar processors ]
Notes: Design the largest primary cache without slowing down the clock
Or adding pipeline stages.

## Slide 9: Cache Misses
Set Associative Caches

## Slide 10: Causes for Cache Misses
Compulsory: first-reference to a block a.k.a. cold start misses
  misses that would occur even with infinite cache
Capacity: cache is too small to hold all data needed by the program
  misses that would occur even under perfect replacement policy
Conflict: misses that occur because of collisions due to block-placement strategy
  misses that would not occur with full associativity

## Slide 11: Cache Miss Types
When observed from the perspective of the program, and its data accesses:
  Compulsory cache-misses
  Capacity cache-misses
  Conflict cache-misses
for(i: 0 ~ 19)
A[i] = const;
W0
W1
W2
W3
Blk-0
Blk-1
Blk-2
Blk-3
5 Comp. CM
for(j: 0 ~ 1)
for(i: 0 ~ 19)
A[i] = const;
5 Capacity CM
5 Blocks
Reused
for(i: 0 ~ 19)
A[i] = B[i];
6 Words
Reused
When Arrays A[20] and B[20] are directly
mapped to the same cache-block boundary.
5x6 Conflict CM

## Slide 12: Effect of Cache Parameters on Performance
Larger cache size
  reduces capacity and conflict misses
  hit time will increase
Higher associativity
  reduces conflict misses
  may increase hit time
Larger block size
  reduces compulsory and capacity (reload) misses
  increases conflict misses and miss penalty
Notes: Requested block first….
The following could be in the slide…
spatial locality reduces compulsory misses and capacity reload misses
  fewer blocks may increase conflict miss rate
  larger blocks may increase miss penalty

## Slide 13: Write Policy Choices
Cache hit:
  write through : write both cache & memory
    generally higher traffic but simplifies cache coherence
  write back : write cache only (memory is written only when the entry is evicted)
    a dirty bit per block can further reduce the traffic
Cache miss:
  no write allocate : only write to main memory
  write allocate (aka fetch on write) : fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 14: Multi-level Caches
Set Associative Caches

## Slide 15: Multilevel Caches
A memory cannot be large and fast
Increasing sizes of cache at each level
CPU
L1$
L2$
DRAM
Local miss rate = misses in cache / accesses to cache
Global miss rate = misses in cache / CPU memory accesses
Misses per instruction = misses in cache / number of instructions
Notes: MPI makes it easier to compute overall performance (jse)

## Slide 16: A Typical Memory Hierarchy
L1 Data Cache
L1 Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory
Multiported register file (part of CPU)
Split instruction & data primary caches
(on-chip SRAM)
Multiple interleaved memory banks
(off-chip DRAM)
Large unified
secondary cache
(on-chip SRAM)
CPU
Notes: Implementation close to the CPU looks like a Harvard machine…(jse)

## Slide 17: Presence of L2 influences L1 design
Use smaller L1 if there is also L2
  Trade increased L1 miss rate for reduced L1 hit time and reduced L1 miss penalty
  Reduces average access energy
Use simpler write-through L1 with on-chip L2
  Write-back L2 cache absorbs write traffic, doesn’t go off-chip
  At most one L1 miss request per L1 access (no dirty victim write back) simplifies pipeline control
  Simplifies coherence issues
  Simplifies error recovery in L1 (can use just parity bits in L1 and reload from L2 when parity error detected on L1 read)

## Slide 18: Inclusion Policy
Inclusive multilevel cache:
  Inner cache holds copies of data in outer cache
  External access needs to only check the outer cache
  Most common case
Exclusive multilevel caches:
  Inner cache may hold data not in outer cache
  Swap lines between inner/outer caches on miss
  Used in AMD Athlon with 64KB primary and 256KB secondary cache
Why choose one type or the other?
Notes: New slide (jse)

## Slide 19: Key Cache Design Parameters
 | L1 typical | L2 typical
Total size (blocks) | 250 to 2000 | 4000 to 250,000
Total size (KB) | 16 to 64 | 500 to 8000
Block size (B) | 32 to 64 | 32 to 128
Miss penalty (clocks) | 10 to 25 | 100 to 1000
Miss rates (global for L2) | 2% to 5% | 0.1% to 2%
Notes: A trace cache finds a dynamic sequence of instructions including taken branches to load into a cache block. Thus, the cache blocks contain dynamic traces of the executed instructions as determined by the CPU rather than static sequences of instructions as determined by memory layout. It folds branch prediction into the cache.

## Slide 20: Two Machines’ Cache Parameters
 | Intel P4 | AMD Opteron
L1 organization | Split I$ and D$ | Split I$ and D$
L1 cache size | 8KB for D$, 96KB for trace cache (~I$) | 64KB for each of I$ and D$
L1 block size | 64 bytes | 64 bytes
L1 associativity | 4-way set assoc. | 2-way set assoc.
L1 replacement | ~ LRU | LRU
L1 write policy | write-through | write-back
L2 organization | Unified | Unified
L2 cache size | 512KB | 1024KB (1MB)
L2 block size | 128 bytes | 64 bytes
L2 associativity | 8-way set assoc. | 16-way set assoc.
L2 replacement | ~LRU | ~LRU
L2 write policy | write-back | write-back
Notes: A trace cache finds a dynamic sequence of instructions including taken branches to load into a cache block. Thus, the cache blocks contain dynamic traces of the executed instructions as determined by the CPU rather than static sequences of instructions as determined by memory layout. It folds branch prediction into the cache.

## Slide 21
Think about optimization techniques to improve cache performance by adjusting cache parameters or enhancing cache architectures
For a 2-way set associative cache of size 16KB and block size 32B = 8 words, what are the total number of misses at the end of 9th iteration (at i=0, j=1 and k=0), with FIFO replacement policy? (Note: Total misses are the sum of all the misses incurred)
What about the end of 17th and 65th iterations?
Assignments
#define N 8
int a[N][N], b[N][N], c[N][N];
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
c[i][j] = a[i][k] * b[k][j];

## Slide 22
Assignments
#define N 8
int a[N][N], b[N][N], c[N][N];
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
c[i][j] = a[i][k] * b[k][j];

## Slide 23
Assume the cache is initially empty. Access pattern of data elements is from right to left of the code and “int” is one word (4 bytes). Also assume that these three int arrays are located consecutively in the memory.
For a fully associative cache with infinite size, block size 32B = 8 words and ideal replacement policy, what is the number of compulsory misses?
For a fully associative cache with infinite size, block size 16B = 4 words and ideal replacement policy, what is the number of compulsory misses?
For a fully associative cache of size 256B and block size 32B = 8 words, with LRU replacement policy, what is the number of compulsory misses at the end of 16th iteration (after i=0; j=1; k=7)?
For a fully associative cache of size 256B and block size 32B = 8 words, with LRU replacement policy, what is the number of capacity misses at the end of 16th iteration (after i=0; j=1; k=7)?
Questions
Notes: 24 (8 blocks for each array a, b, c)
48 (16 blocks for each array a, b, c)
10 compulsory misses (10 blocks such as B0,…,B7,A0,C0 from access patterns [B0,A0,C0, …, B7,A0,C0]^2 will be used where Bn=b[n][0]~b[n][7])
8 capacity misses (from the 9th iteration, i.e., after the first references to the arrays, B0~B7 will be located where B2, B3, B4, B5, B6, B7, B0, B1, B2, and B3 were located in the cache due to the small size of caches, i.e., 8 blocks allowed)

## Slide 24
Assume the cache is initially empty. Access pattern of data elements is from right to left of the code and “int” is one word (4 bytes). Also assume that these three int arrays are located consecutively in the memory.
For a 2-way set associative cache of size 16KB and block size 32B = 8 words, what are the total number of misses at the end of 9th iteration (at i=0, j=1 and k=0), with FIFO replacement policy? (Note: Total misses are the sum of all the misses incurred)
What about the end of 17th and 65th iterations?
Questions
Notes: 5) 10 (no conflict miss since all blocks will be assigned to different sets and no capacity miss since the cache is of 512 blocks large enough)
6) 12 compulsory misses (since 2 arrays such as A1 and C1 need to be incoming into cache)

## Slide 25
Cache Parameters
Summary
Cache Misses and Optimizations
Next: Virtual Memory