## Slide 1: Lecture 10 Out-of-order Execution Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module4

## Slide 2
Agenda
Dynamic Scheduling
Out-of-order Execution

## Slide 3: Dynamic Scheduling
Virtual Memory

## Slide 4: Can HW get CPI closer to 1?
Why dynamic scheduling in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea #1: Allow instructions behind stall to proceed DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14

## Slide 5: Can HW get CPI closer to 1?
Why dynamic scheduling in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea #1: Allow instructions behind stall to proceed DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14 Out-of-order execution  out-of-order completion?

## Slide 6: Can HW get CPI closer to 1?
Why dynamic scheduling in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea #1: Allow instructions behind stall to proceed
Key idea #2: Register Renaming DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F0,F8,F14 MULD F6,F10,F0

## Slide 7: Can HW get CPI closer to 1?
Why dynamic scheduling in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea #1: Allow instructions behind stall to proceed
Key idea #2: Register Renaming DIVD F0,F2,F4 DIVD F0,F2,F4 ADDD F10,F0,F8 ADDD F10,F0,F8 SUBD F0,F8,F14 SUBD F100,F8,F14 MULD F6,F10,F0 MULD F6,F10,F100 Totally removes WAR and WAW hazards.
WAR: Write After Read data hazard
WAW: Write After Write data hazard

## Slide 8: Dynamic scheduling
Hardware re-arranges the instruction execution to reduce the stalls while maintaining data flow in the pipeline.
  Compatibility
  Dependence information may not be known at compile time (e.g. dynamic linking)
  Tolerance for “un-predictable” delay (e.g. long-latency cache misses)

## Slide 9: Out-of-order Execution
Virtual Memory

## Slide 10: In-order instruction issue and execution
DIV.D F0, F2, F4
ADD.D F10, F0, F8
SUB.D F12, F8, F14
In the classic 5-stage pipeline, when are structural and data hazards checked and known?

## Slide 11: In-order instruction issue and execution
DIV.D F0, F2, F4
ADD.D F10, F0, F8
SUB.D F12, F8, F14
In the classic 5-stage pipeline, when are structural and data hazards checked and known?
After ID stage  all data hazards have been resolved

## Slide 12: Out-of-order (OOO) execution
We want an instruction to begin execution as soon as its data operands are available!
  Potential WAR and WAW hazards
DIV.D F0, F2, F4
ADD.D F6, F0, F8
SUB.D F8, F10, F14
MUL.D F6, F10, F8
WAR (anti-dependence)
DIV.D F0, F2, F4
ADD.D F6, F0, F8
SUB.D F8, F10, F14
MUL.D F6, F10, F8
WAW (output-dependence)

## Slide 13: Moving beyond the five-stage pipeline
Why limit performance for slow/less frequent ops?
  Variable latencies/out-of-order execution desirable
How do we prevent WAR and WAW hazards?
How do we deal with variable latency?
  Forwarding for RAW hazards harder.

## Slide 14: Moving beyond the five-stage pipeline
RAW
WAR

## Slide 15: Out-of-order (OOO) execution
Split the ID pipe stage
  Issue – Decode instructions, check for structural hazard
  Read operands – Wait until no data hazards, then read operands
All instructions are issued in-order, but executed out-of-order.

## Slide 16
What is the main advantage of dynamic scheduling?
Why don’t you compose WAR and WAW data hazards?
Assignments

## Slide 17
Dynamic Scheduling
Summary
In-order Issue, Out-of-order Execution
Next: Register Scoreboarding