## Slide 1: Lecture 11 Register Scoreboarding Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module4

## Slide 2
Agenda
Scoreboarding
Scoreboard Architecture

## Slide 3: Scoreboarding
Out-of-Order Execution

## Slide 4: OoO execution
Scoreboarding
  Allowing instructions to execute OoO when there are sufficient resources and no data dependences
    Handles WAR hazards
Tomasulo algorithm
    Handles WAR and WAW hazards
    Handles speculations

## Slide 5: Scoreboard: a bookkeeping technique
Scoreboards date to CDC6600 in 1963
Instructions execute if not dependent on previous instructions and no hazards
CDC 6600: In order issue, out-of-order execution, out-of-order commit (or completion)
  No forwarding!
  Imprecise interrupt/
  exception model for now
Baseball Scoreboard

## Slide 6: Scoreboard Architecture
Out-of-Order Execution

## Slide 7: Scoreboard Architecture (CDC 6600)
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 8: Scoreboard Implications
Solutions for WAR:
  Stall writeback until registers have been read
  Read registers only during Read Operands stage
Solution for WAW:
  Detect hazard and stall issue of new instruction until other instruction completes
No register renaming! (Introduced in Tomasulo)
Need to have multiple instructions in execution phase  multiple execution units or pipelined execution units
Scoreboard keeps track of dependencies between instructions that have already issued
Scoreboard replaces ID, EX, WB with 4 stages

## Slide 9: Four Stages of Scoreboard Control
Issue—decode instructions & check for structural hazards (ID1)
  Instructions issued in program order (for hazard checking)
  Don’t issue if structural hazard
  Don’t issue if instruction is output dependent on any previously issued but uncompleted instruction (no WAW hazards)
Read operands—wait until no data hazards, then read operands (ID2)
  All real dependencies (RAW hazards) resolved in this stage, since we wait for instructions to write back data.
  No forwarding of data in this model!

## Slide 10: Four Stages of Scoreboard Control
Execution—operate on operands (EX)
  The functional unit begins execution upon receiving operands
  When the result is ready, it notifies the scoreboard that it has completed execution
Write result—finish execution (WB)
  Stall until no WAR hazards with previous instructions: Example: DIVD F0, F2, F4 ADDD F10, F0, F8 SUBD F8, F8, F14 CDC 6600 scoreboard would stall SUBD until ADDD reads operands

## Slide 11: Three Parts of the Scoreboard
Instruction status: Which of 4 steps the instruction is in
Functional unit status: Indicates the state of the functional unit (FU). 9 fields for each functional unit
  Busy: Indicates whether the unit is busy or not
  Op: Operation to perform in the unit (e.g., + or –)
  Fi: Destination register
  Fj,Fk: Source-register numbers
  Qj,Qk: Functional units producing source registers Fj, Fk
  Rj,Rk: Flags indicating when Fj, Fk are ready
Register result status: Indicates which functional unit will write each register, if one exists. Blank when no pending instructions will write that register
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 12
Out-of-Order Execution: Scoreboarding and Tomasulo Algorithm
Summary
Scoreboard Architecture: handle Structural Hazards and WAR Hazards
Next: Scoreboard Example