## Slide 1: Lecture 12 Tomasulo Algorithm Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module4

## Slide 2
Agenda
Data Dependence and Dynamic Scheduling
Register Renaming
Tomasulo Algorithm

## Slide 3: Data Dependence & Dynamic Scheduling
Out-of-Order Execution

## Slide 4: Data Dependence and Hazards
Dependences are a property of programs
Presence of dependence indicates potential for a hazard, but actual hazard and length of any stall is a property of the pipeline
Importance of the data dependencies
  indicates the possibility of a hazard
  determines order in which results must be calculated
  sets an upper bound on how much parallelism can possibly be exploited
Looking at HW schemes to avoid hazard

## Slide 5: Advantages of Dynamic Scheduling
Handles cases when dependences unknown at compile time
  e.g., because they may involve a memory reference
It simplifies the compiler
Allows code that compiled for one pipeline to run efficiently on a different pipeline
Hardware speculation, a technique with significant performance advantages, that builds on dynamic scheduling

## Slide 6: HW Schemes: Instruction Parallelism
Key idea: Allow instructions behind to proceed DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14
Enables out-of-order execution and allows out-of-order completion
Will distinguish when an instruction begins execution and when it completes execution;
  In between the 2 times, the instruction is in execution
In a dynamically scheduled pipeline, all instructions pass through issue stage in order (in-order issue)

## Slide 7: Dynamic Scheduling Step 1
Simple pipeline had 1 stage to check both structural and data hazards: Instruction Decode (ID), also called Instruction Issue
Split the ID pipe stage of simple 5-stage pipeline into 2 stages:
Issue—Decode instructions, check for structural hazards
Read operands—Wait until no data hazards, then read operands

## Slide 8: Scoreboard recap
Limitations
  No forwarding
  Small number of functional units
    Instructions using the same FU cannot proceed (structural hazard)
  Wait for WAR hazards
  Prevent WAW hazards in ID

## Slide 9: Another dynamic algorithm – Tomasulo
For IBM 360/91 about 3 years after CDC6600
Difference between IBM360 & CDC6600 ISAs
  IBM has only 2 register specifiers/instruction vs. 3 in CDC6600
  IBM has 4 FP registers vs. 8 in CDC6600
  Implications?

## Slide 10: Difference b/w Tomasulo & Scoreboarding
Control & buffers distributed with FU vs. centralized in scoreboard
Registers in instructions replaced by pointers to reservation station buffer
  Scoreboard  registers primary operand storage
  Tomasulo  reservation stations as operand storage
HW renaming to avoid WAR & WAW hazards
  Scoreboard  both source registers read together (thus cannot be overwritten while we wait for the other)
  Tomasulo  each register read as soon as possible
Common Data Bus (CDB) broadcasts results to all FUs
Load Store Queue (LSQ)

## Slide 11: Tomasulo’s Algorithm
For IBM 360/91 (before caches!)
Goal: High Performance without special compilers
Small number of floating point registers (4 in 360) prevented interesting compiler scheduling of operations
  This led Tomasulo to try to figure out how to get more effective register-renaming in hardware!
Why study 1966’s computer?
The descendants of this have flourished!
  Alpha 21264, HP 8000, MIPS 10000, Pentium III, PowerPC 604, …

## Slide 12: Register Renaming
Out-of-Order Execution

## Slide 13: Eliminating data hazards
RAW hazard
  Avoided by executing an instruction only when its operands are available (same as Scoreboard)
WAW & WAR hazards
  Avoided by using register renaming
    Renaming all destination registers, including those with a pending read or write from an easier instruction

## Slide 14: Register renaming concept
DIV F0, F2, F4
ADD F6, F0, F8
Store F6, 0(R1)
SUB F8, F10, F14
MUL F6, F10, F8

## Slide 15: Register renaming concept
DIV F0, F2, F4
ADD F6, F0, F8
Store F6, 0(R1)
SUB F8, F10, F14
MUL F6, F10, F8
WAR
WAW
WAR

## Slide 16: Register renaming concept
DIV F0, F2, F4
ADD S, F0, F8
Store S, 0(R1)
SUB T, F10, F14
MUL F6, F10, T
WAR
WAW
WAR

## Slide 17: Register renaming concept
DIV F0, F2, F4
ADD S, F0, F8
Store S, 0(R1)
SUB T, F10, F14
MUL F6, F10, T
WAR
WAW
WAR
The renaming process can be done by compiler analysis; however, finding the use of F8 (or T) in the later code segment is challenging, esp. when there is interleaving branches!

## Slide 18: Tomasulo Algorithm
Out-of-Order Execution

## Slide 19: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”
Registers in instructions replaced by values or pointers to reservation stations (RS);
  A form of register renaming ;
  Avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations that compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as well

## Slide 20: Tomasulo organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
Reservation
Stations
Common Data Bus (CDB)
To Mem
Load Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Instruction
FP Op
Queue
FP Registers
Store
Buffers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 21: Reservation Station Components
Op Operation to perform in the unit (e.g., + or –)
Vj, Vk Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0  ready
  Store buffers only have Qi for RS producing result
Busy Indicates reservation station or FU is busy
A Address information for a load/store. Initially holding the imm field; later, holding the effective addr.
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.

## Slide 22: Three Stages of Tomasulo Algorithm
1.Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2.Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3.Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available

## Slide 23: Three Stages of Tomasulo Algorithm
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed: Load (2 cc), Adder (2 cc), Mult (10 cc), Div (40 cc)

## Slide 24
Dynamic Scheduling – Tomasulo Algorithm vs. Register Scoreboarding
Summary
Tomasulo Organization and Components
Next: Tomasulo Example