## Slide 1: Lecture 13 Superscalar Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module5

## Slide 2: Where are we and where to?
Assembly Language
Simple Processor Design
Pipelined Processor
Memory Hierarchy
Out-of-Order Execution
  Register Scoreboarding
  Register Renaming
Superscalar
Multithreading
Manycores
Accelerators

## Slide 3
Agenda
Superscalar Organization
(Recall) Dependency
Out-of-order Completion
Register Renaming
Branch Prediction

## Slide 4: Superscalar Organization
Superscalar Machine

## Slide 5: What is Superscalar?
A Superscalar machine executes multiple independent instructions in parallel
They are pipelined as well.
  “Common” instructions (arithmetic, load/store, conditional branch) can be executed independently
  Equally applicable to RISC & CISC, but more straightforward in RISC machines
  The order of execution is usually assisted by the compiler

## Slide 6: Example of Superscalar Organization
2 Integer ALU pipelines,
2 FP ALU pipelines,
1 memory pipeline
Integer Register File
Pipelined functional units
Floating Point Register File
Memory

## Slide 7: Superscalar vs. Superpipelined
Successive instructions
Superscalar
Superpipelined
Base machine
Key:
Ifetch
Decode
Execute
Write
Time in base cycle

## Slide 8: (Recall) Dependency
Superscalar Machine

## Slide 9: (Recall)True Data Dependency(Must W before R)
ADD r1, r2 r1+r2  r1
MOVE r3, r1 r1  r3
Can fetch and decode second instruction in parallel with first
LOAD r1, X X(memory)  r1
MOVE r3, r1 r1 r3
Can NOT execute second instruction until first is finished
  Second instruction is dependent on first (R after W)
True Dependency
= Data Dependency
= RAW Dependency

## Slide 10: (Recall) Antidependancy (Must R before W)
ADD R4, R3, 1 R3 + 1  R4
ADD R3, R5, 1 R5 + 1  R3
Cannot complete the second instruction before the first has read R3
ADD R4, R3, 1 R3 + 1  R4
ADD R4, R5, 1 R5 + 1  R4
Cannot complete the second write before the first write to R4
Anti-Dependency
= WAR Dependency
Output Dependency
= WAW Dependency

## Slide 11: (Recall) Control Dependency
Cannot execute instructions after a branch
in parallel with instructions before a branch, because….?
Note: Also, if instruction length is not fixed, instructions have to be decoded to find out how many fetches are needed

## Slide 12: (Recall) Resource Conflict
Two or more instructions requiring access to the same resource at the same time
  e.g. two arithmetic instructions need the ALU
Solution - Can possibly duplicate resources
  e.g. have two arithmetic units

## Slide 13: Effect of Dependencies on Superscalar Operation
Notes:
Superscalar operation is double impacted by a stall
2) CISC machines typically have different length instructions and need to be at least partially decoded before the next can be fetched – not good for superscalar operation
Ifetch
Decode
Execute
Write
i0
i1
i0
i1
i0
i1/branch
i2
i3
i4
i5
i0
i1
No Dependency
Data Dependency (i1 uses data computed by i0)
Procedural Dependency
0 1 2 3 4 5 6 7 8 Time in base cycles
Resource conflict
(i0 and i1 use the same functional unit)

## Slide 14: Instruction-level Parallelism – degree of
Consider:
LOAD R1, R2
ADD R3, 1
ADD R4, R2
  These can be handled in parallel
Consider:
ADD R3, 1
ADD R4, R3
STO (R4), R0
  These cannot be handled in parallel
The “degree” of instruction-level parallelism is determined by the number of instructions that can be executed in parallel without stalling for dependencies

## Slide 15: Out-of-order Completion
Superscalar Machine

## Slide 16: Instruction Issue Policies
Order in which instructions are fetched
Order in which instructions are executed
Order in which instructions update registers and memory values (order of completion)

## Slide 17: In-Order Issue / In-Order Completion (e.g.)
Assume:
I1 requires 2 cycles to execute
I3 & I4 conflict for the same functional unit
I5 depends upon value produced by I4
I5 & I6 conflict for a functional unit
I1 | I2
I3 | I4
I3 | I4
 | I4
I5 | I6
 | I6
I1 | I2
I3 | I4
I5 | I6
I1 | I2 | 
I1 |  | 
 |  | I3
 |  | I4
 | I5 | 
 | I6 | 
1
2
3
4
5
6
7
8
Cycle
Decode
Execute
Write

## Slide 18: In-Order Issue / Out-of-Order Completion (e.g.)
How does this effect interrupts?
I1 | I2
I3 | I4
 | I4
I5 | I6
 | I6
I2 | 
I1 | I3
I4 | 
I5 | 
I6 | 
I1 | I2 | 
I1 |  | I3
 |  | I4
 | I5 | 
 | I6 | 
1
2
3
4
5
6
7
8
Cycle
Decode
Execute
Write
Again:
I1 requires 2 cycles to execute
I3 & I4 conflict for the same functional unit
I5 depends upon value produced by I4
I5 & I6 conflict for a functional unit

## Slide 19: Register Renaming
Superscalar Machine

## Slide 20: Register Renaming to avoid hazards
Output and antidependencies occur because register contents may not reflect the correct ordering from the program
Can require a pipeline stall
One solution: Allocate Registers dynamically (renaming registers)

## Slide 21: Register Renaming example
Add R3, R3, R5 R3b:=R3a + R5a (I1)
Add R4, R3, 1 R4b:=R3b + 1 (I2)
Add R3, R5, 1 R3c:=R5a + 1 (I3)
Add R7, R3, R4 R7b:=R3c + R4b (I4)
Without “subscript” refers to logical register in instruction
With subscript is hardware register allocated: R3a R3b R3c
Note: R3c avoids: antidependency on I2 output dependency I1

## Slide 22: Speedups of Machine Organizations
Not worth duplication of functional units without register renaming
  Need instruction window large enough (more than 8, probably not more than 32)
Speedup
Speedup
Without renaming
With renaming
Base +Id/st +alu +both
Base +Id/st +alu +both
Window size (construction)
8
16
32

## Slide 23: Branch Prediction
Superscalar Machine

## Slide 24: Branch Prediction in Superscalar Machines
Delayed branch slot not used much
  Multiple instructions need to execute in the delay slot
  This leads to too much complexity in recovery
Branch prediction should be used
  Branch history is very useful

## Slide 25: View of Superscalar Execution
Static Program
Instruction fetch and branch prediction
Instruction
dispatch
Instruction
issue
Instruction
execution
Instruction reorder and commit
Window of execution

## Slide 26: Committing or Retiring Instructions
Results need to be put into order (commit or retire)
Results sometimes must be held in temporary storage until it is certain they can be placed in “permanent” storage.
  either committed or retired/flushed
Temporary storage requires regular clean up – overhead – done in hardware.

## Slide 27: Superscalar Hardware Support
Facilities to simultaneously fetch multiple instructions
Logic to determine true dependencies involving register values and Mechanisms to communicate these values
Mechanisms to initiate multiple instructions in parallel
Resources for parallel execution of multiple instructions
Mechanisms for committing process state in correct order

## Slide 28
Scalar vs. Superscalar vs. Superpipelined
Summary
Dependency, OoO Completion, Register Renaming, Branch Prediction, etc. in Superscalar Machines
Next: SIMD and Vector Processors