## Slide 1: Lecture 13 SIMD, VECTOR and SSE Courtesy of A. Shrivastava (ASU) & Tack-Don Han (Yonsei)
Department of Computer Science
Kyoungwoo Lee
Computer Architecture-Module5

## Slide 2
Agenda
Flynn’s Taxonomy
SIMD/Vector Processors
SSE (Streaming SIMD Extensions) Processors

## Slide 3: Flynn’s Taxonomy
SIMD/Vector/SSE

## Slide 4: Flynn’s Taxonomy
SISD : Single Instruction operates on single data
  Example : Processors like MIPS, Intel Pentium 4, etc.
SIMD : Single Instruction operates on multiple data
  Vector processors
MISD : Multiple instruction operates on single data
  No example as of now
MIMD : Multiple instruction operates on multiple data
  Multicore, Multithreaded processors (Intel Xeon Clovertown)
Inst. Data | Single | Multiple
Single | SISD | SIMD
Multiple | MISD | MIMD

## Slide 5: SIMD and Vector Processors
SIMD/Vector/SSE

## Slide 6: SIMD Advantages & Disadvantages
Advantages:
  Reduces cost over control unit over dozens of executions
  Reduces program memory
    SIMD may need only one copy of the code that is being simultaneously executed, while message passing MIMD may require multiple copies
Disadvantages:
  SIMD is best suited for highly regular memory access
  Best suited for for loops but weak for switch cases

## Slide 7: Scalar vs. Vector Processors
R1
R2
R3
+
VR1
VR2
VR3
+
add R3, R1, R2
add VR3, VR1, VR2
Vector Processor
Scalar Processor

## Slide 8: Vectorizable Loops
Loop in which one iteration is not dependent on the other is vectorizable
Only vectorizable loops can be efficiently executed by vector processors
Example
  for i : 0 - 100 c[i] = ( a[i] + b[i] ) / 10

## Slide 9: Vector Processor Requirements
Load/store of vector values
  Vector Registers
Operate on Vectors of different lengths
  Vector length register or strip-mining
Elements can be stored apart from each other
  Vector Stride Register

## Slide 10: VMIPS Vector architecture

## Slide 11: Vector Processing Example
SIMD/Vector/SSE

## Slide 12: Scalar Example DAXPY
Double precision a times X Plus Y ()
Scalar MIPS code for DAXPY
  L.D F0, a ;load scalar a
  DADDIU R4, Rx, #512 ;last address
  Loop: L.D F2, 0(Rx) ;load X[i]
  MUL.D F2, F2, F0 ;a * X[i]
  L.D F4, 0(Ry) ;load Y[i]
  ADD.D F4, F4, F2 ;a * X[i] + y[i]
  S.D F4, 0(Ry) ;store into Y[i]
  DADDIU Rx, Rx, #8 ;Increment X index
  DADDIU Ry, Ry, #8 ;Increment Y index
  DSUBU R20, R4, Rx ;compute bound
  BNEZ R20, Loop ;loop
Total 576 (64*9) dynamic instructions!

## Slide 13: Vector Example DAXPY
ADDVV.D: add two vectors of doubles
ADDVS.D: add vector to a scalar
LV/SV: vector load and vector store from address
Example: DAXPY
Requires 6 instructions vs. almost 600 for MIPS
  L.D F0,a ; load scalar a
  LV V1,Rx ; load vector X
  MULVS.D V2,V1,F0 ; vector-scalar multiply
  LV V3,Ry ; load vector Y
  ADDVV V4,V2,V3 ; add
  SV Ry,V4 ; store the result

## Slide 14: Memory is a PROBLEM!
Vector processor requires highly regular data access by the program
There should a support from memory as well
For a single memory with only one bank, the time taken to load different vector values will be more than the operating on the data
Solution can be memory banking but,
Memory can still become a bottleneck!
  if compute/memory operation balance is not maintained
  Data is not mapped appropriately to the memory banks

## Slide 15: Scatter-Gather
What if data is not stored in a strided manner in the memory?
Use indirect access called Scatter-Gather.
Scatter-Gather operation are often implemented in Hardware to handle sparse matrices
Example (K and M are index vectors that are added to base register to generate the address)
    for (i =o; i<n ; i++) A[K[i]] = A[K[i]] + C[M[i]]

## Slide 16: Scatter-Gather
Use of LVI/SVI instructions : load/store vector indices/gather
  LV Vk, Rk ;load K
  LVI Va, (Ra+Vk) ;load A[K[]]
  LV Vm, Rm ;load M
  LVI Vc, (Rc+Vm) ;load C[M[]]
  ADDVV.D Va, Va, Vc ;Add A[K[]], C[M[]]
  SVI (Ra+Vk), Va ;store A[K[]]

## Slide 17: Streaming SIMD Extensions (SSE)
SIMD/Vector/SSE

## Slide 18: Streaming SIMD Extensions-SSE
Adds eight 128-bit registers
Allows SIMD operations on packed single-precision floating-point numbers
Most SSE instructions require 16-aligned addresses

## Slide 19: SSE features

## Slide 20: SSE features
Add eight 128-bit data registers (XMM registers) in non-64-bit modes; sixteen XMM registers are available in 64-bit mode.
32-bit MXCSR register (control and status)
Add a new data type: 128-bit packed single-precision floating-point (4 FP numbers.)
Instruction to perform SIMD operations on 128-bit packed single-precision FP and additional 64-bit SIMD integer operations.
Instructions that explicitly prefetch data, control data cacheability and ordering of store

## Slide 21: SSE programming environment
XMM0
|
XMM7
MM0
|
MM7
EAX, EBX, ECX, EDX
EBP, ESI, EDI, ESP

## Slide 22
Question) Which of the following code is not vectorizable?
(Note: the code is present inside a for loop)
(1) c[i] =a[i]+(b[i]*100);
(2) c[i] = c[i] + 2*c[i];
(3) c[2*i] = a[i] + b[3*i];
(4) c[i] = a[i-2] + b[i-1]
(5) c[i] = a[i]=b[i]; e[i] = f[i]+d[i];
Assignments

## Slide 23
Flynn’s Taxonomy – SISD, MISD, SIMD, MIMD
Summary
Vector Processing and Streaming SIMD Extension
Next: Multithreading