## Slide 1: CSI3102: Computer Architecture I
MIPS ISA
Recommended Reading :
CAQA, Hennessy & Patterson – Appendix A
COAD, Patterson & Hennessy – Chapter 2
Courtesy of Prof. Aviral Shrivastava in ASU

## Slide 2: What is this?
00100111101111011111111111100000
10101111101111110000000000010100
10101111101001000000000000100000
10101111101001010000000000100100
10101111101000000000000000011000
10101111101000000000000000011100
10001111101011100000000000011100
10001111101110000000000000011000
00000001110011100000000000011001
00100101110010000000000000000001
00101001000000010000000001100101
10101111101010000000000000011100
00000000000000000111100000010010
00000011000011111100100000100001
00010100001000001111111111110111
10101111101110010000000000011000
00111100000001000001000000000000
10001111101001010000000000011000
00001100000100000000000011101100
00100100100001000000010000110000
10001111101111110000000000010100
00100111101111010000000000100000
00000011111000000000000000001000
00000000000000000001000000100001
MIPS machine language code for a routine to compute and print the sum of the squares of integers between 0 and 100.
int main (int argc, char *argv[])
{
  int i;
  int sum = 0;
  for (i = 0; i <= 100; i = i + 1) sum = sum + i * i;
  printf ("The sum from 0 .. 100 is %d\n", sum);
}

## Slide 3: The Instruction Set Architecture (ISA)
instruction set architecture
software
hardware
ISA - The interface description separating the software and hardware.

## Slide 4: High-Level Languages
Higher-level languages
  Allow the programmer to think in a more natural language
    Customized for their intended use, e.g.,
      Fortran for scientific computation
      Cobol for business programming
      Lisp for symbol manipulation
  Improve programmer productivity and maintainability
    more understandable code that is easier to debug and validate
  Independent of
    Computer on which the applications are developed
    Computer on which the applications will execute
Enabler
  Optimizing Compiler Technology
Now very little programming at the assembler level
Notes: For lecture

## Slide 5: Translation from High Level Languages
High-level language program (in C)
swap (int v[], int k)
. . .
Assembly language program (for MIPS)
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Machine (object) code (for MIPS)
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
C - Compiler
Assembler
Notes: For lecture
Computer only understands zeros and ones – instructions of 0’s and 1’s

## Slide 6: Instruction Set Architecture
Syntax and semantics of a list of instructions
Many ISAs
  X86/ia32, ia64, ARM, PowerPC
Quick reference guides available in “Interesting Reads” link in BB
RISC vs. CISC
  Reduced Instruction-Set Computer
  Complex Instruction-Set Computer

## Slide 7: Main Concepts
Instructions are also data
  Encoded in binary and stored in memory
Program Counter
  Points to the location of the instruction to be executed
Fetch instruction from memory location pointed to by the PC
Execute the instruction
Update the PC

## Slide 8: MIPS R4000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
Registers

## Slide 9: Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction specifies exactly three operands
  destination  source1 op source2
All operands are contained in the Register File
  $t0, $s1,$s2 are in Register File

## Slide 10: Program Template
# Title: Filename:
# Author: Date:
# Description:
# Input:
# Output:
################# Data segment #####################
.data
. . .
################# Code segment #####################
.text
.globl main
main: # main program entry
. . .
li $v0, 10 # Exit program
syscall

## Slide 11: .DATA, .TEXT, & .GLOBL Directives
.DATA directive
  Defines the data segment of a program containing data
  The program's variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables
.TEXT directive
  Defines the code segment of a program containing instructions
.GLOBL directive
  Declares a symbol as global
  Global symbols can be referenced from other files
  We use this directive to declare main procedure of a program

## Slide 12: Simple Program (2+3)
# Title: Filename:
# Author: Date:
# Description:
# Input:
# Output:
################# Data segment #####################
.data
. . .
################# Code segment #####################
.text
.globl main
main: # main program entry
ori $8,$0,0x2 # put two's comp. two into register 8
ori $9,$0,0x3 # put two's comp. three into register 9 addu $10,$8,$9 # add register 8 and 9, put result in 10
li $v0, 10 # Exit program
syscall

## Slide 13: Compiling More Complex Statements
What is the assembler equivalent of
  h = (b - c) + d
Assume
  Variable b is stored in register $s1
  Variable c is stored in $s2
  Variable d is stored in $s3
  Result is to be left in $s0
Notes: For lecture
sub $t0, $s1, $s2
add $s0, $t0, $s3

## Slide 14: Compiling More Complex Statements
What is the assembler equivalent of
  h = (b - c) + d
Assume
  Variable b is stored in register $s1
  Variable c is stored in $s2
  Variable d is stored in $s3
  Result is to be left in $s0
sub $t0, $s1, $s2
add $s0, $t0, $s3
## $t0 = b - c
## $s0 = $t0 + d
Notes: For lecture
sub $t0, $s1, $s2
add $s0, $t0, $s3

## Slide 15: MIPS Register File
Register File
  Holds thirty-two 32-bit registers
  Two read ports and
  One write port
  R0 is hardwired to 0
Registers are
  Faster than main memory
  Easier for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order vs. stack
  Can hold variables so that
    code density improves (since register are named with fewer bits than a memory location)
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32
Notes: For lecture
All machines (since 1975) have used general purpose registers
How many bits wide are each of the lines going into/out of the register file?

## Slide 16: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 17: MIPS ALU
32-bit ALU
  2 32-bit sources
  1 32-bit result
Operations
  Arithmetic
    ADD, SUB, ...
  Logical
    AND, OR, NOR, XOR, …
ALU
32-bit
32-bit
32-bit

## Slide 18: How does it work?
sub $t0, $s1, $s2
Register File
src1 reg no
src2 reg no
src1 data
src2 data
$t0  R8
$s1  R17
$s2  R18
R0
R1
R8
25
R17
R18
17
18
10
25
10
-
dst addr
write data
15
8
15
15
R31
25
10
Arithmetic instructions can only change the contents of the Register File
  In CISC processors, arithmetic instructions are much more powerful – they can read and change the contents of the memory

## Slide 19: Accessing Memory
MIPS has two basic data transfer instructions for accessing memory
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
(assume $s3 holds 2410)
The data transfer instruction must specify
  Memory address
    where in memory to read from (load) or write to (store)
  Register destination (source)
    where in the register file to write to (load) or read from (store)
The memory address is formed by
  Adding the constant portion of the instruction and the contents of the second register
28
32
Notes: For lecture
What is the memory address of the given load and store instructions if $s3 contains the address 24?

## Slide 20: View of the Memory
Memory is viewed as a large, single-dimension array, with an address
A memory address is an index into the array
Processor
Memory
? locations
read addr/
write addr
read data
write data
32
32
32
232
? width
Notes: For class handout

## Slide 21: Memory Organization
How wide is the memory
What is each unit
Each unit is a bit
  0, 1
8-bits = 1 byte
  In MIPS memory is byte addressable
  232 locations of 1 byte
Software likes to operate on “words”
  1 word = 4 bytes = 32 bits
  230 locations of 1 word
Memory
Memory
232 Locations
8-bit
32-bit
230 Locations

## Slide 22: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the MIPS assembly code for the C statement
A[8] = A[2] - b
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
Notes: For lecture
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)

## Slide 23: Compiling with Loads and Stores
Assuming variable b is stored in $s2 and that the base address of array A is in $s3, what is the MIPS assembly code for the C statement
A[8] = A[2] - b
$s3
$s3+4
$s3+8
$s3+12
. . .
A[2]
A[3]
. . .
A[1]
A[0]
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)
Notes: For lecture
lw $t0, 8($s3)
sub $t0, $t0, $s2
sw $t0, 32($s3)

## Slide 24: Compiling with a Variable Array Index
Assuming A is an array of 50 elements whose base is in register $s4, and variables b, c, and i are in $s1, $s2, and $s3, respectively, what is the MIPS assembly code for the C statement
c = A[i] - b
add $t1, $s3, $s3 #array index i is in $s3
add $t1, $t1, $t1 #temp reg $t1 holds 4*i
Notes: For lecture
add $t1, $t1, $s4 # addr of A[i]
lw $t0, 0($t1)
sub $s2, $t0, $s1
A natural (first) mistake is to try
lw $t0, $t1($s4)
sub $s2, $t0, $t1

## Slide 25: Compiling with a Variable Array Index
add $t1, $s3, $s3 #array index i is in $s3
add $t1, $t1, $t1 #temp reg $t1 holds 4*i
add $t1, $t1, $s4 #addr of A[i]
lw $t0, 0($t1)
sub $s2, $t0, $s1
Assuming A is an array of 50 elements whose base is in register $s4, and variables b, c, and i are in $s1, $s2, and $s3, respectively, what is the MIPS assembly code for the C statement
c = A[i] - b
Notes: For lecture
add $t1, $t1, $s4 # addr of A[i]
lw $t0, 0($t1)
sub $s2, $t0, $s1
A natural (first) mistake is to try
lw $t0, $t1($s4)
sub $s2, $t0, $t1

## Slide 26: Branch Instructions
Decision making instructions
  alter the control flow of the program
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: bne $s0, $s1, Label #go to Label if $s0$s1 beq $s0, $s1, Label #go to Label if $s0=$s1
Example: if (i==j) h = i + j;
bne $s0, $s1, Lab1 add $s3, $s0, $s1 Lab1: ...

## Slide 27: Unconditional Jumps
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Example: if (i!=j) h=i+j; else h=i-j;
beq $s0, $s1, Lab1 add $s3, $s0, $s1 j Lab2 Lab1: sub $s3, $s0, $s1 Lab2: ...
Notes: If-then-else code compilation

## Slide 28: Compiling Loops
Compile the assembly code for the C while loop where i is in $s0, j is in $s1, and k is in $s2
while (i!=k) i=i+j;
Loop: beq $s0, $s2, Exit add $s0, $s0, $s1 j Loop Exit: . . .
Notes: For lecture
Loop beq $s0, $s2, Exit
add $s0, $s0, $s1
j Loop
Exit: . . .

## Slide 29: Array access in Loop
int a[10];
for (i=0; i<10; i++) sum += a[i];
# $s0 contains the start address of array “a”
add $s1, $s0, 40 # $s1 is end address
add $t0, $s0, $0 # $t0 is current addr.
Loop: beq $t0, $s1, Exit
lw $t1, 0($t0) add $s2, $t1, $s2 #$s2 is sum
add $t0, $t0, 4 j Loop
Exit: . . .

## Slide 30: Example MIPS Programs
1-add23.asm
  simply adds 2 and 3
2-sum.asm
  adds 17 and 5 and outputs the result
3-basic-input-output.asm
  How to read and write
4-fibonacci.asm
  Compute first 12 fibonacci numbers
The MARS simulator (available in BB) is one way to work with MIPS code.
Home Work:
Not graded
Do not submit

## Slide 31: MIPS Instructions
Category | Instr | Op Code | Example | Meaning
Arithmetic (R format) | add | 0 and 32 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
Data transfer (I format) | load word | 35 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 43 | sw $s1, 100($s2) | Memory($s2+100) = $s1
 | load byte | 32 | lb $s1, 101($s2) | $s1 = Memory($s2+101)
 | store byte | 40 | sb $s1, 101($s2) | Memory($s2+101) = $s1
Cond. Branch | br on equal | 4 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 5 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than | 0 and 42 | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1 else $s1=0
Uncond. Jump | jump | 2 | j 2500 | go to 10000
 | jump register | 0 and 8 | jr $t1 | go to $t1

## Slide 32: MIPS Organization
32
32
32
read data
32
32
32
5
5
5
32
1
5
Processor
Memory
32 bits
230
words
read/write
addr
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
ALU
0
2
3
7
6
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec

## Slide 33: MIPS R3000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
Registers
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
3 Instruction Formats: all 32 bits wide
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target