## Slide 1: CSI3102: Computer Architecture I
Function Calls
Recommended Reading :
COAD - Chapter 2
Courtesy of Prof. Aviral Shrivastava in ASU

## Slide 2: MIPS Instructions
Category | Instr | Op Code | Example | Meaning
Arithmetic (R format) | add | 0 and 32 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
Data transfer (I format) | load word | 35 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 43 | sw $s1, 100($s2) | Memory($s2+100) = $s1
 | load byte | 32 | lb $s1, 101($s2) | $s1 = Memory($s2+101)
 | store byte | 40 | sb $s1, 101($s2) | Memory($s2+101) = $s1
Cond. Branch | br on equal | 4 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 5 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than | 0 and 42 | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1 else $s1=0
Uncond. Jump | jump | 2 | j 2500 | go to 10000
 | jump register | 0 and 8 | jr $t1 | go to $t1

## Slide 3: MIPS Organization
32
registers
($zero - $ra)
32
32
32
read data
32
32
32
32
32
32
32
32
32
5
5
5
32
1
5
Processor
Memory
32 bits
230
words
read/write
addr
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
32
PC
ALU
0
2
3
7
6
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
4
Add
br offset

## Slide 4: MIPS R3000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
Registers
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
3 Instruction Formats: all 32 bits wide
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target

## Slide 5: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 6: Example MIPS Programs
1-add23.asm
  simply adds 2 and 3
2-sum.asm
  adds 17 and 5 and outputs the result
3-basic-input-output.asm
  How to read and write
4-fibonacci.asm
  Compute first 12 fibonacci numbers
The MARS simulator is one way to work with MIPS code.

## Slide 7: Programming Styles
Procedures (subroutines) allow the programmer to structure programs making them
  easier to understand and debug and
  allowing code to be reused
Procedures allow the programmer to concentrate on one portion of the code at a time
  parameters act as barriers between the procedure and the rest of the program and data, allowing the procedure to be passed values (arguments) and to return values (results)
Notes: barriers concept is important!!

## Slide 8: C Functions
main(){ int i,j,k,m; ... i = mult(j,k);
... m = mult(i,i);
...
}
/* really dumb mult function */
int mult (int mcand, int mlier){ int product;
product = 0; while (mlier > 0) { product = product + mcand; mlier = mlier -1; } return product; }
- 2 functions interacting
- What information must the programmer keep track of?

## Slide 9: Requirements for Functions
Pass arguments to the function
Get results from the function
Can call from anywhere
Can always return back
Nested and Recursive Functions
Saving and Restoring Registers
Functions with more than 4 parameters

## Slide 10: Requirements for Functions
Pass arguments to the function
Get results from the function
Can call from anywhere
Can always return back
Nested and Recursive Functions
Saving and Restoring Registers
Functions with more than 4 parameters

## Slide 11: Function Call Bookkeeping
Registers play a major role in keeping track of information for function calls.
Register conventions:
  Return address $ra
  Arguments $a0, $a1, $a2, $a3
  Return value $v0, $v1
  Saved Local variables $s0, $s1, … , $s7
The stack is also used
  we’ll study about that later.

## Slide 12: Compiling Functions
... sum(a,b);... /* a,b:$s0,$s1 */ }
int sum(int x, int y) { return x+y; }
address 1000 1004 1008 1012 1016
2000 2004
C
M I P S

## Slide 13: Compiling Functions
... sum(a,b);... /* a,b:$s0,$s1 */ }
int sum(int x, int y) { return x+y; }
address 1000 add $a0,$s0,$zero # x = a 1004 add $a1,$s1,$zero # y = b 1008 addi $ra,$zero,1016 #ra=1016 1012 j sum #jump to sum 1016 ...
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S

## Slide 14: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
Can always return back
Nested and Recursive Function
Saving and Restoring Registers
Functions with more than 4 parameters

## Slide 15: Compiling Functions
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S
Question: Why use jr here? Why not simply use j?
Answer: sum might be called by many functions, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.

## Slide 16: Compiling Functions
Single instruction to jump and save return address:
  jump and link (jal)
Before: 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #go to sum
After: 1008 jal sum # $ra=1012,go to sum
Why have a jal? Make the common case fast: function calls are very common.
Also, you don’t have to know where the code is loaded into memory with jal.

## Slide 17: Compiling Functions
Syntax for jal (jump and link) is the same as for j (jump):
  jal label
jal should really be called laj for “link and jump”:
  Step 1 (link): Save address of next instruction into $ra
    Why next instruction? Why not current one?
  Step 2 (jump): Jump to the given label

## Slide 18: Compiling Functions
Syntax for jr (jump register):
  jr register
Instead of providing a label to jump to, the jr instruction provides a register which contains an address to jump to.
Only useful if we know the exact address to jump to.
Very useful for function calls:
  jal stores return address in register ($ra)
  jr $ra jumps back to that address

## Slide 19: Compiling Functions
... sum(a,b);... /* a,b:$s0,$s1 */ }
int sum(int x, int y) { return x+y; }
address 1000 add $a0,$s0,$zero # x = a 1004 add $a1,$s1,$zero # y = b 1008 jal sum # ra=1012 1012 ... 1016 ...
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S

## Slide 20: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
  jal
Can always return back
  jr
Nested and Recursive Functions
Saving and Restoring Registers
Functions with more than 4 parameters

## Slide 21: Nested Functions
int main(int x) {
...
sumSquare(x, y);
...
}
int sumSquare(int x, int y) { ...
return mult(x,x)+ y;
}
int mult(int x, int z) {
...
return x*z;
}
Execution starts from main function
  Assume $ra is uninitialized
main calls sumSquare
  $ra contains the address of the instruction after sumSquare
sumSquare calls mult
  Cannot overwrite $ra
  Need to save $ra
Also registers that main was using across the sumSquare function
  Need to be saved
1000 JAL sumSquare
# $ra=1004
2000 JAL mult
# $ra=2004
2004 ADD …
2008 JR $ra
# $ra≠1004
3000 JR $ra
# $ra=2004

## Slide 22: Nested Functions
When a C program is run, there are 3 important memory areas allocated:
  Static: Variables declared once per program, cease to exist only after execution completes. E.g., C globals
  Heap: Variables declared dynamically
  Stack: Space to be used by procedure during execution; this is where we can save register values

## Slide 23: Layout of a Program in Memory
Stack Segment
0x7FFFFFFF
Dynamic Area
Static Area
Text Segment
Reserved
0x04000000
0x10000000
0
Data Segment
Memory
Addresses
in Hex
Stack Grows
Downwards

## Slide 24: Using the Stack
Register $sp always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
  int sumSquare(int x, int y)
  { return mult(x,x)+ y; }

## Slide 25: Using the Stack
sumSquare:
addi $sp,$sp,-8 # space on stack
sw $ra, 4($sp) # save ret addr
sw $a1, 0($sp) # save y
add $a1,$a0,$zero # mult(x,x)
jal mult # call mult
lw $a1, 0($sp) # restore y
add $v0,$v0,$a1 # mult()+y
lw $ra, 4($sp) # get ret addr
addi $sp,$sp,8 # restore stack
jr $ra
mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y;
  }
“push”
“pop”
Stack
0xFFFB
0xFFF7
Growing downwards
[$ra]
$a1=y
[0($sp)]
[4($sp)]
$sp
0x
0xFFF7

## Slide 26: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
  jal
Can always return back
  jr
Nested and Recursive Functions
  Save $ra on stack
Saving and Restoring Registers
Functions with more than 4 parameters

## Slide 27: Register Conventions
CalleR: the calling function
CalleE: the function being called
When callee returns from executing, the caller needs to know which registers may have changed and which are guaranteed to be unchanged.
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (jal) and which may be changed.

## Slide 28: Register Conventions
None guaranteed  inefficient
  Caller will be saving lots of regs that callee doesn’t use!
All guaranteed  inefficient
  Callee will be saving lots of regs that caller doesn’t use!
Register convention: A balance between the two.

## Slide 29: Register Conventions – Saved Registers
$0: No Change. Always 0.
$s0-$s7: Restore if you change. Very important, that’s why they’re called saved registers. If the callee changes these in any way, it must restore the original values before returning.
$sp: Restore if you change. The stack pointer must point to the same place before and after the jal call, or else the caller won’t be able to restore values from the stack.
HINT -- All saved registers start with s!

## Slide 30: Register Conventions–Volatile Registers
$ra: Can Change. The jal call itself will change this register. Caller needs to save on stack if nested call.
$v0-$v1: Can Change. These will contain the new returned values.
$a0-$a3: Can change. These are volatile argument registers. Caller needs to save if they’ll need them after the call.
$t0-$t9: Can change. That’s why they’re called temporary: any procedure may change them at any time. Caller needs to save if they’ll need them afterwards.

## Slide 31: Other Registers
$at: may be used by the assembler at any time; unsafe to use
  Assembler Temporary
$k0-$k1: may be used by the OS at any time; unsafe to use
  Kernel Reserved Registers DONOT USE
$gp, $fp: don’t worry about them
  Feel free to read up on $gp and $fp in Appendix A, but you can write perfectly good MIPS code without them.

## Slide 32: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 33: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
  jal
Can always return back
  jr
Nested and Recursive Functions
  Save $ra on stack
Saving and Restoring Registers
  Register Conventions
Functions with more than 4 parameters
  Pass them on the stack

## Slide 34: Examples
int sum( int arr[], int size )
{
if (size == 0) return 0 ;
else return sum(arr, size - 1) + arr[size - 1] ;
}
Factorial
Fibonacci
Sum of array
Switch-case statement
void chico (int *X, int Y, int Z )
{*X = Y/ 4 - Z * 10 + *X * 8 ;}
int main()
{
int J, K, L , M ;
cin >> J, K, L;
chico (& J, K, L);
M = J - ( K + L);
cout << M;
return
}
  switch (k)
  {
  case 0: f = i + j; break;
  case 1: f = g + h; break;
  case 2: f = g – h; break;
  case 3: f = i – j; break;
  default: f = 0;
  }