## Slide 1: CSI3102: Computer Architecture I
Recommended Reading :
COAD, Patterson & Hennessy - Chapter 2
CAQA, Hennessy & Patterson – Appendix A
The Assembly Language
Courtesy of Prof. Aviral Shrivastava in ASU

## Slide 2: MIPS Instruction Set
Category | Instr | Op Code | Example | Meaning
Arithmetic (R format) | add | 0 and 32 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
Data transfer (I format) | load word | 35 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 43 | sw $s1, 100($s2) | Memory($s2+100) = $s1
 | load byte | 32 | lb $s1, 101($s2) | $s1 = Memory($s2+101)
 | store byte | 40 | sb $s1, 101($s2) | Memory($s2+101) = $s1
Cond. Branch | br on equal | 4 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 5 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than | 0 and 42 | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1 else $s1=0
Uncond. Jump | jump | 2 | j 2500 | go to 10000
 | jump register | 0 and 8 | jr $t1 | go to $t1
 | jump and link | 3 | jal 2500 | go to 10000; $ra=PC+4

## Slide 3: MIPS Organization
32
registers
($zero - $ra)
32
32
32
read data
32
32
32
32
32
32
32
32
32
5
5
5
32
1
5
Processor
Memory
32 bits
230
words
read/write
addr
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
32
PC
ALU
0
2
3
7
6
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
4
Add
br offset

## Slide 4: MIPS R3000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
Registers
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
3 Instruction Formats: all 32 bits wide
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target

## Slide 5: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$at | 1 | Assembler temporary | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$k0, $k1 | 26, 27 | Kernel reserved | n.a.
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 6: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
  jal
Can always return back
  jr
Nested and Recursive Functions
  Save $ra on stack
Saving and Restoring Registers
  Register Conventions
Functions with more than 4 parameters
  Pass them on the stack

## Slide 7: Below the Program
High-level language program (in C)
swap (int v[], int k)
. . .
Assembly language program (for MIPS)
swap: sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Machine (object) code (for MIPS)
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
C - Compiler
Assembler
Notes: For lecture
Computer only understands zeros and ones – instructions of 0’s and 1’s

## Slide 8: Assembly Generation: Arithmetic Instructions
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0,$s1,$s2
  registers have numbers $t0=$8, $s1=$17, $s2=$18
Instruction Format:
op rs rt rd shamt funct
000000 10001 10010 01000 00000 100000
What do the field names stand for?
0
31
Notes: For lecture

## Slide 9: Reason behind their positions
PC is updated with next-PC
  Ready for Next instruction fetch
Read
Address
Instruction
Instruction
Memory
Add
PC
4
32
32
32
registers
($zero - $ra)
32
32
32
5
5
5
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
Instr[25-21]
Instr[20-16]
Instr[15-11]
Instr[31-26]
Opcode
Register names are used to access the respective regs
  Retrieve/use data in RF for the arithmetic operation.
$rs
$rt
$rd

## Slide 10: MIPS Instruction Fields
op
rs
rt
rd
shamt
funct
op rs rt rd shamt funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
= 32 bits
: opcode indicating operation to be performed
: address (or name) of the first register source operand
: address (or name) of the second register source operand
: the register destination address
: shift amount (for shift instructions)
: function code that selects the specific variant of the operation specified in the opcode field
R Format
Notes: for lecture

## Slide 11: Assembly Generation: Load Instruction
Consider the load-word and store-word instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for data transfer instructions
  previous format was R-type for register
Example: lw $t0, 24($s2)
op rs rt 16 bit number
100011 10010 01000 0000000000011000
35 18 8 24
I Format
Notes: For lecture
destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 12: Assembly Generation: Store Instruction
sw $t0, 24($s2)
op rs rt 16 bit number
43 18 8 24
101011 10010 01000 0000000000011000
A 16-bit address means access is limited to memory locations within a region of 213 or 8,192 words (215 or 32,768 bytes) of the address in the base register $s2
Notes: For lecture
why is it 2**13 (2**15) and NOT 2**14 (2**16) like we just saw with memory (here we have to represent signed numbers so the most significant bit is the sign bit)

## Slide 13: What happens to the offset ?
Read
Address
Instruction
Instruction
Memory
Add
PC
4
32
32
Instr[25-21]
Instr[20-16]
Instr[15-0]
Instr[31-26]
Opcode
Signed
Offset
Sign Extension
32-bit Value
Base address
(from Register $rs) is added with the offset
$rs
$rt
- The value of the left-most bit of the immediate operand (bit 15) is copied to all bits to the left (into the high-order bits).
- So if the 16-bit immediate operand is a 16-bit two's complement negative integer, the 32-bit ALU operand is a 32-bit version of the same negative integer.

## Slide 14: Assembling Code
Example:
  A[8] = A[2] – b
  # $s3 <- A[0]
  lw $t0, 8($s3) # load A[2] into $t0
  sub $t0, $t0, $s2 # subtract b (in $s2) from A[2]
  sw $t0, 32($s3) # store result in A[8]
Assemble the MIPS code for these three instructions
35
lw
19
8
8
43
sw
19
8
32
0
sub
8
18
8
0
34
R Format
I Format
I Format
Notes: For lecture
$t0 = 8
$s2 = 18
$s3 = 19

## Slide 15: Assembling Branches
op rs rt 16 bit number
Instructions:
bne $s0, $s1, Label #go to Label if $s0$s1 beq $s0, $s1, Label #go to Label if $s0=$s1
Machine Formats:
I format
5 16 17 ????
4 16 17 ????
How is the branch destination address specified?

## Slide 16: What happens to the br. offset ?
32
32
32
32
32
32
PC
Add
4
Add
br offset
2
16
00
Offset Pre-processing:
Sign Extended 16-bit offset
Shift-left 2-bits, to access the correct instruction word
Branch instructions
 Offset + PC + 4
= Distance (in number of bytes) to the target from PC+4

## Slide 17: Specifying Branch Destinations
bne $s0,$s1,Lab1
add $s3,$s0,$s1
Could use a register (like lw and sw) and add to it the 16-bit offset
  which register?
    Instruction Address Register
      PC = program counter
    its use is automatically implied by instruction
    PC gets updated (PC+4) during the fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 instructions from the (instruction after the) branch instruction, but
    most branches are local anyway (principle of locality)
...
Lab1:
PC 
Could specify the memory address
  But that would require 32 bit field
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 18: Assembling Branches Example
op rs rt 16 bit offset
5 16 17
Assembly code
bne $s0, $s1, Lab1 add $s3, $s0, $s1 Lab1: ...
Machine Format of bne:
I format
1
Remember
  After the bne instruction is fetched, the PC is updated to address the add instruction (PC = PC + 4).
  Two low-order zeros are concatenated to the offset number (which is a sign-extended 32-bit value) is added to the (updated) PC
Notes: For lecture.
For the code shown, the offset field should be 1 instruction (resulting in 4 = 1|00) not two instructions (resulting in 8 = 10|00) since the PC is now pointing to the add instruction (after the bne is fetched).

## Slide 19: Assembling Jumps
op 26-bit address
Instruction:
j label #go to label
Machine Format:
How is the jump destination address specified?
  As an absolute address formed by
    concatenating the upper 4 bits of the current PC (now PC+4) to the 26-bit address and
    concatenating 00 as the 2 low-order bits
J format
2 ????

## Slide 20: Assembling the concatenations
31-28
32
PC + 4
NEXT PC
From Instruction
jmp address
4
25-0
26
2
00
Jump Instructions
Concatenate
  PC + 4 (4 MSB bits)
  Instruction (26 LSB bits)
  00 LSB bits (for byte access)

## Slide 21: CISC Vs RISC Example Program
Main Memory
General Purpose Registers
ALU

## Slide 22
Consider the task of Multiplication
15
20
Operands:
M[2:3] = operand 1 (15)
M[5:2] = operand 2 (20)
Task : Multiplication
Result:
M[2:3] <= result

## Slide 23: The CISC Approach
Instruction :
MULT 2:3, 5:2
Operations:
Loads the two operands into separate registers
Multiplies the operands in the execution unit
Then stores the product in the some temporary register
Stores value back to memory location 2:3
MULT is what is known as a "complex instruction."
Operates directly on the computer's memory banks
Does not require the programmer to explicitly call any loading or storing functions.
closely resembles a command in a higher level language.
  e.g. a ‘C’ statement "a = a * b."

## Slide 24
The RISC Approach
Instructions :
LW A, 2:3 LW B, 5:2 MULT A, B SW 2:3, A
Operations:
Load operand1 into register A
Load operand2 into register B
Multiply the operands in the execution unit and store result in A
Store value of A back to memory location 2:3
These set of Instructions is known as a “Reduced Instructions."
Cannot Operate directly on the computer's memory banks
Requires the programmer to explicitly call any loading or storing functions.
RISC processors only use simple instructions that can be executed within one clock cycle

## Slide 25
CISC
RISC
Primary goal is to complete a task in as few lines of assembly as possible
Emphasis on hardware
Includes multi-clock complex instructions
Memory-to-memory: "LOAD" and "STORE" incorporated in instructions
Small code sizes
High cycles per second
Variable length Instructions
Primary goal is to speedup individual instruction
Emphasis on software
Single-clock, reduced instruction only
Register to register: "LOAD" and "STORE" are independent instructions
Large code sizes
Low cycles per second
Equal length instructions which make pipelining possible

## Slide 26: The Performance Equation
The following equation is commonly used for expressing a computer's performance ability:
The CISC approach
minimizes the number of instructions per program (2)
sacrificing the number of cycles per instruction. (1)
RISC does the opposite
reduces the cycles per instruction (1)
sacrificing number of instructions per program (2)
1
2