## Slide 1: CSI3102: Computer Architecture I
Simple Processor Implementation
Recommended Reading :
COAD - Chapter 5.1 – 5.4
Courtesy of Prof. Aviral Shrivastava in ASU

## Slide 2: MIPS Instruction Set
Category | Instr | Op Code | Example | Meaning
Arithmetic (R format) | add | 0 and 32 | add $s1, $s2, $s3 | $s1 = $s2 + $s3
 | subtract | 0 and 34 | sub $s1, $s2, $s3 | $s1 = $s2 - $s3
Data transfer (I format) | load word | 35 | lw $s1, 100($s2) | $s1 = Memory($s2+100)
 | store word | 43 | sw $s1, 100($s2) | Memory($s2+100) = $s1
 | load byte | 32 | lb $s1, 101($s2) | $s1 = Memory($s2+101)
 | store byte | 40 | sb $s1, 101($s2) | Memory($s2+101) = $s1
Cond. Branch | br on equal | 4 | beq $s1, $s2, L | if ($s1==$s2) go to L
 | br on not equal | 5 | bne $s1, $s2, L | if ($s1 !=$s2) go to L
 | set on less than | 0 and 42 | slt $s1, $s2, $s3 | if ($s2<$s3) $s1=1 else $s1=0
Uncond. Jump | jump | 2 | j 2500 | go to 10000
 | jump register | 0 and 8 | jr $t1 | go to $t1
 | jump and link | 3 | jal 2500 | go to 10000; $ra=PC+4

## Slide 3: MIPS Organization
32
registers
($zero - $ra)
32
32
32
read data
32
32
32
32
32
32
32
32
32
5
5
5
32
1
5
Processor
Memory
32 bits
230
words
read/write
addr
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
32
PC
ALU
0
2
3
7
6
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
4
Add
br offset

## Slide 4: MIPS R3000 ISA
Instruction Categories
  Arithmetic
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
Registers
R Format
I Format
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
3 Instruction Formats: all 32 bits wide
6 bits
5 bits
5 bits
16 bits
J Format
6 bits
26 bits
jump target

## Slide 5: MIPS Register Convention
Name | Register Number | Usage | Should preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 6: Requirements for Functions
Pass arguments to the function
  $a0, $a1, $a2, $a3
Get results from the function
  $v0, $v1
Can call from anywhere
  jal
Can always return back
  jr
Nested and Recursive Functions
  Save $ra on stack
Saving and Restoring Registers
  Register Conventions
Functions with more than 4 parameters
  Pass them on the stack

## Slide 7: Assembling Code
Example:
  A[8] = A[2] – b
  lw $t0, 8($s3) #load A[2] into $t0
  sub $t0, $t0, $s2 #subtract b from A[2]
  sw $t0, 32($s3) #store result in A[8]
Assemble the MIPS code for these three instructions
35
lw
19
8
8
43
sw
19
8
32
0
sub
8
18
8
0
34
Notes: For lecture
lw 35 19 8 8
sub 0 8 18 8 0 34
sw 43 19 8 32

## Slide 8: Branching
32
32
32
32
32
32
PC
Add
4
Add
br offset
2
16
00
Offset
Pre-processing
Branch instructions
- Offset + PC + 4
Jump Instructions
Concatenate
  PC (4 MSB bits)
  Instruction (26 LSB bits)
31-28
32
PC + 4
NEXT PC
From Instruction
jmp address
4
25-0
26
2
00

## Slide 9: MIPS Machine
PCSrc
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 10: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC to hold the address of the next instruction
  PC is updated every cycle, so it does not need an explicit write control signal
  Instruction Memory is read every cycle, so it doesn’t need an explicit read control signal
Read
Address
Instruction
Instruction
Memory
Add
PC
4
32
32

## Slide 11: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction
rs
rt
6+6=12

## Slide 12: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform the indicated (by op and funct) operation on values in rs and rt
  store the result back into the Register File (into location rd)
  Note that Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
rd

## Slide 13: Executing Load and Store
Load and store operations
  compute a memory address by adding the base register (in rs) to the 16-bit signed offset field in the instruction
    base register was read from the Register File during decode
    offset value in the low order 16 bits of the instruction must be sign extended to create a 32-bit signed value
  store value, read from the Register File during decode, must be written to the Data Memory
  load value, read from the Data Memory, must be stored in the Register File
I-Type:
op
rs
rt
address offset
31
25
20
15
0

## Slide 14: Executing Load and Store
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
Notes: For class handout

## Slide 15: Executing Store and Load
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32
Base Address in [rs]
Bits 15-0 from Instruction
Computed Address
Data for
Memory Write
Data from
Memory Read
Notes: For lecture

## Slide 16: Executing Branch Operations
Conditional Branch operations have to
  compare the operands read from the Register File during decode (rs and rt values) for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the sign extended16-bit signed offset field in the instruction
    “base register” is the updated PC
    offset value in the low order 16 bits of the instruction must be sign extended to create a 32-bit signed value
    and then shifted left 2 bits to turn it into a word address
I-Type:
op
rs
rt
address offset
31
25
20
15
0

## Slide 17: Executing Branch Operations
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)
Bits 15-0 from Instruction
Data for compare operation
32
PC + 4
Update PC to Fetch the next Instruction
Notes: For lecture

## Slide 18: Executing Jump Operations
Jump operations have to
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28
J-Type:
op
31
25
0
jump target address
[25-0]
From Instruction
Bits [31-28]
from PC+4

## Slide 19: Adding the pieces together
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite

## Slide 20: R-type instructions + store
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
Only ONE of the inputs is active for any ONE instruction

## Slide 21: Multiplexor Insertion
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 22: Reading from Memory
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 23: R-type + load + store
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 24: Multiplexor Insertion
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 25: Adding the Branch Portion
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Add
PCSrc
PC + 4
Select PC+4 or branch offset address

## Slide 26: Adding the Jump Portion
26
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Add
PCSrc
0
1
Shift
left 2
Jump
28
PC+4[31-28]
32

## Slide 27: MIPS Machine (with Controls)
26
Instr[25-0]
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
Control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
PC+4[31-28]
28
2
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 28: Main Control Unit
Instr | RegDst | ALUSrc | MemtoReg | RegWr | MemRd | MemWr | Branch | ALUOp1 | ALUOp2
R-type 000000 |  |  |  |  |  |  |  |  | 
lw 100011 |  |  |  |  |  |  |  |  | 
sw 101011 |  |  |  |  |  |  |  |  | 
beq 000100 |  |  |  |  |  |  |  |  | 
Completely determined by the instruction opcode field
  Note that a multiplexor whose control input is 0 has a definite action, even if it is not used in performing the operation
Notes: For class handout

## Slide 29: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
Notes: For lecture

## Slide 30
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
ARITHMETIC
Notes: For lecture

## Slide 31: Main Control Unit
Instr | RegDst | ALUSrc | MemtoReg | RegWr | MemRd | MemWr | Branch | ALUOp1 | ALUOp0
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw 100011 |  |  |  |  |  |  |  |  | 
sw 101011 |  |  |  |  |  |  |  |  | 
beq 000100 |  |  |  |  |  |  |  |  | 
Notes: For lecture

## Slide 32: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
Notes: For lecture

## Slide 33
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
I-Type:
op
rs
rt
address offset
31
25
20
15
0
LOAD WORD
Notes: For lecture

## Slide 34: Main Control Unit
Instr | RegDst | ALUSrc | MemtoReg | RegWr | MemRd | MemWr | Branch | ALUOp1 | ALUOp0
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw 101011 |  |  |  |  |  |  |  |  | 
beq 000100 |  |  |  |  |  |  |  |  | 
Notes: For lecture

## Slide 35: Store Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
Notes: For lecture

## Slide 36
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
I-Type:
op
rs
rt
address offset
31
25
20
15
0
STORE WORD
Notes: For lecture

## Slide 37: Main Control Unit
Instr | RegDst | ALUSrc | MemtoReg | RegWr | MemRd | MemWr | Branch | ALUOp1 | ALUOp0
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw 101011 | X | 1 | X | 0 | X | 1 | 0 | 0 | 0
beq 000100 |  |  |  |  |  |  |  |  | 
Notes: For lecture

## Slide 38: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
Notes: For lecture

## Slide 39
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
2
I-Type:
op
rs
rt
address offset
31
25
20
15
0
BRANCH
Notes: For lecture

## Slide 40: Main Control Unit
Completely determined by the instruction opcode field
  Note that a multiplexor whose control input is 0 has a definite action, even if it is not used in performing the operation
Instr | RegDst | ALUSrc | MemtoReg | RegWr | MemRd | MemWr | Branch | ALUOp1 | ALUOp0
R-type 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw 101011 | X | 1 | X | 0 | X | 1 | 0 | 0 | 0
beq 000100 | X | 0 | X | 0 | X | 0 | 1 | 0 | 1
Notes: For lecture

## Slide 41: Control Unit Logic
From the truth table can design the Main Control logic
Instr[31]
Instr[30]
Instr[29]
Instr[28]
Instr[27]
Instr[26]
R-type
lw
sw
beq
RegDst
ALUSrc
MemtoReg
RegWrite
MemRead
MemWrite
Branch
ALUOp1
ALUOp0