## Slide 1: Chap 1: Basic concepts
Computer Systems (CSI2107-02)
YONSEI UNIVERSITY
Spring 2015
(Courtesy of Prof. Shin-Dug Kim in YU
and Textbook Author)

## Slide 2: Overview of the course
Intro. to computer system organization
Processor architecture and design
I/O organization
Chap 1: Basic Concepts
Chap 2: x86 Processor Architecture
Chap 3: Assembly Language Fundamentals
Chap 4: Data Transfers, Addressing, and Arithmetic
Chap 5: Procedures
Chap 6: Conditional Processing
Chap 7: Integer Arithmetic
Chap 8: Advanced Procedures
Chap 9: Strings and Arrays
Chap 10: Structures and Macros
Chap 11: MS-Windows Programming
Chap 12: Floating-Point Processing and Instruction Encoding
Chap 13: High-Level Language Interface
Computer System
Organization
Basic Assembly
Language
Advanced Assembly
Programming

## Slide 3: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data representation
Boolean Operations

## Slide 4: Motivation
Why low level assembly language?
  to design programs on embedded systems
  to control directly computer hardware to communicate with OS
  to optimize critical areas of application programs to speed up
  to communicate with OS
Understand computer systems
  interaction between CPU and programs
    Instrs: a bridge between HW and SW
  interaction between OS and application/assembly programs

## Slide 5: What is Assembly Language?
Languages for computers
  high level language (HLL): C, C++, PASCAL, COBOL, JAVA, etc.
  assembly language
  machine language: binary code executable by the CPU
Compiler
Assembler
Linker
Loader
HLL
Assembly code
Library
routines
Executable code
Memory
Object code

## Slide 6: What is Assembly Language?
Assembly language
  a machine-specific programming language
  one-to-one correspondence
    between assembly instructions and machine instructions
Assembler
  a program converting assembly code into machine code
  linker: combine individual files into a single executable program
  debugger: trace and examine execution of a program
What is assembly language?
  a symbolic form of machine language
  allows alphabetic mnemonics for operation codes and storage locations

## Slide 7: Why learn Assembly Language?
What is assembler?
  translates a program written in assembly language (AL) to machine language (ML)
  AL mnemonics: understandable by programmers
  ML code: understandable by the CPU
Creates object module: machine language representation of any program
Why learn assembly language?
  No language is perfect
  strong points & corresponding week points
  to understand the computer architecture and operating system
  for its utilities that are not supported by high-level languages
Benefits of programming in AL: speed, versatility, flexibility, and compact

## Slide 8: Why learn Assembly Language?
For real-time applications such as device drivers
  programs in AL are fast (compact code)
  routines include only code that programmers want to include
HLL: interpretive and compiled, but
  too slow (too much redundant code)
  no specific HW control mechanism
Versatility: anything that can be done with a computer can be done with AL
Flexibility
  AL: multiple ways to accomplish one task
  HLL: some languages have rigid coding restraint
Big programs in AL: harder and error prone
When to use ==> HLL cannot give necessary performance from HW

## Slide 9: Machine Language
Instruction set
  a set of machine instructions that a processor can execute
  a processor interprets and translates machine instructions into HW signals
  downward compatibility
EX: MOV AL,5
  moves 5 into AL register
  1011000000000101
  operational code (OP-code)
  Operand: data “5”

## Slide 10: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data representation
Boolean Operations

## Slide 11: Virtual Machines
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 12: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 13: Specific Machine Levels

## Slide 14: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language (Level 4)

## Slide 15: Assembly Language
Level 3
Instruction mnemonics that have an one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 16: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 17: Digital Logic
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors

## Slide 18: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data representation
Boolean Operations

## Slide 19: Data Representation
Binary numbers
  0/off/0v, 1/on/5v
Bits, bytes, words and D-words
  word: 16-bits
  double word: 32bits
  quad word: 64bits
1 0 1 1 0 1 0 1 1 0 1 1 0 1 0 1
word
byte
byte
bits

## Slide 20: Data Representation
Various number systems

## Slide 21: Data Representation
Translating unsigned binary integers to decimal
  Bin = Dn-1Dn-2 …D1D0
    (e.g.) 0 0 0 0 1 0 0 1 = D7 D6 D5 D4 D3 D2 D1 D0
  Dec = (Dn-1X2n-1) + (Dn-2X2n-2) + …+(D1X21) + (D0X20)
    (e.g.) 0 0 0 0 1 0 0 1 = (1X23) + (1X20) = 9 D
Binary | Decimal | Hexadecimal
0001 | 1 | 1
0111 | 7 | 7
1010 | 10 | A
1111 | 15 | F

## Slide 22: Data Representation
Translating unsigned decimal integers to binary
  37D 100101B
  Divide decimal by 2 repeatedly, save remainder as binary digit
Division | Quotient | Remainder
37/2 | 18 | 1
18/2 | 9 | 0
9/2 | 4 | 1
4/2 | 2 | 0
2/2 | 1 | 0
1/2 | 0 | 1

## Slide 23: Data Representation
Binary addition
  0 + 0 = 0, 0 + 1 = 1, 1 + 0 = 1, 1 + 1 = 10
Ranges of unsigned integers
Storage Type | Range (low – high) | Power of 2
Unsigned byte | 0 to 255 | 0 to (28 – 1)
Unsigned word | 0 to 65,536 | 0 to (216 -1)
Unsigned D-word | 0 to 4,294,967,295 | 0 to (232 -1)
Unsigned Q-word | 0 to 18,446,744,073,709,551,615 | 0 to (264 -1)
0 0 0 0 0 1 0 0 (4)
0 0 0 0 0 1 1 1 (7)
+ --------------------------
0 0 0 0 1 0 1 1 (11)

## Slide 24: Data Representation
Converting unsigned hexadecimal to decimal
  4-digit Hexadecimal integer: D3D2D1D0
    Dec = (D3X163) + (D2X162) +(D1X161) + (D0X160)
  N-digit hexadecimal
    Dec = (Dn-1X16n-1) + (Dn-2X16n-2) + …+(D1X161) + (D0X160)
EX: 3BA4
  3 x 163 = 12,288, 11 x 162 = 2816
  10 x 161 = 160, 4 x 160 = 4
  3x163 + 11x162 + 10x161 + 4x160 = 15,268
Converting unsigned decimal to hexadecimal: 422  Hex #
Division | Quotient | Remainder
422/16 | 26 | 6
26/16 | 1 | A
1/16 | 0 | 1
 1A6 H

## Slide 25: Data Representation
The highest bit indicates the sign: 1 = negative, 0 = positive

## Slide 26: Data Representation
Signed numbers
  sign bit: MSB
  1 0 0 0 1 0 1 0 = - 10
  0 0 0 0 1 0 1 0 = 10
Two’s complement number
  way to represent negative number
  toggle each bit value and add one
11110110 = -10
00001001 (toggle bits)
+ 1 (add 1)
--------------------------------
00001010 = + 10

## Slide 27: Data Representation
Example
Storing numbers
  “123” : 00110001 00110010 00110011
  ‘1’ ‘2’ ‘3’
  123 : 01111011
Decimal | Binary(n) | NEG(n) | Decimal
+2 | 00000010 | 11111110 | -2
+16 | 00010000 | 11110000 | -16
+127 | 01111111 | 10000001 | -127

## Slide 28: Sample Program
Sample program
15
05
35
35
1. MOV AX,5
2. ADD AX,10
3. ADD AX,20
4. MOV[0120],AX
5. INT 20
AX content
Memory Content
011C
011E
0120
0122
0124
35

## Slide 29: Debug Program Usage
Commands
Command | Description
A | Starts assembling a program, placing each instruction in memory. EX: A100
G | Executes the program. EX: G, G100…
Q | Quits debugger
R | Display register contents or replace. EX: R, R AX, R BX, ..
T | Traces (executes) one instruction or more. EX: T, T3, Tn…

## Slide 30: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data representation
Boolean Operations

## Slide 31: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 32: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 33: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 34: AND
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 35: OR
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 36: Operator Precedence
Examples showing the order of operations:

## Slide 37: Truth Tables (1 of 3)
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 38: Truth Tables (2 of 3)
Example: X  Y

## Slide 39: Truth Tables (3 of 3)
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 40: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software