## Slide 1: Chapter 2: x86 Processor Architecture
Computer Systems (CSI2107-02)
YONSEI UNIVERSITY
Spring 2015
(Courtesy of Prof. Shin-Dug Kim in YU
and Textbook Author)

## Slide 2: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input/Output System

## Slide 3: Basic Microcomputer Design
Why computer organization to ASL programming ?
  need to understand memory addressing scheme by 8086 family
    programming to access data items in memory
  I/O programming (to know how components are interconnected)
  features of ASL reflect the underlying computer organization
  need to understand the differences among family of 8086
CPU: fetch, decode, & execute cycle

## Slide 4: Basic Microcomputer Design
CU
ALU
Status
Reg
Data Reg
Addrs Reg
Memory
CPU
Data
Bus
Control Bus
Address
Bus

## Slide 5: Another View of Microcomputer

## Slide 6: Basic Microcomputer Design
Clock
  every operation is synchronized by clock
Instruction execution cycle
  Fetch
  Decode
  Operand fetch
  Execute: ALU execution
  Write back (store output operand)

## Slide 7: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 8: Pentium CPU Block Diagram
Multi-stage Pipeline

## Slide 9: Basic Microcomputer Design
Multi-stage pipeline
  Each step in instruction cycle takes one clock cycle
  IA-32 processor: pipelined with 6-stage execution cycle
  Bus interface unit (BIU): memory access & I/O access
  Code fetch unit: get instructions from BIU & put into I-queue
  Decode unit: decode instructions from I-queue & translate into micro-code
  Execution unit: executes micro-code instructions
  Segment unit: translate logical address into linear address
  Paging unit: translate linear address into physical address

## Slide 10: Pipelining: Its Natural!
Laundry Example
  Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 11: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 12: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Note:
More time to do project

## Slide 13: Applied to Computer Design
Inst. # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Inst. i | IF | ID | EX | MEM | WB |  |  | 
Inst. i+1 |  | IF | ID | EX | MEM | WB |  | 
Inst. i+2 |  |  | IF | ID | EX | MEM | WB | 
Inst. i+3 |  |  |  | IF | ID | EX | MEM | WB
Clock Number
ALU
Reg
IM
DM
Reg
ALU
Reg
IM
DM
Reg
ALU
Reg
IM
DM
Reg
ALU
Reg
IM
DM
Reg
Program execution order (in instructions)
Time
Potential of n-times speedup. n = no of pipeline stages

## Slide 14: 6-stage non-pipelined processor
 | S1 | S2 | S3 | S4 | S5 | S6
1 | I-1 |  |  |  |  | 
2 |  | I-1 |  |  |  | 
3 |  |  | I-1 |  |  | 
4 |  |  |  | I-1 |  | 
5 |  |  |  |  | I-1 | 
6 |  |  |  |  |  | I-1
7 | I-2 |  |  |  |  | 
8 |  | I-2 |  |  |  | 
9 |  |  | I-2 |  |  | 
10 |  |  |  | I-2 |  | 
11 |  |  |  |  | I-2 | 
12 |  |  |  |  |  | I-2
Cycles
Stages
For k-stages, n-instructions take (n*k) cycles  waste of CPU

## Slide 15: 6-stage pipelined processor
 | S1 | S2 | S3 | S4 | S5 | S6
1 | I-1 |  |  |  |  | 
2 | I-2 | I-1 |  |  |  | 
3 |  | I-2 | I-1 |  |  | 
4 |  |  | I-2 | I-1 |  | 
5 |  |  |  | I-2 | I-1 | 
6 |  |  |  |  | I-2 | I-1
7 |  |  |  |  |  | I-2
Cycles
Stages
For k-stages, n-instructions take k +(n-1) cycles

## Slide 16: Superscalar processor: 2 or more pipelines
 | S1 | S2 | S3 | S4 | S5 | S6
1 | I-1 |  |  |  |  | 
2 | I-2 | I-1 |  |  |  | 
3 | I-3 | I-2 | I-1 |  |  | 
4 |  | I-3 | I-2 | I-1 |  | 
5 |  |  | I-3 | I-1 |  | 
6 |  |  |  | I-2 | I-1 | 
7 |  |  |  | I-2 |  | I-1
8 |  |  |  | I-3 | I-2 | 
9 |  |  |  | I-3 |  | I-3
10 |  |  |  |  | I-3 | 
11 |  |  |  |  |  | I-3
12 |  |  |  |  |  | 
Cycles
Stages
Assume S4 needs 2 cycles
For k-stages, n-instructions take (k+2n-1) cycles
EX

## Slide 17: Superscalar processor: u-pipeline & v-pipeline
 | S1 | S2 | S3 | S4-u | S4-v | S5 | S6
1 | I-1 |  |  |  | EX |  | 
2 | I-2 | I-1 |  |  |  |  | 
3 | I-3 | I-2 | I-1 |  |  |  | 
4 |  | I-3 | I-2 | I-1 |  |  | 
5 |  |  | I-3 | I-1 | I-2 |  | 
6 |  |  |  | I-3 | I-2 | I-1 | 
7 |  |  |  | I-3 | I-4 | I-2 | I-1
8 |  |  |  |  | I-4 | I-3 | I-2
9 |  |  |  |  |  | I-4 | I-3
10 |  |  |  |  |  |  | I-4
Cycles
Stages
EX
Assume S4 needs 2 cycles, odd numbered instruction u-pipe
even numbered instruction  v-pipe
For k-stages, n-instructions take (k+n) cycles

## Slide 18: Reading from Memory
cycle1
cycle2
cycle3
cycle4
CLK
ADDR
RD
DATA
Cycle1: address bits of memory operand are placed on address bus
Cycle2: RD is set low
Cycle3: CPU waits one cycle to give memory time to respond
Cycle4: RD goes to one, signaling CPU to read data on data bus

## Slide 19: Cache Memory
Cache memory
  DRAMs are slower than CPU speed
  Need high speed memory = cache memory
  L-1 cache inside the CPU
  L-2 cache outside CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory

## Slide 20: Program Execution
How a program runs
  Type program name under OS control
  OS search filename in current directory/paths
  If found, retrieves file information (size, location, etc)
  OS determines next available location in memory to load program file into memory
  OS branch to the first instruction of the file  process (running program)
  When finishes, remove file handle & memory space allocated

## Slide 21: IA-32 Processor Architecture
Modes of operation
  Protected mode: native state of processor (prevent programs from outside segment)
    A program can access 4 GB memory (0 – 0FFFFFFFFH)
  Virtual-8086 mode: while in protected mode, can execute real-address mode software (MS-DOS programs)
  Real-address mode: Intel 8086 programming execution mode under MS-DOS

## Slide 22: 16-bit Intel Processor Architecture
Registers
  8, 16, 32-bit storage locations in CPU
  general-purpose, special purpose, & hidden
Data registers: arithmetic & data move
  16-bit general-purpose: AX, BX, CX, & DX
  8-bit: AH, AL, BH, BL, CH, CL, DH, DL
  AX: Accumulator
  BX: Base register (hold address of a procedure or variable)
  CX: Counter register
  DX: Data (special role in multiply/divide)
Segment registers
  CS: code segment (base location of instruction code)
  DS: data segment (base location for data)
  SS: stack segment (base location for stack)
  ES: extra segment (additional location for variables)

## Slide 23: 16-bit Intel Processor Architecture
Index registers (offsets of instructions and data)
  BP: base pointer (offset from SS)
  SP: stack pointer (offset of TOS in SS)
  SI: source index (string movement)
  DI: destination index (string movement)
Status and control registers
  IP: instruction pointer (the offset of next instruction to be executed)
  CS:IP form the complete address
  Flags: control & status
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
C
x
P
X
A
x
Z
S
T
I
D
O
x
x
x
x
Bit position

## Slide 24: 16-bit Intel Processor Architecture
Flags (control & status)
  DF: direction of data transfer (0: up, 1: down, MOVS, CMPS, STD, &CLD)
  IF: interrupt control (1: EN, 0: DE by CLI & STI)
  TF: halt after each instruction execution (1: on by INT 3)
  CF: when the result of unsigned arithmetic is too big to fit: 1=carry, 0=no carry
  OF: when the result of signed arithmetic is too big to fit
  SF: 1=negative, 0=positive
  ZF: when the result of arithmetic/logic operation: 1= zero, 0=nonzero
  A: auxiliary carry showing a carry from bit 3 to bit 4
  P: parity

## Slide 25: 16-bit Intel Processor Architecture
System bus (internal communication channel)
  a set of electronic wires
  address, data, & control signals
Instruction execution cycle
  fetch instructions (6 byte instruction queue for prefetch)
  decode instructions => pass to the execution unit
  execute by execution unit
Intel family
  8080, 8088: 8-bit
  8086: 16-bit
  80386: 32-bit
  80486: 32-bit & 8K cache memory
  Pentium: 64bit 2-way superscalar & separate I/D-caches

## Slide 26: IA-32 Intel Processor Architecture
Improved execution cycle (386 – Pentium)
  BIU (bus interface unit): access memory & I/O
  code prefetch unit: get instructions from BIU and inserts in P-Q
  instruction decode unit: decode instructions from prefetch queue
  execution unit: execute instructions
  segment unit: translate logical addresses to linear addresses
  paging unit: translate virtual addresses into physical addresses
AX
BX
CX
DX
EAX
EBX
ECX
EDX
32-bit register set
Index: EBP, ESP, ESI, EDI
Segment: CS, SS, DS, ES,
FS, GS
Status & control: EFLAGS, EIP
General
Purpose

## Slide 27: IA-32 Intel Processor Architecture
General purpose registers
32-bit | 16-bit | 8-bit(high) | 8-bit(low)
EAX | AX | AH | AL
EBX | BX | BH | BL
ECX | CX | CH | CL
EDX | DX | DH | DL
32-bit | 16-bit
ESI | SI
EDI | DI
EBP | BP
ESP | SP

## Slide 28: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 29: Memory Addressing: real addressing mode
Memory is divided into segments
  each segment contains 216 locations (64 KB long)
  address formation in segmented memory (SM)
  16 bit segment address
  16 bit segment offset
  ex) segment 2000H & offset 0BAFH
  => actual address 20000H
  + 0BAFH
  ------------
  20BAFH
  code and data can be in the same segment
  code and data may not be in the same segment (separate segments)
  code segment (64 KB long for program instructions)
  data segment (64 KB long for data used)

## Slide 30: Memory Addressing: real addressing mode
Memory is divided into segments
00000
10000
20000
30000
40000
50000
60000
70000
80000
6000:000
SEG:Offset
6000:FFFF
250
6000:0250

## Slide 31: Memory Addressing
How to obtain real physical (linear) address?
  notation : < seg addrs > : < offset addrs >
Ex) 020A:1BCD => offset 1BCDH in segment 020AH
  step 1 : add a hex 0 to the right side of the seg addrs
  step 2 : add the offset to that shifted seg addrs
  ex) 020A:1BCD 020A0H
  + 1BCDH
  --------------
  03C6DH
Addresses and advanced 8086 family
  8086 : 20 bit addrs (16 bit data)
  80286 : 24 bit addrs (16 bit data)
  80386/486 : 32 bit addrs (32 bit data)
  all members support 20 bit segmented addressing

## Slide 32: System Memory Map
Address | Mapping Info
00000 – 003FF | INT Vector Table
00400 - | DOS Data Area & SW BIOS
 | DOS kernel & command
 | User programs
0A0000 - 0AFFFF | Video Graphics Buffer
0B0000 – 0B7FFF | MDA Text Buffer
0B8000 – 0BFFFF | Color Text Buffer
0F0000 – 0FFFF0 | ROM BIOS
0FFFF0 | Reserved area for reset

## Slide 33: Operating System & Memory
History of PC memory usage
  8088 & 8086: 1MB using 20 bits (0000-FFFFFH)
  RAM: 00000 - BFFFFH
  ROM: C0000H – FFFFFH
Memory architecture
  00000 - 003FFH: interrupt vector table of 32-bit addresses
  00400H - : software BIOS
  routines for managing KBD, display,
  BIOS data area map: Table 1

## Slide 34: Operating System & Memory
System startup
  reset  initialization program in ROM BIOS
  initial : bootstrap loader  loads the boot record  OS load  OS execution
Video display
  memory-mapped video display
  text mode: B0000H
  graphics mode: B8000H
Serial communication ports
  COM1: 0400:0000 03F8H
  COM2: 0400:0002 02F8H
  COM3: 0400:0004 0000H
  COM4: 0400:0006 0000H
ROM: BIOS (0C0000H – 0FFFFFH)

## Slide 35: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 36: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 37: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 38: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 39: Intel 965 Express Chipset

## Slide 40: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required
* This link may change over time.

## Slide 41: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 42: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 43: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 44: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 45: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 46: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 47: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 48: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 49: Programming levels
Assembly language programs can perform input-output at each of the following levels: