## Slide 1: Chapter 6: conditional processing
Computer Systems (CSI2107-02)
YONSEI UNIVERSITY
Spring 2015
(Courtesy of Prof. Shin-Dug Kim in YU
and Textbook Author)

## Slide 2: Chapter Overview
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures

## Slide 3: Boolean and Comparison Instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
TEST Instruction
CMP Instruction

## Slide 4: BOOLEAN AND COMPARISON INSTRUCTIONS
Perform bitwise operations (manipulate individual bits)
  Instructions for Boolean algebra
Operation | Description
AND | Result is 1 when both input bits are 1
OR | Result is 1 when either input bit is 1
XOR | Result is 1 when the input bits are different (called exclusive-OR)
NOT | Result is the reverse of the input bit (i.e., 1 becomes 0, and 0 becomes 1)
TEST | Perform an implied AND operation on the destination operand, setting the flags appropriately
BT,BTC,BTR,BTS | Copy bit n from the source operand to the Carry flag and complement (toggle)/reset (clear)/set the same bit in the source operand
Table 1. Boolean Instructions

## Slide 5: CPU Status Flags
Arithmetic instructions affect the Flag registers
  Zero flag is set when the result of an operation is zero
  Carry flag is set when the result of an unsigned addition is too large or when a subtraction requires a borrow
    In unsigned arithmetic, watch the carry flag to detect errors.
    In unsigned arithmetic, the overflow flag tells you nothing interesting.
  Sign flag is set when the high bit of the destination operand is set, indicating a negative result
  Overflow flag is set when a signed arithmetic operation generates an invalid signed result (that is out of range)
    In signed arithmetic, watch the overflow flag to detect errors.
    In signed arithmetic, the carry flag tells you nothing interesting.
  Parity flag is set when an instruction generates even number of 1 bits in low byte of the destination operand

## Slide 6: Carry Flag vs. Overflow Flag
Carry Flag is set when on operation generates a carry out of the highest bit of the destination operand
  The carry flag is set if the addition of two numbers causes a carry out of the most significant (leftmost) bits added.
    (ex) 1111 + 0001 = 0000 (Carry flag is turned on)
    (ex) MOV al, 0FFh; ADD al, 1;
  The carry (borrow) flag is also set if the subtraction of two numbers requires a borrow into the most significant (leftmost) bits subtracted.
    (ex) 0000 - 0001 = 1111 (Carry flag is turned on)
    (ex) MOV al, 1; SUB al, 2;
Overflow Flag is set when an instruction generates an invalid sighed result
  If the sum of two numbers with the sign bits off yields a result number with the sign bit on, the "overflow" flag is turned on.
    (ex) 0100 + 0100 = 1000 (Overflow flag is turned on)
    (ex) MOV al, +127; ADD al, 1;
  If the sum of two numbers with the sign bits on yields a result number with the sign bit off, the "overflow" flag is turned on.
    (ex) 1000 + 1000 = 0000 (Overflow flag is turned on)
    (ex) MOV al, -128; SUB al, 1;

## Slide 7: AND Instruction
Boolean AND operation between two operands & places the result in the first operand
      AND reg,reg AND reg,mem AND reg,imm
      AND mem,reg AND mem,imm
  Reg, mem and immed are 8, 16, or 32 bits
  Applied rules
    If both bits equal 1, the result bit is 1
    Otherwise, the result bit is 0
  Affected flags : Overflow, Sign, Zero, Parity, Carry
    AND always clears Overflow and Carry flags

## Slide 8: AND Instruction (Masking)
Clear selected bits in an operand, while carefully preserving, or masking the remaining bits
  00001111 is called a bit mask
      MOV al,00111011b
      AND al,00001111b ;AL=00001011b

## Slide 9: AND Instruction (Converting to Upper Case)
Converting Characters to Upper case
      0 1 1 0 0 0 0 1 = 61h (’a’)
      0 1 0 0 0 0 0 1 = 41h (’A’)
  (EX) Characters are converted into uppercase
.data
array BYTE 50 DUP (?)
.code
MOV ecx, LENGTHOF array
MOV esi, OFFSET array
L1:
AND BYTE PTR [esi], 11011111b ;clear bit 5
INC esi
LOOP L1

## Slide 10: OR Instruction
Boolean OR operation
  place the result in the 1st operand
    OR reg,reg OR reg,mem OR reg,imm OR mem,reg OR mem,imm
  Reg, mem and imm are 8, 16, or 32 bits
  Applied rules
    If both bits are 0, the result bit is 0 & Otherwise, the result bit is 1
  Affected flags : Overflow, Sign, Zero, Parity, Carry
  Example: OR 3Bh with 0Fh
      MOV al,00111011b ;3Bh
      OR al,00001111b ;AL=3Fh

## Slide 11: OR Instruction (Decimal to ASCII)
Convert a single decimal digit to ASCII by setting bits 4 and 5
      Binary value: 00000101 (05h)
      Boolean OR : 00110000 (30h)
      ------------
      Result: 00110101 (35h) ‘5’
      Assembly code : MOV dl, 5 ;binary value
      OR dl, 30h ;convert to ASCII

## Slide 12: OR Instruction (Sign or Value)
Checking the Sign or Value
  A number ORed with itself does not change, but the flags affected
      OR al, al
    Affected flags : Overflow, Sign, Zero, Parity, Carry
    If ZF=1, AL=0;
    if SF=1, AL<0;
    if ZF=0 and SF=0, AL>0;

## Slide 13: XOR Instruction
Boolean exclusive OR operation
      XOR reg,reg XOR reg,mem XOR reg,imm
      XOR mem,reg XOR mem,imm
  Reg, mem and immed are 8, 16, or 32 bits
    Operands must be the same size
    Only one operand can be a memory operand
  Applied rules
    If both bits are the same, the result bit is 0
    Otherwise, the result bit is 1
  Affected flags : Overflow, Sign, Zero, Parity, Carry

## Slide 14: XOR Instruction (Checking the parity)
Check the Parity Flag by XORing a number with zero
  An effective way to check the parity of the number without changing its value
  Example: checking the parity flag
      MOV al,10110101b ;5 bits = odd parity
      XOR al,0 ;parity flag clear (PO)
      MOV al,11001100b ;4 bits = even parity
      XOR al,0 ;parity flag set (PE)
  16-bit parity : check the parity of 16-bit register by performing an exclusive-OR between the upper and lower bytes:
    MOV ax, 64c1h ;0110 0100 1100 0001
    XOR ah, al ;Parity flag set (PE)

## Slide 15: NOT Instruction
NOT instruction toggles all bits in an operand
NOT reg NOT mem
  The result is called one’s complement
    NEG is TWO’s complement
  Affected flags: no flags are affected
  Example:
MOV al,11110000b
NOT al ;AL = 00001111b

## Slide 16: TEST Instruction
Perform an implied AND operation (sets the flags accordingly)
      TEST reg,reg TEST reg,mem TEST reg,immed
      TEST mem,reg TEST mem,immed
  TEST does not modify the destination operand
  If matching bit positions are set both operands, ZF=0
  Affected flags: Overflow, Sign, Zero, Parity, Carry
Example: Testing Multiple Bits (Suppose we want to know whether bit 0 or bit 3 is set)
    0 0 1 0 0 1 0 1 <- input value
    0 0 0 0 1 0 0 1 <- test value
    0 0 0 0 0 0 0 1 <- result: ZF=0
    0 0 1 0 0 1 0 0 <- input value
    0 0 0 0 1 0 0 1 <- test value
    0 0 0 0 0 0 0 0 <- result: ZF=1

## Slide 17: CMP Instruction
Performs an implied subtraction of a source operand from a destination operand (neither operand is modified)
      CMP reg,reg CMP reg,mem CMP reg,immed
      CMP mem,reg CMP mem,immed
  Segment register cannot be used
  Affected flags: Overflow, Sign, Zero, Parity, Carry, Auxiliary Carry
Flag conditions
    When signed operands are compared, the Zero, Sign, and Overflow flags are set by the CMP instruction:
CMP Results | CF | ZF
Destination < source | 1 | 0
Destination = source | 0 | 1
Destination > source | 0 | 0
CMP Results | Flags
Destination < source | SF ≠ OF
Destination = source | ZF = 1
Destination > source | SF=OF

## Slide 18: CMP Instruction (Conditional Logic)
CMP is valuable because it provides the basis for most conditional logic structures
  Example 1: Using the CMP Instruction
      Label1:
      MOV ax, 5
      CMP ax, 10 ;CF=1 and ZF=0 (dest < src)
      Label2:
      MOV ax, 1000
      MOV cx, 1000
      CMP cx, ax ;ZF=1 and CF=0 (dest = src)
      Label3:
      MOV si, 105
      CMP si, 0 ;ZF=0 and CF=0 (dest > src)

## Slide 19: CMP Instruction (Conditional Logic)
  Example 2: Using the CMP Instruction (signed)
      Label4:
      MOV al, 5
      CMP al, -2 ;sign flag = overflow flag = 0 (dest > src)
      Label5:
      MOV al, -1
      CMP al, 5 ;sign flag(1) ≠ overflow flag(0) (dest < src)
      Label6:
      MOV al, 127
      CMP al, -1 ;sign flag = overflow flag = 1 (dest > src)
      Label7:
      MOV al, -128
      CMP al, 1 ;sign flag(0) ≠ overflow flag(1) (dest < src)

## Slide 20: Setting and Clearing Individual CPU Flags
To set the Zero flag
    AND al , 0 ; set Zero flag
    OR al , 1 ; clear Zero flag
To set the Sign flag
    OR al, 80h ; set Sign flag
    AND al, 7fh ; clear Sign flag
To set the Carry flag
    STC ; set Carry flag
    CLC ; clear Carry flag
To set the Overflow flag
    MOV al, 7fh ; AL = +127
    INC al ; AL = 80h (-128), OF = 1 (set Overflow flag)
    OR eax, 0 ; clear Overflow flag

## Slide 21: Conditional Jumps
Jumps Based On . . .
  Specific Flags
  Equality
  Unsigned Comparisons
  Signed Comparisons

## Slide 22: Conditional Jump (Jcond) Instruction
A conditional jump when a flag condition is true
      Syntax: Jcond destination
Cond : refers to a flag condition (state of one or more flags)
      jc ;jump if Carry flag set
      jnc ;jump if Carry flag clear
      jz ;jump if Zero flag set
      jnz ;jump if Zero flag clear
Using CMP
  Example: CMP sets the Zero flag if AX=BX. JE jumps if ZF=1:
      mov ax,5
      cmp ax,5
      je L1 ;jump if equal
      mov ax,5
      cmp ax,6
      jl L1 ;jump if less
      mov ax,5
      cmp ax,4
      jg L1 ;jump if greater

## Slide 23: Conditional Jump (Jcond) Instruction
Types of Conditional Jump Instructions
  4 groups of conditional jumps
    Based on specific flag values
    Based on equality between operands, or the value of (E)CX
    Based on comparisons of unsigned operands
    Based on comparisons of signed operands

## Slide 24: 1. Specific Flag Values
Table 3. Jumps Based on Specific Flag Values
Mnemonic | Description | Flags
JZ | Jump if zero | ZF=1
JNZ | Jump if not zero | ZF=0
JC | Jump if carry | CF=1
JNC | Jump if not carry | CF=0
JO | Jump if overflow | OF=1
JNO | Jump if not overflow | OF=0
JS | Jump if signed | SF=1
JNS | Jump if not signed | SF=0
JP | Jump if parity (even) | PF=1
JNP | Jump if not parity (odd) | PF=0
Mnemonic | Description | Flags
JZ |  | 
JNZ |  | 
JC |  | 
JNC |  | 
JO |  | 
JNO |  | 
JS |  | 
JNS |  | 
JP |  | 
JNP |  | 

## Slide 25: 2. Equality
Table 2. Jumps Based on Equality
Mnemonic | Description
JE | Jump if equal (if op1 = op2)
JNE | Jump if not equal (if op1 not <> op2)
JCXZ | Jump if CX = 0
JECXZ | Jump if ECX = 0
Mnemonic | Description
JE | 
JNE | 
JCXZ | 
JECXZ | 

## Slide 26: 3. Unsigned Comparisons
Table 4. Jumps Based On Unsigned Comparisons
Mnemonic | Description
JA | Jump if above (if op1>op2)
JNBE | Jump if not below or equal (if op1 not <= op2) (JA)
JAE | Jump if above or equal (if op1>=op2)
JNB | Jump if not below (if op1 not < op2) (JAE)
JB | Jump if below (if op1<op2)
JNAE | Jump if not above or equal (if op1 not >=op2) (JB)
JBE | Jump if below or equal (if op1<=op2)
JNA | Jump if not above (if op1 not > op2) (JBE)
Mnemonic | Description
JA | 
JNBE | 
JAE | 
JNB | 
JB | 
JNAE | 
JBE | 
JNA | 

## Slide 27: 4. Signed Comparisons
Mnemonic | Description
JG | Jump if greater (if op1>op2)
JNLE | Jump if not less than or equal (if op1 not <= op2) (JG)
JGE | Jump if greater than or equal (if op1>=op2)
JNL | Jump if not less (if op1 not < op2) (JGE)
JL | Jump if less (if op1<op2)
JNGE | Jump if not greater than or equal (if op1 not >=op2) (JL)
JLE | Jump if less than or equal (if op1<= op2)
JNG | Jump if not not greater (if op1 not > op2) (JLE)
Table 5. Jumps Based On Signed Comparisons
Mnemonic | Description
JG | 
JNLE | 
JGE | 
JNL | 
JL | 
JNGE | 
JLE | 
JNG | 

## Slide 28: Conditional Jump Examples
Testing Status Bits
  AND, OR, NOT, CMP, TEST for conditional jump instructions
    Example: status=8bit memory operand
      mov al,status
      test al,00100000b ;bit 5=1 for equipment offline
      jnz EquipOffline
    Jump to another label if either bit 0,1,or 4 is set:
      mov al,status
      test al,0010011b ;test bits 0,1,4
      jnz InputDataByte
    Jump to a different label if bits 2,3,and 7 are all set:
      mov al,status
      and al,10001100b ;test bits 2,3,7
      cmp al,10001100b ;all bits set?
      je ResetMachine

## Slide 29: Announcements
Quiz 2: Next Thursday at Class
  Chap 5. and Chap 6.
Lab: TBD
  Will be announced in YSCEC
Office Hours
  4:00 pm ~ 5:50 pm today (May 7th)
  5:00 pm ~ 5:50 pm next Tuesday (May 12th)

## Slide 30: Conditional Jump Examples
Larger of Two Numbers
  Example: compares the unsigned value in AX and BX and moves the larger of the two to DX
      mov dx,ax ;assume AX is larger
      cmp ax,bx ;if AX is >=BX then
      jae L1 ; jump to L1
      mov dx,bx ;else mov BX to DX
      L1:

## Slide 31: Conditional Jump Examples
Smallest of Three Integers
  Example: compare the unsigned values in the variable V1, V2, V3 and move the smallest value to a AX
      .data
      V1 WORD ?
      V2 WORD ?
      V3 WORD ?
      .code
      mov ax, V1 ; assume V1 is smalleast
      cmp ax, V2 ; if ax <= V2 then
      jbe L1 ; jump to L1
      mov ax, V2 ; else move V2 to ax
      L1: cmp ax, V3 ; if ax <= V3 then
      jbe L2 ; jump to L2
      mov ax, V3 ; else move V3 to ax
      L2:

## Slide 32: Conditional Jump Examples
Application : Scanning an Array
TITLE Scanning an Array (ArryScan.asm)
; Scan an array for the first nonzero value.
; Last update: 2/16/02
INCLUDE Irvine32.inc
.data
intArray SWORD 0,0,0,0,1,20,35,-12,66,4,0
;intArray SWORD 1,0,0,0
;intArray SWORD 0,0,0,0
;intArray SWORD 0,0,0,1
noneMsg BYTE "A non-zero value was not found",0
.code
main PROC
mov ebx,OFFSET intArray ; point to the array
mov ecx,LENGTHOF intArray ; loop counter
L1:
cmp WORD PTR [ebx],0 ; compare value to zero
jnz found ; found a value
add ebx,2 ; point to next
loop L1 ; continue the loop
jmp notFound ; none found

## Slide 33: Conditional Jump Examples
found:
movsx eax,WORD PTR [ebx] ; otherwise, display it
call WriteInt
jmp quit
notFound:
mov edx,OFFSET noneMsg ; display "not found" message
call WriteString
quit:
call crlf
exit
main ENDP
END main

## Slide 34: Conditional Jump Examples
Application : String Encryption
TITLE Encryption Program (Encrypt.asm)
; This program demonstrates simple symmetric
; encryption using the XOR instruction.
; Chapter 6 example.
INCLUDE Irvine32.inc
KEY = 239 ; any value between 1-255
BUFMAX = 128 ; maximum buffer size
.data
sPrompt BYTE "Enter the plain text: ",0
sEncrypt BYTE "Cipher text: ",0
sDecrypt BYTE "Decrypted: ",0
buffer BYTE BUFMAX dup(0)
bufSize DWORD ?
.code
main PROC
call InputTheString ; input the plain text
call TranslateBuffer ; encrypt the buffer
mov edx,OFFSET sEncrypt ; display encrypted message
call DisplayMessage
call TranslateBuffer
; decrypt the buffer
mov edx,OFFSET sDecrypt ; display decrypted message
call DisplayMessage
exit
main ENDP

## Slide 35: Conditional Jump Examples
;-----------------------------------------------------
InputTheString PROC
;
; Asks the user to enter a string from the
; keyboard. Saves the string and its length
; in variables.
; Receives: nothing. Returns: nothing
;-----------------------------------------------------
    pushad ; Pushes EAX, EBX, ECX, EDX, ESP, EBP, ESI, EDI
mov edx,offset sPrompt ; display a prompt
call WriteString ; Write a null-terminated string to standard output. Input: EDX points to the string.
mov ecx,BUFMAX ; maximum character count
mov edx,offset buffer ; point to the buffer
call ReadString ; Read a string of characters from standard input and store them in a null-terminated string. Input: EDX points to the string, ECX=maximum character count. Output: EAX= number of characters typed.
mov bufSize,eax ; save the length
call Crlf ; Write an end of line sequence to standard output
popad
ret
InputTheString ENDP
;-----------------------------------------------------

## Slide 36: Conditional Jump Examples
;-----------------------------------------------------
DisplayMessage PROC
;
; Display the encrypted or decrypted message.
; Receives: EDX points to the message
; Returns: nothing
;-----------------------------------------------------
pushad
call WriteString
mov edx,offset buffer ; display the buffer
call WriteString
call Crlf
call Crlf
popad
ret
DisplayMessage ENDP
;-----------------------------------------------------

## Slide 37: Conditional Jump Examples
;-----------------------------------------------------
TranslateBuffer PROC
;
; Translates the string by exclusive-ORing each byte
; with the same integer.
; Receives: nothing. Returns: nothing
;-----------------------------------------------------
pushad
mov ecx,bufSize ; loop counter
mov esi,0 ; index 0 in buffer
L1:
xor buffer[esi],KEY ; translate a byte
inc esi ; point to next byte
loop L1
popad
ret
TranslateBuffer ENDP
;-----------------------------------------------------
END main

## Slide 38: The Book’s Link Library
Selected Procedures in the Book’s Link Library
Procedure | Description
Clrscr | Clear the screen and locate the cursor at the upper left corner.
Crlf | Write an end of line sequence to standard output
DumpMem | Writes a block of memory to standard output in hexadecimal. ESI=starting address, ECX=number of unit, EBX=unit size(1=byte,2=word,4=doubleword).
Gotoxy | Locate the cursor at a specified row and column on the screen. Input: DH = row (0-24), DL =column (0-79).
RandomRange | Generate a pseudorandom integer in EAX between 0 and n-1. Input:EAX contains n.
Random32 | Generate a 32-bit pseudorandom integer in the range 0 to FFFFFFFFh. Output:EAX contains the number.
Randomize | Automatically seed random number generator with a random value, based on the current time of day.
ReadInt | Reads a 32-bit signed integer from standard input and returns the value in EAX. Output: EAX contains the value.
ReadChar | Reads a single character from standard input. Output: AL contains returned character.
ReadHex | Read a 32-bit hexadecimal integer from standard input. Output: EAX contains 32-bit hexadecimal integer.

## Slide 39: The Book’s Link Library
Selected Procedures in the Book’s Link Library (cont.)
ReadString | Read a string of characters from standard input and store them in a null-terminated string. Input: EDX points to the string, ECX=maximum character count. Output: EAX= number of characters typed.
SetTextColor | Sets the foreground and background colors of all subsequent text output to the console. EAX contains desired color.
WaitMsg | Displays the message “Press [Enter] to continue…”, and waits for the user to press the Enter key. It has no input and output parameters.
WriteBin | Write an unsigned 32-bit integer to standard output in ASCII binary format. EAX contains integer to display.
WriteChar | Write a single character to standard output. Input: AL contains the character.
WriteDec | Write 32-bit unsigned integer to standard output in decimal format. Input: EAX contains integer to display.
WriteHex | Write 32-bit unsigned integer to standard output in 8-digit hexadecimal format. Input: EAX contains integer to display.
WriteInt | Write a signed 32-bit integer to standard output in decimal format. Input : EAX=the integer to display.
WriteString | Write a null-terminated string to standard output. Input: EDX points to the string.

## Slide 40: Conditional Loop Instructions
LOOPZ( loop if Zero ), LOOPE( loop if Equal )
  Let a loop continue while ZF=1 and ECX>0
    Syntax: LOOPZ destination; LOOPE destination
  Useful when scanning an array for the first element that does not match a given value.
LOOPNZ( loop while not zero), LOOPNE( loop while not equal )
  Counterpart to LOOPZ, LOOPE
  Loop continues while ZF=0 and ECX>0
  Syntax: LOOPNZ destination; LOOPNE destination
  Useful when scanning an array for the first element that matches a given value.

## Slide 41: Conditional Loop Instructions
  Example: scan each number in an array until a positive number is found
TITLE Scanning for a Positive Value (Loopnz.asm)
; Scan an array for the first positive value.
; If no value is found, ESI will point to a sentinel
; value (0) stored immediately after the array.
; Last update: 11/4/01
INCLUDE Irvine32.inc
.data
array SWORD -3,-6,-1,-10,10,30,40,4
;array SWORD -3,-6,-1,-10 ; alternate test data
sentinel SWORD 0
.code
main PROC

## Slide 42: Conditional Loop Instructions
mov esi, OFFSET array
mov ecx, LENGTHOF array
next:
test WORD PTR [esi], 10000000b ; test highest bit
pushfd ; push flags on stack
add esi, TYPE array
popfd ; pop flags from stack
loopnz next ; continue loop
jnz quit ; none found
sub esi, TYPE array ; ESI points to value
quit:
call crlf
exit
main ENDP
END main

## Slide 43: Announcements
Quiz 2: This Thursday at Class
  Chap 5. and Chap 6.
Lab: A528, 7:00 pm today (May 12th)
  announced in YSCEC
Office Hours
  No Office Hour today
  4:00 pm ~ 5:50 pm today (May 14th)

## Slide 44: Conditional Structures
Structured IF, ELSE, or WHILE
  Not provided by Intel instruction set
  Several instructions are combined to create any logical structure
  optimize the logic structures more efficiently than High level language

## Slide 45: Conditional Structure
Block-Structured IF Statements
  Example: Using Java/C++ syntax, two statements are executed if op1 is equal to op2
  if (op1== op2){
    <statement1>
    <statement2>
    }
    Translate IF statement into a compare followed by one or more conditional jump instructions
    cmp op1,op2
    je True
    jmp EndIf
    True:
    <statement1>
    <statement2>
    EndIf:
    Eliminate one of the jumps by reversing the comparison for equal to not equal
    cmp op1,op2
    jne False
    <statement1>
    <statement2>
    False:

## Slide 46: Compound IF Statement
Using the AND Operator
  Example: all 2 conditions must be true before statement1 execution
    if (al > bl ) AND (bl > cl )
    X = 1;
    Straightforward implementation
    cmp al, bl ; first expression…
    ja L1
    jmp next
    L1:
    cmp bl, cl ; second expression…
    ja L2
    jmp next
    L2: ; both are true
    mov X,1 ; set X to 1
    next:
    We can simplify the code reversing JA to JBE instead
    cmp al, bl ; first expression…
    jbe next ; quit if false
    cmp bl, cl ; second expression
    jbe next ; quit if false
    mov X, 1 ; both are true
    next:

## Slide 47: Compound IF Statement
Using the OR Operator
  Assembly language can easily evaluate expressions that use the logical OR operator
    if ( al > bl ) OR ( bl > cl ) OR ( cl > dl )
    X = 1;
    Linear nested-IF structure chains through a series of conditions
    cmp al, bl ; 1: compare AL to BL
    ja L1 ; if true , skip second expression
    cmp bl, cl ; 2: compare BL to CL
    ja L1 ; if true , skip third expression
    cmp cl, dl ; 3: compare CL to DL
    jbe next ; false: skip next statement
    L1: mov X, 1 ; true: set X = 1
    next:

## Slide 48: WHILE Structure
Tests a condition first before performing a block of statements
  As long as the while condition remains true, statements are repeated
    while ( val1 < val2 ) {
    val1++;
    val2--;
    }
  Reverse the condition, jump to the label endwhile when cond true:
    mov eax, val1 ; copy variable to eax
    while:
    cmp eax, val2 ; if not (val1 < val2)
    jnl endwhile ; exit the loop
    inc eax ; val++
    dec val2 ; val—
    jmp while ; repeat the loop
    endwhile:
    mov val1, eax ; save new value for val1

## Slide 49: WHILE Structure
IF Statement Nested In a Loop
Assembly Code
mov eax, op1
mov ebx, op2
mov ecx, op3
L1: cmp eax, ebx ; EAX < EBX?
jl L2 ; true
jmp L7 ; false
L2: inc eax
L3: cmp ebx, ecx ; EBX == ECX ?
je L4 ; true
jmp L5 ; false
L4: mov X, 2 ; X = 2
jmp L6
L5: mov X, 3 ; X = 3
L6: jmp L1 ; repeat the loop
L7: mov op1, eax ; update op1
C++ Code
while ( op1 < op2 )
{
op1++;
if ( op2 == op3 )
X = 2;
else
X = 3;
}

## Slide 50: Table-Driven Selection
More efficient way to process a CASE structure
  Assembler calculates a label’s offset and places it in a variable
  Example : Table Containing Offsets of Procedures
    Let’s assume that processes are located at addresses 120h, etc.
    .data
    CaseTable BYTE ‘A’ ;lookup value
    DWORD Process_A ;address of procedure
    BYTE ‘B’
    DWORD Process_B
    BYTE ‘C’
    DWORD Process_C
    BYTE ‘D’
    DWORD Process_D
Figure 1. Table of Procedure Offsets.
‘A’
00000120
Lookup value
‘B’
00000130
‘C’
00000140
‘D’
00000150
address of process_B

## Slide 51: Table-Driven Selection
  Example program
    User inputs a character and loop compares the character to each entry in table
    Founding first match causes a call to procedure offset stored immediately after the lookup value
    Each procedure loads EDX with the offset of a different string
TITLE Table of Procedure Offsets (ProcTble.asm)
; This program contains a table with offsets of procedures.
; It uses the table to execute indirect procedure calls.
; Last update: 11/4/01
INCLUDE Irvine32.inc
.data
CaseTable BYTE 'A' ; lookup value
DWORD Process_A ; address of procedure
BYTE 'B'
DWORD Process_B
BYTE 'C'
DWORD Process_C
BYTE 'D'
DWORD Process_D
NumberOfEntries = 4

## Slide 52: Table-Driven Selection
prompt BYTE "Press capital A,B,C,or D: ",0
msgA BYTE "Process_A", 0
msgB BYTE "Process_B", 0
msgC BYTE "Process_C", 0
msgD BYTE "Process_D", 0
.code
main PROC
mov edx, OFFSET prompt ; ask user for input
call WriteString
call ReadChar ; read one character
mov ebx, OFFSET CaseTable ; point EBX to the table
mov ecx, NumberOfEntries ; loop counter
L1:
cmp al, [ebx] ; match found?
jne L2 ; no: continue
call NEAR PTR [ebx + 1] ; yes: call the procedure
call WriteString ; display message
call Crlf
jmp L3 ; exit the search
L2:
add ebx, 5 ; point to the next entry
loop L1 ; repeat until ECX = 0
L3:
exit
main ENDP

## Slide 53: Table-Driven Selection
Process_A PROC
mov edx, OFFSET msgA
ret
Process_A ENDP
Process_B PROC
mov edx,O FFSET msgB
ret
Process_B ENDP
Process_C PROC
mov edx, OFFSET msgC
ret
Process_C ENDP
Process_D PROC
mov edx, OFFSET msgD
ret
Process_D ENDP
END main

## Slide 54: Using the .IF Directive (Optional)
.IF Directive
  MASM provide high level directives to make programming compound IF statements much easier
  Syntax
  .IF and .ENDIF directives make boundary of IF statements
  .ELSE and .ELSEIF directives are optional
  condition is a boolean expression or compound boolean expression
.IF condition1
statements
[.ELSEIF condition2
statements ]
[.ELSE
statements ]
.ENDIF
eax > 10000h
val1 <= 100
(eax > 0) && (eax > 10000h)
(val1 <= 100 ) || (val2 <= 100)
(val2 != ebx ) && !CARRY

## Slide 55: Using the .IF Directive (Optional)
Generating ASM Code
  When Using high-level directives, at assembly time assembler expands them into assembly language instructions
  The new label name @C0001 was created by assembler to guarantee that all labels within same procedure are unique
mov eax, 6
.IF eax > val1
mov result, 1
.ENDIF
mov eax, 6
cmp eax, val1
jbe @C0001
mov result, 1
@C0001:
expanded at assembly time

## Slide 56: .REPEAT and .WHILE Directives
.REPEAT Directive
  Execute the loop body before testing the runtime condition following the .UNTIL directive
.WHILE Directive
  Test the condition before executing the loop
  With .ENDW directive make loop boundary
.REAPEAT
statements
.UNTIL condition
.WHILE condition
statements
.ENDW
EX: mov eax,0
.REPEAT
inc eax,
call WriteDec
call Crlf
.UNTIL eax == 10
EX: mov eax,0
.WHILE eax<10
inc eax,
call WriteDec
call Crlf
.ENDW