## Slide 1: Chap. 2 Combinational Logic
Digital Logic (CSI2111-02)
Kyoungwoo Lee
(Courtesy of Textbook Authors)
© Copyright 2004, Gaetano Borriello and Randy H. Katz

## Slide 2: Combinational logic
Basic logic
  Boolean algebra, proofs by re-writing, proofs by perfect induction
  logic functions, truth tables, and switches
  NOT, AND, OR, NAND, NOR, XOR, . . ., minimal set
Logic realization
  two-level logic and canonical forms
  incompletely specified functions
Simplification
  uniting theorem
  grouping of terms in Boolean functions
Alternate representations of Boolean functions
  cubes
  Karnaugh maps

## Slide 3: Possible logic functions of two variables
        X Y 16 possible functions (F0–F15) 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1
        1 0 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1
        1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
0
X and Y
X
Y
X or Y
not Y
not X
1
X
Y
F
X xor Y
X nor Y not (X or Y)
X = Y
X nand Y not (X and Y)
There are 16 possible functions of 2 input variables:
  in general, there are 2**(2**n) functions of n inputs

## Slide 4: Cost of different logic functions
Different functions are easier or harder to implement
  each has a cost associated with the number of switches needed
  0 (F0) and 1 (F15): require 0 switches, directly connect output to low/high
  X (F3) and Y (F5): require 0 switches, output is one of inputs
  X’ (F12) and Y’ (F10): require 2 switches for "inverter" or NOT-gate
  X nor Y (F4) and X nand Y (F14): require 4 switches
  X or Y (F7) and X and Y (F1): require 6 switches
  X = Y (F9) and X  Y (F6): require 16 switches
  thus, because NOT, NOR, and NAND are the cheapest they are the functions we implement the most in practice

## Slide 5: Minimal set of functions
X Y X nand Y 0 0 1 1 1 0
X Y X nor Y 0 0 1 1 1 0
X nand Y  not ( (not X) nor (not Y) ) X nor Y  not ( (not X) nand (not Y) )
Can we implement all logic functions from NOT, NOR, and NAND?
  For example, implementing X and Y is the same as implementing not (X nand Y)
In fact, we can do it with only NOR or only NAND
  NOT is just a NAND or a NOR with both inputs tied together
  and NAND and NOR are "duals", that is, its easy to implement one using the other
But lets not move too fast . . .
  lets look at the mathematical foundation of logic

## Slide 6: An algebraic structure
An algebraic structure consists of
  a set of elements B
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
1. the set B contains at least two elements: a, b 2. closure: a + b is in B a • b is in B 3. commutativity: a + b = b + a a • b = b • a 4. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 5. identity: a + 0 = a a • 1 = a 6. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 7. complementarity: a + a’ = 1 a • a’ = 0

## Slide 7: Boolean algebra
Boolean algebra
  B = {0, 1}
  variables
  + is logical OR, • is logical AND
  ’ is logical NOT
All algebraic axioms hold

## Slide 8: Logic functions and Boolean algebra
X, Y are Boolean algebra variables
X Y X • Y 0 0 0 0 1 0 1 0 0
1 1 1
X Y X’ Y’ X • Y X’ • Y’ ( X • Y ) + ( X’ • Y’ ) 0 0 1 1 0 1 1 0 1 1 0 0 0 0 1 0 0 1 0 0 0
1 1 0 0 1 0 1
( X • Y ) + ( X’ • Y’ )  X = Y
X Y X’ X’ • Y 0 0 1 0 0 1 1 1 1 0 0 0
1 1 0 0
Boolean expression that is true when the variables X and Y have the same value
and false, otherwise
Any logic function that can be expressed as a truth table can be written as an expression in Boolean Algebra using the operators: ’, +, and •

## Slide 9: Axioms and theorems of Boolean algebra
identity 1. X + 0 = X 1D. X • 1 = X
null 2. X + 1 = 1 2D. X • 0 = 0
idempotency: 3. X + X = X 3D. X • X = X
involution: 4. (X’)’ = X
complementarity: 5. X + X’ = 1 5D. X • X’ = 0
commutativity: 6. X + Y = Y + X 6D. X • Y = Y • X
associativity: 7. (X + Y) + Z = X + (Y + Z) 7D. (X • Y) • Z = X • (Y • Z)

## Slide 10: Axioms and theorems of Boolean algebra (cont’d)
distributivity: 8. X • (Y + Z) = (X • Y) + (X • Z) 8D. X + (Y • Z) = (X + Y) • (X + Z)
uniting: 9. X • Y + X • Y’ = X 9D. (X + Y) • (X + Y’) = X
absorption: 10. X + X • Y = X 10D. X • (X + Y) = X 11. (X + Y’) • Y = X • Y 11D. (X • Y’) + Y = X + Y
factoring: 12. (X + Y) • (X’ + Z) = 12D. X • Y + X’ • Z = X • Z + X’ • Y (X + Z) • (X’ + Y)
concensus: 13. (X • Y) + (Y • Z) + (X’ • Z) = 13D. (X + Y) • (Y + Z) • (X’ + Z) = X • Y + X’ • Z (X + Y) • (X’ + Z)

## Slide 11: Axioms and theorems of Boolean algebra (cont’d)
de Morgan’s: 14. (X + Y + ...)’ = X’ • Y’ • ... 14D. (X • Y • ...)’ = X’ + Y’ + ...
generalized de Morgan’s: 15. f’(X1,X2,...,Xn,0,1,+,•) = f(X1’,X2’,...,Xn’,1,0,•,+)
establishes relationship between • and +

## Slide 12: Axioms and theorems of Boolean algebra (cont’d)
Duality
  a dual of a Boolean expression is derived by replacing • by +, + by •, 0 by 1, and 1 by 0, and leaving variables unchanged
  any theorem that can be proven is thus also proven for its dual!
  a meta-theorem (a theorem about theorems)
duality: 16. X + Y + ...  X • Y • ...
generalized duality: 17. f (X1,X2,...,Xn,0,1,+,•)  f(X1,X2,...,Xn,1,0,•,+)
Different than deMorgan’s Law
  this is a statement about theorems
  this is not a way to manipulate (re-write) expressions

## Slide 13: Proving theorems (rewriting)
Using the axioms of Boolean algebra:
  e.g., prove the theorem: X • Y + X • Y’ = X
  e.g., prove the theorem: X + X • Y = X
distributivity (8) X • Y + X • Y’ = X • (Y + Y’)
complementarity (5) X • (Y + Y’) = X • (1)
identity (1D) X • (1) = X 
identity (1D) X + X • Y = X • 1 + X • Y
distributivity (8) X • 1 + X • Y = X • (1 + Y)
identity (2) X • (1 + Y) = X • (1)
identity (1D) X • (1) = X 

## Slide 14: Activity
Prove the following using the laws of Boolean algebra:
  (X • Y) + (Y • Z) + (X’ • Z) = X • Y + X’ • Z
(X • Y) + (Y • Z) + (X’ • Z)
identity (X • Y) + (1) • (Y • Z) + (X’ • Z)
complementarity (X • Y) + (X’ + X) • (Y • Z) + (X’ • Z)
distributivity (X • Y) + (X’ • Y • Z) + (X • Y • Z) + (X’ • Z)
commutativity (X • Y) + (X • Y • Z) + (X’ • Y • Z) + (X’ • Z)
factoring (X • Y) • (1 + Z) + (X’ • Z) • (1 + Y)
null (X • Y) • (1) + (X’ • Z) • (1)
identity (X • Y) + (X’ • Z) 

## Slide 15: Proving theorems (perfect induction)
(X + Y)’ = X’ • Y’ NOR is equivalent to AND with inputs complemented
(X • Y)’ = X’ + Y’ NAND is equivalent to OR with inputs complemented
X Y X’ Y’ (X + Y)’ X’ • Y’ 0 0 1 1 0 1 1 0
1 0 0 1
1 1 0 0
X Y X’ Y’ (X • Y)’ X’ + Y’ 0 0 1 1
0 1 1 0 1 0 0 1
1 1 0 0
Using perfect induction (complete truth table):
  e.g., de Morgan’s:
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
0

## Slide 16: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 17: Apply the theorems to simplify expressions
The theorems of Boolean algebra can simplify Boolean expressions
  e.g., full adder’s carry-out function (same rules apply to any function)
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 18: Activity
Fill in the truth-table for a circuit that checks that a 4-bit number is divisible by 2, 3, or 5
Write down Boolean expressions for By2, By3, and By5
X8 X4 X2 X1 By2 By3 By5
0 0 0 0 1 1 1
0 0 0 1 0 0 0
0 0 1 0 1 0 0
0 0 1 1 0 1 0

## Slide 19: Activity
X8 X4 X2 X1 By2 By3 By5
0 0 0 0 1 1 1
0 0 0 1 0 0 0
0 0 1 0 1 0 0
0 0 1 1 0 1 0
0 1 0 0 1 0 0
0 1 0 1 0 0 1
0 1 1 0 1 1 0
0 1 1 1 0 0 0
1 0 0 0 1 0 0
1 0 0 1 0 1 0
1 0 1 0 1 0 1
1 0 1 1 0 0 0
1 1 0 0 1 1 0
1 1 0 1 0 0 0
1 1 1 0 1 0 0
1 1 1 1 0 1 1
By2 = X8’X4’X2’X1’ + X8’X4’X2X1’
+ X8’X4X2’X1’ + X8’X4X2X1’ + X8X4’X2’X1’ + X8X4’X2X1’ + X8X4X2’X1’ + X8X4X2X1’
= X1’
By3 = X8’X4’X2’X1’ + X8’X4’X2X1
+ X8’X4X2X1’ + X8X4’X2’X1 + X8X4X2’X1’ + X8X4X2X1
By5 = X8’X4’X2’X1’ + X8’X4X2’X1
+ X8X4’X2X1’ + X8X4X2X1

## Slide 20: From Boolean expressions to logic gates
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X Y 0 1 1 0
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
X
X
Y
Y
Z
Z
NOT X’ X ~X
AND X • Y XY X  Y
OR X + Y X  Y

## Slide 21: From Boolean expressions to logic gates (cont’d)
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y
X xor Y = X Y’ + X’ Y X or Y but not both ("inequality", "difference")
X xnor Y = X Y + X’ Y’ X and Y are the same ("equality", "coincidence")
NAND
NOR
XOR X Y
XNOR X = Y

## Slide 22: From Boolean expressions to logic gates (cont’d)
T1
T2
A
B
C
D
T2
T1
Z
use of 3-input gate
A
B
C
D
Z
More than one way to map expressions to gates
  e.g., Z = A’ • B’ • (C + D) = (A’ • (B’ • (C + D)))

## Slide 23: Waveform view of logic functions
time
change in Y takes time to "propagate" through gates
Just a sideways truth table
  but note how edges don’t line up exactly
  it takes time for a gate to switch its output!

## Slide 24: Choosing different realizations of a function
A B C Z 0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
two-level realization (we don’t count NOT gates)
XOR gate (easier to draw but costlier to build)
multi-level realization (gates with fewer inputs)

## Slide 25: Which realization is best?
Reduce number of inputs
  literal: input variable (complemented or not)
    can approximate cost of logic gate as 2 transitors per literal
    why not count inverters?
  fewer literals means less transistors
    smaller circuits
  fewer inputs implies faster gates
    gates are smaller and thus also faster
  fan-ins (# of gate inputs) are limited in some technologies
Reduce number of gates
  fewer gates (and the packages they come in) means smaller circuits
    directly influences manufacturing costs

## Slide 26: Which is the best realization? (cont’d)
Reduce number of levels of gates
  fewer level of gates implies reduced signal propagation delays
  minimum delay configuration typically requires more gates
    wider, less deep circuits
How do we explore tradeoffs between increased circuit delay and size?
  automated tools to generate different solutions
  logic minimization: reduce number of gates and complexity
  logic optimization: reduction while trading off against delay

## Slide 27: Are all realizations equivalent?
Under the same input stimuli, the three alternative implementations have almost the same waveform behavior
  delays are different
  glitches (hazards) may arise – these could be bad, it depends
  variations due to differences in number of gate levels and structure
The three implementations are functionally equivalent

## Slide 28: Implementing Boolean functions
Technology independent
  canonical forms
  two-level forms
  multi-level forms
Technology choices
  packages of a few gates
  regular logic
  two-level programmable logic
  multi-level programmable logic

## Slide 29: Canonical forms
Truth table is the unique signature of a Boolean function
The same truth table can have many gate realizations
Canonical forms
  standard forms for a Boolean expression
  provides a unique algebraic signature

## Slide 30: Sum-of-products canonical forms
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F =
F’ = A’B’C’ + A’BC’ + AB’C’
Also known as disjunctive normal form
Also known as minterm expansion
F = 001 011 101 110 111
+ A’BC
+ AB’C
+ ABC’
+ ABC
A’B’C

## Slide 31: Sum-of-products canonical form (cont’d)
short-hand notation for minterms of 3 variables
A B C minterms 0 0 0 A’B’C’ m0
0 0 1 A’B’C m1
0 1 0 A’BC’ m2
0 1 1 A’BC m3
1 0 0 AB’C’ m4
1 0 1 AB’C m5
1 1 0 ABC’ m6
1 1 1 ABC m7
F in canonical form: F(A, B, C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
Notes: AC’ + C = AC’ + C*(A+1) = AC’ + AC + C = A + C

## Slide 32: Product-of-sums canonical form
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F = 000 010 100 F =
F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
Also known as conjunctive normal form
Also known as maxterm expansion
(A + B + C)
(A + B’ + C)
(A’ + B + C)

## Slide 33: Product-of-sums canonical form (cont’d)
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C’ M1
0 1 0 A+B’+C M2
0 1 1 A+B’+C’ M3
1 0 0 A’+B+C M4
1 0 1 A’+B+C’ M5
1 1 0 A’+B’+C M6
1 1 1 A’+B’+C’ M7
short-hand notation for maxterms of 3 variables
F in canonical form: F(A, B, C) = M(0,2,4) = M0 • M2 • M4
= (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)

## Slide 34: S-o-P, P-o-S, and de Morgan’s theorem
Sum-of-products
  F’ = A’B’C’ + A’BC’ + AB’C’
Apply de Morgan’s
  (F’)’ = (A’B’C’ + A’BC’ + AB’C’)’
  F = (A + B + C) (A + B’ + C) (A’ + B + C)
Product-of-sums
  F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
Apply de Morgan’s
  (F’)’ = ( (A + B + C’)(A + B’ + C’)(A’ + B + C’)(A’ + B’ + C)(A’ + B’ + C’) )’
  F = A’B’C + A’BC + AB’C + ABC’ + ABC

## Slide 35: Four alternative two-level implementations of F = AB + C
canonical sum-of-products minimized sum-of-products canonical product-of-sums minimized product-of-sums
F1
F2
F3
B
A
C
F4

## Slide 36: Waveforms for the four alternatives
Waveforms are essentially identical
  except for timing hazards (glitches)
  delays almost identical (modeled as a delay per level, not type of gate or number of inputs to gate)

## Slide 37: Mapping between canonical forms
Minterm to maxterm conversion
  use maxterms whose indices do not appear in minterm expansion
  e.g., F(A,B,C) = m(1,3,5,6,7) = M(0,2,4)
Maxterm to minterm conversion
  use minterms whose indices do not appear in maxterm expansion
  e.g., F(A,B,C) = M(0,2,4) = m(1,3,5,6,7)
Minterm expansion of F to minterm expansion of F’
  use minterms whose indices do not appear
  e.g., F(A,B,C) = m(1,3,5,6,7) F’(A,B,C) = m(0,2,4)
Maxterm expansion of F to maxterm expansion of F’
  use maxterms whose indices do not appear
  e.g., F(A,B,C) = M(0,2,4) F’(A,B,C) = M(1,3,5,6,7)

## Slide 38: Incompleteley specified functions
A B C D W X Y Z 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
off-set of W
these inputs patterns should never be encountered in practice – "don’t care" about associated output values, can be exploited in minimization
Example: binary coded decimal increment by 1
  BCD digits encode the decimal digits 0 – 9 in the bit patterns 0000 – 1001
don’t care (DC) set of W
on-set of W

## Slide 39: Notation for incompletely specified functions
Don’t cares and canonical forms
  so far, only represented on-set
  also represent don’t-care-set
  need two of the three sets (on-set, off-set, dc-set)
Canonical representations of the BCD increment by 1 function:
  Z = m0 + m2 + m4 + m6 + m8 + d10 + d11 + d12 + d13 + d14 + d15
  Z =  [ m(0,2,4,6,8) + d(10,11,12,13,14,15) ]
  Z = M1 • M3 • M5 • M7 • M9 • D10 • D11 • D12 • D13 • D14 • D15
  Z =  [ M(1,3,5,7,9) • D(10,11,12,13,14,15) ]

## Slide 40: Simplification of two-level combinational logic
Finding a minimal sum of products or product of sums realization
  exploit don’t care information in the process
Algebraic simplification
  not an algorithmic/systematic procedure
  how do you know when the minimum realization has been found?
Computer-aided design tools
  precise solutions require very long computation times, especially for functions with many inputs (> 10)
  heuristic methods employed – "educated guesses" to reduce amount of computation and yield good if not best solutions
Hand methods still relevant
  to understand automatic tools and their strengths and weaknesses
  ability to check results (on small examples)

## Slide 41: The uniting theorem
A B F
0 0 1
0 1 0
1 0 1
1 1 0
B has the same value in both on-set rows – B remains
A has a different value in the two rows – A is eliminated
F = A’B’+AB’ = (A’+A)B’ = B’
Key tool to simplification: A (B’ + B) = A
Essence of simplification of two-level logic
  find two element subsets of the ON-set where only one variable changes its value – this single varying variable can be eliminated and a single product term used to represent both elements

## Slide 42: Boolean cubes
1-cube
X
0
1
Visual technique for indentifying when the uniting theorem can be applied
n input variables = n-dimensional "cube"
2-cube
X
Y
11
00
01
10
3-cube
X
Y
Z
000
111
101
4-cube
W
X
Y
Z
0000
1111
1000
0111

## Slide 43: Mapping truth tables onto Boolean cubes
A B F
0 0 1
0 1 0
1 0 1
1 1 0
ON-set = solid nodes OFF-set = empty nodes DC-set = 'd nodes
two faces of size 0 (nodes) combine into a face of size 1(line)
A varies within face, B does not this face represents the literal B'
Uniting theorem combines two "faces" of a cube into a larger "face"
Example:
A
B
11
00
01
10
F

## Slide 44: Three variable example
A B Cin Cout
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
(A'+A)BCin
AB(Cin'+Cin)
A(B+B')Cin
Cout = BCin+AB+ACin
the on-set is completely covered by the combination (OR) of the subcubes of lower dimensionality - note that “111” is covered three times
Binary full-adder carry-out logic
A
B
C
000
111
101

## Slide 45: Higher dimensional cubes
F(A,B,C) = m(4,5,6,7)
on-set forms a square i.e., a cube of dimension 2
represents an expression in one variable i.e., 3 dimensions – 2 dimensions
A is asserted (true) and unchanged
B and C vary
This subcube represents the
literal A
Sub-cubes of higher dimension than 2
A
B
C
000
111
101
100
001
010
011
110

## Slide 46: m-dimensional cubes in a n-dimensional Boolean space
In a 3-cube (three variables):
  a 0-cube, i.e., a single node, yields a term in 3 literals
  a 1-cube, i.e., a line of two nodes, yields a term in 2 literals
  a 2-cube, i.e., a plane of four nodes, yields a term in 1 literal
  a 3-cube, i.e., a cube of eight nodes, yields a constant term "1"
In general,
  an m-subcube within an n-cube (m < n) yields a term with n – m literals

## Slide 47: Karnaugh maps
A B F
0 0 1
0 1 0
1 0 1
1 1 0
Flat map of Boolean cube
  wrap–around at edges
  hard to draw and visualize for more than 4 dimensions
  virtually impossible for more than 6 dimensions
Alternative to truth-tables to help visualize adjacencies
  guide to applying the uniting theorem
  on-set elements with only one variable changing value are adjacent unlike the situation in a linear truth-table
0 2
1 3
0
1
A
B
0
1
1
0
0
1

## Slide 48: Karnaugh maps (cont’d)
Numbering scheme based on Gray–code
  e.g., 00, 01, 11, 10
    00, 01, 10, 11 (in the sequence of truth-table)
  only a single bit changes in code for adjacent map cells
0 2
1 3
00
01
AB
C
0
1
6 4
7 5
11
10
C
B
A
0 2
1 3
6 4
7 5
C
B
A
0 4
1 5
12 8
13 9
D
A
3 7
2 6
15 11
14 10
C
B
13 = 1101= ABC’D

## Slide 49: Adjacencies in Karnaugh maps
Wrap from first to last column
Wrap top row to bottom row
000 010
001 011
110 100
111 101
C
B
A
A
B
C
000
111
101
100
001
010
011
110

## Slide 50: Karnaugh map examples
obtain the complement of the function by covering 0s with subcubes
F =
Cout =
f(A,B,C) = m(0,4,5,7)
0 0
0 1
1 0
1 1
Cin
B
A
1 1
0 0
B
A
1 0
0 0
0 1
1 1
C
B
A
B’
AB
AC
+ ACin
+ BCin
+ B’C’
+ AB’

## Slide 51: More Karnaugh map examples
F(A,B,C) = m(0,4,5,7)
F'(A,B,C) =  m(1,2,3,6)
F' simply replace 1's with 0's and vice versa
G(A,B,C) =
0 0
0 0
1 1
1 1
C
B
A
1 0
0 0
0 1
1 1
C
B
A
0 1
1 1
1 0
0 0
C
B
A
A
= AC + B’C’
= BC’ + A’C

## Slide 52: Karnaugh map: 4-variable example
C
+ B’D’
find the smallest number of the largest possible subcubes to cover the ON-set
(fewer terms with fewer inputs per term)
F(A,B,C,D) = m(0,2,3,5,6,7,8,10,11,14,15) F =
D
A
B
A
B
C
D
0000
1111
1000
0111
1 0
0 1
0 1
0 0
1 1
1 1
1 1
1 1
C
+ A’BD

## Slide 53: Karnaugh maps: don’t cares
+ B’C’D
f(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  without don't cares
    f =
0 0
1 1
X 0
X 1
D
A
1 1
0 X
0 0
0 0
B
C
A’D

## Slide 54: Karnaugh maps: don’t cares (cont’d)
f(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  f = A'D + B'C'D without don't cares
  f = with don't cares
don't cares can be treated as 1s or 0s depending on which is more advantageous
0 0
1 1
X 0
X 1
D
A
1 1
0 X
0 0
0 0
B
C
A'D
by using don't care as a "1" a 2-cube can be formed rather than a 1-cube to cover this node
+ C'D

## Slide 55: Activity
Minimize the function F = m(0, 2, 7, 8, 14, 15) + d(3, 6, 9, 12, 13)
1 0
0 0
X 1
X X
X 1
1 X
1 0
1 0
D
A
B
C
F =
AC’ +
A’C +
BC +
AB +
A’B’D’ +
B’C’D’
1 0
0 0
X 1
X X
X 1
1 X
1 0
1 0
D
A
B
C
1 0
0 0
X 1
X X
X 1
1 X
1 0
1 0
D
A
B
C
F = BC + A’B’D’ + B’C’D’
F = A’C + AB + B’C’D’

## Slide 56: Combinational logic summary
Logic functions, truth tables, and switches
  NOT, AND, OR, NAND, NOR, XOR, . . ., minimal set
Axioms and theorems of Boolean algebra
  proofs by re-writing and perfect induction
Gate logic
  networks of Boolean functions and their time behavior
Canonical forms
  two-level and incompletely specified functions
Simplification
  a start at understanding two-level simplification
Later
  automation of simplification
  multi-level logic
  time behavior
  hardware description languages
  design case studies