## Slide 1: Chap. 8 Working with Finite State Machines
Digital Logic (CSI2111-02)
Kyoungwoo Lee
(Courtesy of Textbook Authors)
© Copyright 2004, Gaetano Borriello and Randy H. Katz

## Slide 2: Agenda
So far
  Chap 1. Introduction to Digital Logic
    Digital Logic Design
    Combinational Logic vs. Sequential Logic
  Chap 2. Combinational Logic
    Boolean Algebra
    Theorems/Axioms
    Truth Table and Implementation
    Simplification
  Chap 3. Working with Combinational Logic
    K-Map
    Mapping NAND/NOR Networks
    Time Behavior
    HDL
  Chap 4. Combinational Logic Techniques
    Muxer
    Demuxer
    PLA, PAL, ROM
  Chap 5. Case Studies in Combinational Logic Design
So far (cont’)
  Chap 6. Sequential Logic Design
    Latches and Edge-Triggered Flip-Flops
    Timing Methodologies
    Shift Registers, Counters, etc.
  Chap 7. Finite State Machine
    FSM and Design Procedure
    Moore vs. Mealy
Now
  Chap 8. Working with FSM
    State Minimization
Next
  Chap 8. Working with FSM
    State/Input/Output Encodings

## Slide 3: Finite state machine optimization
State minimization
  fewer states require fewer state bits
  fewer bits require fewer logic equations
Encodings: state, inputs, outputs
  state encoding with fewer bits has fewer equations to implement
    however, each may be more complex
  state encoding with more bits (e.g., one-hot) has simpler equations
    complexity directly related to complexity of state diagram
  input/output encoding may or may not be under designer control

## Slide 4: Algorithmic approach to state minimization
Goal – identify and combine states that have equivalent behavior
Equivalent states:
  same output
  for all input combinations, states transition to same or equivalent states
Algorithm sketch
  1. place all states in one set
  2. initially partition set based on output behavior
  3. successively partition resulting subsets based on next state transitions
  4. repeat (3) until no further partitioning is required
    states left in the same set are equivalent
  polynomial time procedure

## Slide 5: State minimization example
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
Sequence detector for 010 or 110
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

## Slide 6: Method of successive partitions (Row-Matching Method)
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
S4 is equivalent to S6
 S4’ = S4 = S6

## Slide 7: Method of successive partitions
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4’ 0 0
1 S2 S5 S4’ 0 0
00 S3 S0 S0 0 0
01 S4’ S0 S0 1 0
10 S5 S0 S0 0 0
11 S4’ S0 S0 1 0
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S1 S2 ) ( S3 S5 ) ( S4 S6 )
S3 is equivalent to S5
 S3’ = S3 = S5

## Slide 8: Method of successive partitions
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3’ S4’ 0 0
1 S2 S3’ S4’ 0 0
00 S3’ S0 S0 0 0
01 or 11 S4’ S0 S0 1 0
10 S3’ S0 S0 0 0
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S1 S2 ) ( S3 S5 ) ( S4 S6 )
( S0 ) ( S1 S2 ) ( S3 S5 ) ( S4 S6 )
S1 is equivalent to S2
 S1’ = S1 = S2

## Slide 9: Method of successive partitions
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1’ S1’ 0 0
0 S1’ S3’ S4’ 0 0
1 S1’ S3’ S4’ 0 0
00 or 10 S3’ S0 S0 0 0
01 or 11 S4’ S0 S0 1 0
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S1 S2 ) ( S3 S5 ) ( S4 S6 )
( S0 ) ( S1 S2 ) ( S3 S5 ) ( S4 S6 )
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6

## Slide 10: Method of successive partitions
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1’ S1’ 0 0
0 or 1 S1’ S3’ S4’ 0 0
00 or 10 S3’ S0 S0 0 0
01 or 11 S4’ S0 S0 1 0

## Slide 11: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0

## Slide 12: More complex state minimization
symbolic state transition table
present next state output state 00 01 10 11 S0 S0 S1 S2 S3 1 S1 S0 S3 S1 S4 0 S2 S1 S3 S2 S4 1 S3 S1 S0 S4 S5 0 S4 S0 S1 S2 S5 1 S5 S1 S4 S0 S5 0
inputs here
Multiple input example
10
01
11
00
00
01
11
10
10
01
11
00
10
00
11
00
11
10
01
10
11
01
00
S0 [1]
S2 [1]
S4 [1]
S1
[0]
S3
[0]
S5
[0]
01

## Slide 13: Minimized FSM
S0-S1
S1-S3
S2-S2
S3-S4
S0-S0
S1-S1
S2-S2
S3-S5
S0-S1
S3-S0
S1-S4
S4-S5
S0-S1
S3-S4
S1-S0
S4-S5
S1-S0
S3-S1
S2-S2
S4-S5
S4-S0
S5-S5
S1-S1
S0-S4
minimized state table
(S0==S4) (S3==S5)
present next state output state 00 01 10 11 S0' S0' S1 S2 S3' 1 S1 S0' S3' S1 S3' 0 S2 S1 S3' S2 S0' 1 S3' S1 S0' S0' S3' 0
Implication chart method
  cross out incompatible states based on outputs
  then cross out more cells if indexed chart entries are already crossed out
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4
present next state output state 00 01 10 11 S0 S0 S1 S2 S3 1 S1 S0 S3 S1 S4 0 S2 S1 S3 S2 S4 1 S3 S1 S0 S4 S5 0 S4 S0 S1 S2 S5 1 S5 S1 S4 S0 S5 0

## Slide 14: Minimizing incompletely specified FSMs
Equivalence of states is transitive when machine is fully specified
But its not transitive when don't cares are present e.g., state output S0 – 0 S1 is compatible with both S0 and S2 S1 1 – but S0 and S2 are incompatible S2 – 1
No polynomial time algorithm exists for determining best grouping of states into equivalent sets that will yield the smallest number of final states

## Slide 15: Minimizing states may not yield best circuit
X Q1 Q0 Q1+ Q0+ Out 0 0 0 0 0 0 0 0 1 0 0 1 0 1 1 0 0 0 1 0 0 0 1 0 1 0 1 1 1 1 1 1 1 1 1 0 – 1 0 0 0 0
Q1+ = X Q0
Q0+ = X ( Q1’ + Q0 )
Example: edge detector - outputs 1 when last two input changes from 0 to 1
00 [0]
11
[0]
01 [1]
X’
X’
X’
X
X
X
Out = Q1’ Q0

## Slide 16: Implication Chart Method for 3 state edge detector
00
01
11
01
X Q1 Q0 Q1+ Q0+ Out 0 0 0 0 0 0 0 0 1 0 0 1 0 1 1 0 0 0 1 0 0 0 1 0 1 0 1 1 1 1 1 1 1 1 1 0 – 1 0 0 0 0
Present(Q1Q0) Next (Q1+Q0+) Out
0 1 0 1 00 00 01 0 0 01 00 11 1 1 11 00 11 0 0
00-00
01-11
Minimized!

## Slide 17: Another implementation of edge detector
"Ad hoc" solution - not minimal but cheap and fast
00 [0]
10
[0]
01 [1]
X’
X
X’
X
X
X
11 [0]
X’
X’
X Q1 Q0 Q1+ Q0+ Out 0 0 0 0 0 0 0 0 1 1 0 1 0 1 0 0 0 0 0 1 1 1 0 0 1 0 0 0 1 0 1 0 1 1 1 1 1 1 0 0 1 0 1 1 1 1 1 0
Q1+ = Q0
Q0+ = X
Out = Q1’ Q0

## Slide 18: State assignment
Choose bit vectors to assign to each “symbolic” state
  with n state bits for m states there are 2n! / (2n – m)! [log n <= m <= 2n]
  2n codes possible for 1st state, 2n–1 for 2nd, 2n–2 for 3rd, …
  huge number even for small values of n and m
    intractable for state machines of any size
    heuristics are necessary for practical solutions
  optimize some metric for the combinational logic
    size (amount of logic and number of FFs)
    speed (depth of logic and fanout)
    dependencies (decomposition)

## Slide 19: State assignment strategies
Possible strategies
  sequential – just number states as they appear in the state table
  random – pick random codes
  one-hot – use as many state bits as there are states (bit=1 –> state)
  output – use outputs to help encode states
  heuristic – rules of thumb that seem to work in most cases
No guarantee of optimality – another intractable problem

## Slide 20: One-hot state assignment
Simple
  easy to encode
  easy to debug
Small logic functions
  each state function requires only predecessor state bits as input
Good for programmable devices
  lots of flip-flops readily available
  simple functions with small support (signals its dependent upon)
Impractical for large machines
  too many states require too many flip-flops
  decompose FSMs into smaller pieces that can be one-hot encoded
Many slight variations to one-hot
  one-hot + all-0 (e.g., 001, 010, 100, 000)

## Slide 21: Heuristics for state assignment
I Q Q+ O i a c j i b c k
I Q Q+ O i a b j k a c l
I Q Q+ O i a b j i c d j
c = i * a + i * b
b = i * a c = k * a
j = i * a + i * c b = i * a d = i * c
i / j
i / k
a
b
c
a
b
c
i / j
k / l
b
d
i / j
a
c
i / j
Adjacent codes to states that share a common next state
  group 1's in next state map
Adjacent codes to states that share a common ancestor state
  group 1's in next state map
Adjacent codes to states that have a common output behavior
  group 1's in output map

## Slide 22: General approach to heuristic state assignment
All current methods are variants of this
  1) determine which states “attract” each other (weighted pairs)
  2) generate constraints on codes (which should be in same cube)
  3) place codes on Boolean cube so as to maximize constraints satisfied (weighted sum)
Different weights make sense depending on whether we are optimizing for two-level or multi-level forms
Can't consider all possible embeddings of state clusters in Boolean cube
  heuristics for ordering embedding
  to prune search for best embedding
  expand cube (more state bits) to satisfy more constraints

## Slide 23: Output-based encoding
Reuse outputs as state bits - use outputs to help distinguish states
  why create new functions for state bits when output can serve as well
  fits in nicely with synchronous Mealy implementations
HG = ST’ H1’ H0’ F1 F0’ + ST H1 H0’ F1’ F0 HY = ST H1’ H0’ F1 F0’ + ST’ H1’ H0 F1 F0’ FG = ST H1’ H0 F1 F0’ + ST’ H1 H0’ F1’ F0’ FY = ST H1 H0’ F1’ F0’ + ST’ H1 H0’ F1’ F0
Output patterns are unique to states, we do not need ANY state bits – implement 5 functions (one for each output) instead of 7 (outputs plus 2 state bits)
Inputs Present State Next State Outputs C TL TS ST H F 0 – – HG HG 0 00 10 – 0 – HG HG 0 00 10 1 1 – HG HY 1 00 10 – – 0 HY HY 0 01 10 – – 1 HY FG 1 01 10 1 0 – FG FG 0 10 00 0 – – FG FY 1 10 00 – 1 – FG FY 1 10 00 – – 0 FY FY 0 10 01 – – 1 FY HG 1 10 01

## Slide 24: Current state assignment approaches
For tight encodings using close to the minimum number of state bits
  best of 10 random seems to be adequate (averages as well as heuristics)
  heuristic approaches are not even close to optimality
  used in custom chip design
One-hot encoding
  easy for small state machines
  generates small equations with easy to estimate complexity
  common in FPGAs and other programmable logic
Output-based encoding
  ad hoc - no tools
  most common approach taken by human designers
  yields very small circuits for most FSMs

## Slide 25: Sequential logic optimization summary
State minimization
  straightforward in fully-specified machines
  computationally intractable, in general (with don’t cares)
State assignment
  many heuristics
  best-of-10-random just as good or better for most machines
  output encoding can be attractive (especially for PAL implementations)